3GPP TSG-S1 	Tdoc S1-99Nokia Comments Rev 3.>391

Hampton Court, UK

10-12 May 1999

| CHANGE REQUEST No : | A020r3 | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- | --- |
| 3GPP Technical Specification | 22.101 | Version: | 3.5.0 |  |
| Submitted to SA | 4 | for approval | x | without presentation ("non-strategic") |  |  |
| list SA plenary meeting no. here ( | for information |  | with presentation ("strategic") | x |  |
| PT SMG CR cover form is available from: http://docbox.etsi.org/tech-org/smg/Document/smg/tools/CR_form/crf28_1.zip |

| Proposed change affects: | SIM | x | ME | x | Network | x |
| --- | --- | --- | --- | --- | --- | --- |

(at least one should be marked with an X)

| Work item: |  |
| --- | --- |

| Source: | Nokia (r3), | Date: | 25/5/99 |
| --- | --- | --- | --- |

| Subject: | Support of Emergency Calls in UMTS |
| --- | --- |

| Category: | F Correction |  | Release: | Phase 2 |  |
| --- | --- | --- | --- | --- | --- |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (one category | B Addition of feature | x |  | Release 97 |  |
| and one release | C Functional modification of feature |  |  | Release 98 |  |
| only shall be | D Editorial modification |  |  | Release 99 | x |
| marked with an X) |  |  |  |  |  |

| Reason for change: | Adds a requirement for the network to able to obtain the number that a user has input for an emergency call. This will allow the network to route the call to the appropriate emergency service if more than one emergency number is supported in a country |
| --- | --- |

| Clauses affected: | 8.4 |
| --- | --- |

| Other specs | Other releases of same spec |  | ( List of CRs: |  |
| --- | --- | --- | --- | --- |
| affected: | Other core specifications |  | ( List of CRs: |  |
|  | MS test specifications / TBRs |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |

| Other comments: |  |
| --- | --- |

<--------- double-click here for help and instructions on how to create a CR.

8.3	Security for the user

It should be possible for the user to authenticate the network when registering and before initiating a service if desired.

Steps shall be taken to ensure the privacy and integrity of sensitive information transferred between the user and all other entities; e.g. user identity and user traffic.

## 8.4	Emergency calls

UMTS shall support an emergency call teleservice as defined in GSM 02.03.

Further following requirement need to be fulfilled:

- It shall be possible for the serving network to obtain the number, which was used to initiate the emergency call.

Note:	This will allow the network to route the call to different emergency call centres if appropriate.