| TSG-SA Working Group 1 (Services) meeting#6 TSGS1#6(99)xxx San Diego, USA, 29th November – 3rd December 1999 | TSG S1 | (99)1010 |
| --- | --- | --- |
|  | Agenda: |  |

| 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- |
|  | 22.060 | CR |  | Current Version: | 3.1.0 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submision to TSG | SA#6 | for approval | X | (only one box should |
| list TSG meeting no. here ( | for information |  | be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM |  | ME |  | UTRAN |  | Core Network | X |
| (at least one should be marked with an X) |
| Source: | Telia | Date: | 1999-11-23 |
| Subject: | Support of Mobile IP in release 99 |
| 3G Work item: | 3TS/SA-0122060 |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature | X |  |  |  |
| shall be marked | C Functional modification of feature |  |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | 3GPP SA2 have for GSM/UMTS release 99 included support of Mobile IP in the architecture for the core network. The corresponding requirements for this should be included in 3GPP SA1 specifications. |
| Clauses affected: | Clause 10.4 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

## 10.4	Interworking for subscriber roaming

Interworking between different GPRS PLMNs is required in order to support subscriber roaming.

It shall be possible for the VPLMN to provide access to the external data network when the external non-GSM data network address is dynamically assigned by the VPLMN.

It shall be possible, as an option, to allow users to roam from one environment to another, between fixed and mobile, between public and private as well as between different public systems.