| TSG-SA Working Group 1 meeting #6 | TSG S1 | (99) 933 |
| --- | --- | --- |
| San Diego, 29 Nov – 03 Dec 1999 | Agenda: | 6.12 |

| 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- |
|  | 02.43 | CR |  | Current Version: | 7.1.0 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submision to TSG | SA#6 | for approval | X | (only one box should |
| list TSG meeting no. here ( | for information |  | be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM |  | ME |  | UTRAN |  | Core Network | X |
| (at least one should be marked with an X) |
| Source: | SA WG1 | Date: |  |
| Subject: | SoLSA correction |
| 3G Work item: |  |
| Category: | F Correction | X |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature |  |  |  |  |
| shall be marked | C Functional modification of feature |  |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | In the case, that an office subscriber moves to a new area to work, in which the LSA ID(s) are different, the operator needs to update the SIM. This is not possible with SIM Uplication Toolkit, if the LSA only access subscriber is not allowed to receive the call unrelated services outside his LSA(s). The LSA only access subscriber should be allowed to have permission for call unrelated services outside his LSA(s). |
| Clauses affected: | 4.2.5 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

### 4.2.2	Localised service area support in idle mode (camping)

The PLMN shall determine, which cells, belonging to the LSA, are to be favoured by the MS when camping.

When camping on a cell in idle mode, the subscriber's mobile station shall use the information provided by the PLMN in selecting cells belonging to his localised service area. The mobile station shall have the ability to reselect a cell in a different LSA with higher priority. This favouring shall not degrade the overall service quality.

There should be no extra delay in cell selection procedure.

### 4.2.3	Localised service area support in active mode (handover)

The PLMN shall determine, which cells, belonging to the LSA, are to be favoured during active mode.

The cells belonging to users LSAs shall be favoured at call setup and when handovers are carried out. This favouring shall not degrade the overall service quality.

### 4.2.4	Exclusive access

For a cell belonging to one or more service areas and where only one or more specific subscribers shall have allowed access, other subscriber’s mobile stations shall be prevented from using the cell to obtain any service, other than TS12 (Emergency Calls).

NOTE: This does not prevent other subscriber's mobile stations from camping on the cell to perform Location Updating.

Handovers into cells belonging to localised service areas where only specific subscribers shall have allowed access, shall be possible to be prevented for other subscribers, if required by a SoLSA application.

### 4.2.5	LSA only access

With access allowed only within one or more localised service areas, it shall be possible to prevent receiving and/or originating calls outside LSA.

It shall be possible to prevent handovers to cells not belonging to allowed localised service areas, if required by a SoLSA application.

### 4.2.6	Preferential access

It shall be possible to allocate resources at call setup and during the active mode to LSA users, if required by a SoLSA application.

NOTE: 	An example of a requirement: the last traffic channel is not allocated to non-LSA user or in case of congestion an ongoing call of a non-LSA user is released and replaced with a call of a LSA user.

# 5	Impact on other services

## 5.1	General

SoLSA is not limited to specific services and there are no modifications necessary for existing services. In particular there shall be no impact to Emergency Call (TS12).

LSA should be able to support all tele, bearer and supplementary services .There is no interaction to supplementary services except those specified below.