TSG-SA Working Group 1 (Services) meeting #5	TSG S1 (99) 978

San Diego, USA 29th Nov – 3rd Dec 1999	Agenda Item: 4.3.3

| 3GPP TSG-CN-WG1, Meeting #8 25-29 October 1999 Kobe, Japan | Tdoc N1-99D29 |
| --- | --- |

Source: 	TSG CN WG1

To: 	TSG CN SS ad hoc, TSG T WG2

cc:	TSG SA WG1, TSG CN WG2, TSG CN WG3

Title:	LS on Service/Baseline Implementation Capabilities

Agenda Item： 	Output Liaison Statement

Source: 	FUJITSU

Document for:	Discussion and Approval

___________________________________________________________________________

TSG-CN WG1 would appreciate comments on the review of “LS on Service/Baseline Implementation Capabilities of the NAS“  in liaison statement TSG_CN_SS-99113 from SS adhoc.

TSG-CN WG1 have revised the table 2 from previous document N1-99B33, some of them were accordingly and some of them were considered according to the comments of SS adhoc. TSG-CN WG1 would like to respond following our comments and the revised table.

- SS adhoc comment 1(outline):

- Missing "network initiated MO call" for CCBS has been identified in the table related to Terminal Service Implementation Capabilities, it shall be added to the table as an optional service capability for terminals supporting speech, fax and cs data.

Discussion and Conclusion:

CCBS has been assumed as a part of R99 and it will be supported as an optional service capabilities. Therefore, "network initiated MO call" (TS24.008 section 5.2.3) is necessary to add to the table as a part of CM procedure of Terminal Service Implementation Capabilities. The MM procedure for the “network initiated MO call” (TS24.008 section 4.5.1.3) has been treated in the table of baseline capabilities already.

Please see the revised information on the table 2 in this document.

- SS adhoc comment 2(outline):

- The section of "Generic Procedure for the control of SS" defines generic handling of call related and call independent supplementary service operations. The procedures for call independent operations are mandatory for terminals supporting supplementary service (as covered by the table). However call related supplementary service procedures are an optional service capability for terminals supporting speech, fax and/or cs data domain.

In addition to the generic procedures defined in 3G TS 24.010 - specific procedures defined in the specifications (24.072, 24.08x-series, 24.09x-series). It is assumed that the support of those specific supplementary service procedures is an optional service capability on a per service basis.

Discussion and Conclusion;

TSG_CN_SS-99113 Identified a necessity of distinction for the call related and the call independent supplementary service operations. N1 understands that the procedures for call related supplementary service operations are an optional service capability depending on terminal’s kinds supporting some supplementary services on speech, fax and/or cs data service domain. On the other hand, the call independent supplementary service operations are categorized independently from speech, fax and/or cs data service domain, if a supplementary service is supported then it is mandatory.

However, assumed that the distinction of the call related and the call independent is categorized by “Operation Name” only in TS 24.080. It is not identified to distinguish by supplementary service type basis, also assumed that even identified such direct connection between “Operation Name “ and the supplementary service type, is not able to be stable considering specification update in near future, concerning such direct connection table may be no meaning by each core specification revised.

Therefore, created additional information as comment in the table 2 that kept basic criteria for the table of Terminal Service Implementation Capabilities as procedure basis (not for service operation(;Operation Name) basis in the table, though recognized the relations with procedures of supplemental services).

In addition, It already assumed to include specific procedures as R99 stage3 are following chart in this time period, though, in order to avoid confusion of detailed information from outside of Technical Specification approach. N1 would like to indicate onlyTS24.072, 24.08x-series, 2409x-series in table 2.

Chart

| 24.072 | Call Deflection Supplementary Service – Stage 3 |
| --- | --- |
| 24.080 | Mobile radio Layer 3 Supplementary Service specification - Formats and coding |
| 24.081 | Line Identification Supplementary Service – Stage 3 |
| 24.082 | Call Forwarding Supplementary Service – Stage 3 |
| 24.083 | Call Waiting (CW) and Call Hold (HOLD) Supplementary Service - Stage 3 |
| 24.084 | MultiParty (MPTY) Supplementary Service – Stage 3 |
| 24.085 | Closed User Group (CUG) Supplementary Service - Stage 3 |
| 24.086 | Advice of Charge (AoC) Supplementary Service - Stage 3 |
| 24.087 | User-to-User Signalling (UUS) – Stage 3 |
| 24.088 | Call Barring (CB) Supplementary Service – Stage 3 |
| 24.090 | Unstructured Supplementary Service Data (USSD) - Stage 3 |
| 24.091 | Explicit Call Transfer (ECT) Supllementary Service - Stage 3 |
| 24.093 | Call Completion to Busy Subscriber (CCBS) - Stage 3 |
| 24.096 | Name Identification Supplementary Service - Stage 3 |

- SS adhoc comment 3(outline):

- The comment regarding the CFU supplementary service for the " Generic Procedure for the control of SS" and the "SS Support procedure" was not understood. TSG CN SS ad hoc is not aware of any requirements for terminals supporting the speech teleservice to support the CFU supplementary service.

Discussion and Conclusion;

CFU supplementary service is a part of call related service. After further study, If a terminal supports speech and/or FAX service, CFU operation is same level of treatment as a one of call related operational supplementary services. Therefore updated that not only highlighting CFU in the comment of table 2.

This document is informative.

Table 1: Terminal Baseline Implementation Capabilities for NAS

M: mandatory, O: Optional, C: Conditional

| Baseline Implementation Capabilities | Ref. Doc | Section(s) | Kind of Terminals | Comments |
| --- | --- | --- | --- | --- |
|  |  |  | CS-only | PS-only | CS+PS |  |
| UMTS CS mobility management (Optional) | MM common procedures | TMSI reallocation procedure | 24.008 | 4.3.1 | M | - | M |  |
|  |  | Authentication procedure | Ditto | 4.3.2 | M | - | M |  |
|  |  | Identification procedure | Ditto | 4.3.3 | M | - | M |  |
|  |  | IMSI detach procedure | Ditto | 4.3.4 | M | - | M |  |
|  |  | Abort procedure | Ditto | 4.3.5 | M | - | M |  |
|  |  | MM information procedure | Ditto | 4.3.6 | O | - | O |  |
|  | MM specific procedure | Location updating procedure | Ditto | 4.4.1 | M | - | M |  |
|  |  | Periodic updating procedure | Ditto | 4.4.2 | M | - | M |  |
|  |  | IMSI attach procedure | Ditto | 4.4.3 | M | - | M |  |
|  |  | Generic Location Updating procedure | Ditto | 4.4.4 | M | - | M |  |
|  | MM connection management procedure | MM connection establishment | Ditto | 4.5.1.1 | M | - | M |  |
|  |  | MM connection establishment for emergency call | Ditto | 4.5.1.5 | C | - | C | Mandatory If speech calls supported. |
|  |  | MM re-establishment | Ditto | 4.5.1.6 | C | - | C | Mandatory If CC supported. |
|  |  | Paging response procedure | Ditto | Not yet defined | M | - | M |  |
|  |  | Network initiated MM connection establishment | Ditto | 4.5.1.3 | O | - | O |  |
|  |  | MM connection release | Ditto | 4.5.3 | M | - | M |  |
| UMTS PS mobility management (Optional) | GMM common procedures | P-TMSI reallocation procedure | ditto | 4.7.6 | - | M | M |  |
|  |  | Authentication and ciphering procedure | ditto | 4.7.7 | - | M | M |  |
|  |  | Identification procedure | ditto | 4.7.8 | - | M | M |  |
|  |  | Paging procedure | ditto | 4.7.9 | - | M | M |  |
|  |  | GMM status procedure | ditto | 4.7.10 | - | M | M |  |
|  |  | GMM support for anonymous access | Ditto | 4.7.11 | - | O | O |  |
|  |  | GMM Information procedure | Ditto | 4.7.12 | - | O | O |  |
|  | GMM specific procedure | GPRS attach procedure | Ditto | 4.7.3.1 | - | M | M |  |
|  |  | Combined GPRS attach procedure | Ditto | 4.7.3.2 | - | - | C | Mandatory If class-A or B. |
|  |  | MS initiated GPRS detach procedure | Ditto | 4.7.4.1 | - | M | M |  |
|  |  | MS initiated Combined GPRS detach procedure | Ditto | 4.7.4.1.3 | - | - | C | Mandatory If class-A or B. |
|  |  | Network initiated GPRS detach procedure | Ditto | 4.7.4.2 | - | M | M |  |
|  |  | Normal and periodic routing area updating Procedure | Ditto | 4.7.5.1 | - | M | M |  |
|  |  | Combined routing area updating Procedure | Ditto | 4.7.5.2 | - | - | C | Mandatory If class-A or B. |

Table 2: Terminal Service Implementation Capability (1/2) for NAS	M: mandatory, O: Optional, C: Conditional

|  | Service Implementation Capabilities | Ref. Doc | Section(s) | Tele-service for Terminals | Comments |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Speech (w/ E. call) | FAX | SMS-PP | SMS-CB |  |  |
|  | Layer 3 specification | UMTS Call Control (Optional) | Mobile originating call Establishment | 24.008 | 5.2.1 | M | M | - | - |  |  |
|  |  |  | Mobile terminating call Establishment | Ditto | 5.2.2 | M | M | - | - |  |  |
|  |  |  | Network initiated MO call (CCBS) | Ditto | 5.2.3 | O | O | - | - |  |  |
|  |  |  | Call clearing | Ditto | 5.4.2 | M | M | - | - |  |  |
|  |  |  |  |  | 5.4.3 | M | M | - | - |  |  |
|  |  |  |  |  | 5.4.4 | M | M | - | - |  |  |
|  |  |  | In-band tones and announcements | Ditto | 5.5.1 | M | M | - | - |  |  |
|  |  |  | Status procedure | Ditto | 5.5.3 | M | M | - | - |  |  |
|  |  |  | DTMF protocol control procedure | Ditto | 5.5.7 | M | - | - | - |  |  |
|  |  | UMTS Session Management(Opt) (Optional) | PDP context activation | Ditto | 6.1.3.1 | - | - | - | - |  |  |
|  |  |  | PDP context modification procedure | Ditto | 6.1.3.2 | - | - | - | - |  |  |
|  |  |  | PDP context deactivation procedure | Ditto | 6.1.3.3 | - | - | - | - |  |  |
|  |  |  | AA PDP context activation | Ditto | 6.1.3.4 | - | - | - | - |  |  |
|  |  |  | AA PDP context deactivation | Ditto | 6.1.3.5 | - | - | - | - |  |  |
|  |  |  | Receiving a SM STATUS message by a SM entity | Ditto | 6.1.3.6 | - | - | - | - |  |  |
|  |  | SMS (Optional) | CM-procedure | 24.011 | 5 | - | - | M | - |  |  |
|  |  |  | SM-RL-procedure | Ditto | 6 | - | - | M | - |  |  |
|  |  |  | Message format on BTS-MS I/F | 04.12 | 3 | - | - | - | M |  | 04.12 For further study |
|  |  | Supplement. (Opt) | Generic Procedure for the control of SS Note: each SS procedures based on specific procedures defined in the TS24.072, 24.08x-series,24.09x-series | 24.010 | 2 | O See comments(1) &(2) | O See comments(1) &(2) | - | - |  | (1) If SS is required, call related SS operations are supported depending on each SS types chosen by terminal, and also each procedures are supported. And see ‘SS for Terminals’ of next page.. (2)SS&CC are Related. |
|  |  |  | SS Support procedure Note: each SS procedures based on specific procedures defined in the TS24.072, 24.08x-series,24.09x-series | Ditto | 3 | O See comments (1) &(2) | O See comments(1) &(2) | - | - |  |  |

Table 2: Terminal Service Implementation Capability (2/2)

|  | Service Implementation Capabilities | Ref. Doc | Section(s) | Bearer service for Terminals | Supplementary service for Terminals | Comments |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Circuit SW data | Packet SW data | Call Forward, Advise of Change, USSD, Explicit Call transfer, and others |  |
|  | Layer 3 specification | UMTS Call Control (Optional) | Mobile originating call Establishment | 24.008 | 5.2.1 | M | - | - |  |
|  |  |  | Mobile terminating call Establishment | Ditto | 5.2.2 | M | - | - |  |
|  |  |  | Network initiated MO call (CCBS) | Ditto | 5.2.3 | O | - | - |  |
|  |  |  | Call clearing | Ditto | 5.4.2 | M | - | - |  |
|  |  |  |  |  | 5.4.3 | M | - | - |  |
|  |  |  |  |  | 5.4.4 | M | - | - |  |
|  |  |  | In-band tones and announcements | Ditto | 5.5.1 | M | - | - |  |
|  |  |  | Status procedure | Ditto | 5.5.3 | M | - | - |  |
|  |  |  | DTMF protocol control procedure | Ditto | 5.5.7 | - | - | - |  |
|  |  | UMTS Session Management(Opt) (Optional) | PDP context activation | Ditto | 6.1.3.1 | - | M | - |  |
|  |  |  | PDP context modification procedure | Ditto | 6.1.3.2 | - | M | - |  |
|  |  |  | PDP context deactivation procedure | Ditto | 6.1.3.3 | - | M | - |  |
|  |  |  | AA PDP context activation | Ditto | 6.1.3.4 | - | O | - |  |
|  |  |  | AA PDP context deactivation | Ditto | 6.1.3.5 | - | O | - |  |
|  |  |  | Receiving a SM STATUS message by a SM entity | Ditto | 6.1.3.6 | - | M | - |  |
|  |  | SMS (Optional) | CM-procedure | 24.011 | 5 | - | - | - |  |
|  |  |  | SM-RL-procedure | Ditto | 6 | - | - | - |  |
|  |  |  | Message format on BTS-MS I/F | 04.12 | 3 | - | - | - | 04.12 For further sturdy |
|  |  | Supp. (Opt) | Generic Procedure for the control of SS Note: each SS procedures based on specific procedures defined in the TS24.072, 24.08x-series,24.09x-series | 24.010 | 2 | C See comment(3)&(4) | - | M(see each specific procedures depending on supporting services. ) See comment(1),(2)&(4) | SA defines items. Call independent SS operations are required per SS type basis Call related SS operations are required per SS type basis SS&CC are Related. |
|  |  |  | SS Support procedure Note: each SS procedures based on specific procedures defined in the TS24.072, 24.08x-series,24.09x-series | Ditto | 3 | C See comment(3)&(4) | - | M(see each specific procedures depending on supporting services. ) See comment(1), (2)&(4) |  |