TSG-SA Working Group 1 (Services) meeting #5	TSG S1 (99) 966

San Diego, USA 29th Nov – 3rd Dec 1999	Agenda Item: 8.3

Date: 	19 November 1999

Source:  	M. Zarri

Title:	3GPP Vocabulary TR 21.905

Agenda Item: 	8.2

Document for: Information to S1

3G TR 21.905 V1.0.0 (1999-10)

Technical Report

3rd Generation Partnership Project;

Technical Specification Group Services and System Aspects

Vocabulary for 3GPP Specifications

(3G TR 21.905 version 1.0.0)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.	 
The present document has not been subject to any approval process by the 3GPP Organisational Partners and shall not be implemented.	 
This Specification is provided for future development work within 3GPP only. The Organisational Partners accept no liability for any use of this Specification.
Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organisational Partners' Publications Offices.

Reference

3TR/TSGS-0021905U

Keywords

Vocabulary

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 1999, 3GPP Organizational Partners (ARIB, CWTS, ETSI, T1, TTA,TTC).

All rights reserved.

# Contents

Contents	4

Foreword	5

1.	Scope	6

2.	References	6

3.	Terms and definitions related to UTRA Radio aspects	6

3.1.	A	6

3.2.	B	6

3.3.	C	7

3.4.	D	7

3.5.	E	7

3.6.	H	7

3.7.	I	7

3.8.	L	8

3.9.	M	8

3.10.	N	9

3.11.	P	9

3.12.	Q	9

3.13.	R	9

3.14.	S	10

3.15.	T	11

3.16.	U	11

3.17.	V	12

4.	Abbreviations	12

4.1.	A	12

4.2.	B	12

4.3.	C	13

4.4.	D	13

4.5.	E	13

4.6.	F	13

4.7.	G	14

4.8.	H	14

4.9.	I	14

4.10.	J	14

4.11.	K	14

4.12.	L	14

4.13.	M	14

4.14.	N	15

4.15.	O	15

4.16.	P	15

4.17.	Q	16

4.18.	R	16

4.19.	S	16

4.20.	T	17

4.21.	U	17

4.22.	V	17

4.23.	W	17

5.	Equations	18

Annex A (informative): Change Request History	19

History	20

# Foreword

This Technical Report has been produced by the 3GPP.

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of this TR, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	Indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the specification.

# Scope

The purpose of this report is to identify specialist technical terms used within the 3GPP project for the purposes of specifying service requirements. The motivations for this are:

- To ensure that editors use terminology that is consistent across specifications.

- To provide a reader with convenient reference for technical terms that are used across multiple documents.

- To prevent inconsistent use of terminology across documents.

This document is a collection of terms, definitions and abbreviations related to the baseline documents defining 3GPP objectives and systems framework. This document provides a tool for further work on 3GPP technical documentation and facilitates their understanding.

The terms, definitions and abbreviations as given in this document are either imported from existing documentation (ETSI, ITU or elsewhere) or newly created by 3GPP experts whenever the need for precise vocabulary was identified.

# References

References may be made to:

- specific versions of publications (identified by date of publication, edition number, version number, etc.), in which case, subsequent revisions to the referenced document do not apply; or

- all versions up to and including the identified version (identified by "up to and including" before the version identity); or

- all versions subsequent to and including the identified version (identified by "onwards" following the version identity); or

- publications without mention of a specific version, in which case the latest version applies.

A non-specific reference to an ETS shall also be taken to refer to later versions published as an EN with the same number.

[1]	 	GSM 01.04: "Digital cellular telecommunication system (Phase 2+); Abbreviations and acronyms".

[2]		TS 25.990: "Technical Specification Group (TSG) RAN; Vocabulary ".

# Terms and definitions related to UTRA Radio aspects

## A

Acceptable Cell A cell that the UE may camp on to make emergency calls. It must satisfy certain conditions.

Access Stratum.

Access Stratum SDU (Service Data Unit) Unit of data transferred over the access stratum SAP (Service Access Point) in the Core Network or in the User Equipment.

Active mode The state of an UE when processing a call.

Active Set Set of radio links simultaneously involved in a specific communication service between an UE and a UTRAN access point.

ALCAP Generic name for the transport signaling protocols used to set-up and tear-down transport bearers.

Allowable PLMN A PLMN which is not in the list of forbidden PLMN in the UE.

Authentication A property by which the correct identity of an entity or party is established with a required assurance. The party being authenticated could be a user, subscriber, home environment or serving network.

Available PLMN A PLMN where the UE has found a cell that satisfies certain conditions.

Average transmit power The average transmitter output power obtained over any specified time interval, including periods with no transmission.

Average Transmitter Power Per Traffic Channel (dBm) The mean of the total transmitted power over an entire transmission period. ***

## B

Basic telecommunication service This term is used as a common reference to both bearer services and teleservices.

Bearer service A Bearer service is a type of telecommunication service that provides the capability of transmission of signals between access points.

Bearer Service An information transmission path of defined capacity, delay and bit error rate, etc.

## C

Cable, Connector, and Combiner Losses (Transmitter) (dB) The combined losses of all transmission system components between the transmitter output and the antenna input (all losses in positive dB values).

Cable, Connector, and Splitter Losses (Receiver) (dB) These are the combined losses of all transmission system components between the receiving antenna output and the receiver input.

Call Control; ***

Camped on a cell The UE is in idle mode and has completed the cell selection/reselection process and has chosen a cell. The UE monitors system information and  (in most cases) paging information. Note that the services may be limited, and that the PLMN may not be aware of the existence of the UE within the chosen cell.

Cell A geographical area that can be identified by a UE from a (cell) identification that is  broadcast from one UTRAN Access Point.

Coded Composite Transport Channel (CCTrCH) A data stream resulting from encoding and multiplexing of one or several transport channels.

Common Channel A Channel not dedicated to a specific UE.

Control channel A logical channel that carries system control information.

Connection A communication channel between two or more end-points (e.g. terminal, server etc.).

Controlling RNC A role an RNC can take with respect to a specific set of UTRAN access points. There is only one Controlling RNC for any UTRAN access point. The Controlling RNC has the overall control of the logical resources of its UTRAN access point's.

Core network An architectural term relating to the part of UMTS which is independent of the connection technology of the terminal (eg radio, wired).

Coverage area (of a mobile cellular system) An area where mobile cellular services are provided by that mobile cellular system to the level required of that system. ***

Coverage area The "coverage area" is the area over which a UMTS service is provided with the service probability above a certain threshold.

## D

Dedicated Channel  A channel dedicated to a specific UE.

Downlink A "downlink" is a unidirectional radio link for the transmission of signals from a UTRAN access point to a UE. Also in general the direction from Network to UE.

Drift RNS The role an RNS can take with respect to a specific connection between a UE and UTRAN. An RNS that supports the Serving RNS with radio resources when the connection between the UTRAN and the User Equipment need to use cell(s) controlled by this RNS is referred to as Drift RNS.

DRX cycle The individual time interval between reading initial paging information for specific UE. ***

## E

Explicit Diversity Gain (dB) The effective gain achieved using diversity techniques.

## H

Handoff Gain/Loss (dB) This is the gain/loss factor (+ or -) brought by handoff to maintain specified reliability at the cell boundary.

Handover The transfer of a user’s connection from one radio channel to another (can be the same or different cell).

Hard Handover Hard handover is a category of handover procedures where all the old radio links in the UE  are abandoned before the new radio links are established.

Home Environment The home environment is responsible for enabling a user to obtain UMTS services in a consistent manner regardless of the user’s location or terminal used (within the limitations of the serving network and current terminal).

Home PLMN This is a PLMN where the Mobile Country Code (MCC) and Mobile Network Code (MNC) of the PLMN identity are the same as the MCC and MNC of the IMSI.

## I

Idle mode The state of UE switched on but which does not have any established RRC connection.

Information Data ***

Rate Rate of the user information, which must be transmitted over the Air Interface. For example, output rate of the voice codec.

Initial paging information This information indicates if the UE needs to continue to read more paging information and eventually receive a page message.

Initial paging occasion The paging occasion the UE uses as starting point for its DRX cycle.

Inter-cell handover A  handover between different cells. An inter-cell handover requires network connections to be altered.

Interference Signal Code Power (ISCP) Given only interference power is received, the average power of the received signal after despreading and combining.

Intra-cell handover A handover within one sector or between different sectors of the same cell. An intra-cell handover does not require network connections to be altered.

Iu Interconnection point between an RNC and a Core Network. It is also considered as a reference point.

Iub Interface between an RNC and a Node B.

Iur A logical interface between two RNC. Whilst logically representing a point to point link between RNC, the physical realisation may not be a point to point link.

## L

Location Registration (LR) The UE registers its presence in a registration area, for instance regularly or when entering a new registration area.

Logical Channel A logical channel is an information stream dedicated to the transfer of a specific type of information over the radio interface. Logical Channels are provided on top of the MAC layer.

Logical Model A Logical Model defines an abstract view of a network or network element by means of information objects representing network element, aggregations of network elements, the topological relationship between the elements, endpoints of connections (termination points), and transport entities (such as connections) that transport information between two or more termination points.
The information objects defined in the Logical Model are used, among others, by connection management functions. In this way a physical implementation independent management is achieved.

Logical O&M Logical O&M is the signaling associated with the control of logical resources (channels, cells,) owned by the RNC but physically implemented in the Node B. The RNC controls these logical resources. A number of O&M procedures physically implemented in Node B impact on the logical resources and therefore require an information exchange between RNC and Node B. All messages needed to support this information exchange are classified as Logical O&M forming an integral part of NBAP.

LSA Localised Service Area. A LSA is an operator-defined area, for which specific access conditions apply. This may correspond to an area in which the Core Network offers specific services. A LSA may be defined within a PLMN or globally. Therefore, a LSA may offer a non-contiguous radio coverage.

## M

Macro cells "Macro cells" are outdoor cells with a large cell radius.

Macro diversity handover "Macro diversity" is a operation state in which a User Equipment simultaneously has radio links with two or more UTRAN access points for the sole aim of improving quality of the radio connection or providing seamless.

Maximum output Power This refers to the measure of average power at the maximum power setting.

Maximum peak power The peak power observed when operating at a given maximum output power.

Maximum Power Setting The highest value of the Power control setting which can be used.

Maximum Total Transmitter Power (dBm) The aggregate maximum transmit power of all channels.

Maximum Transmitter Power Per Traffic Channel (dBm) The maximum power at the transmitter output for a single traffic channel.

Medium Access Control;

Micro cells "Micro cells" are small  cells.

Mobile evaluated handover Mobile evaluated handover (MEHO) is a type of handover triggered by an evaluation made in the mobile.  The mobile evaluates the necessity of handover based on the measured radio environment and based on criteria defined by the network.  When the evaluation meets the hand-off criteria the necessary information is sent from the mobile to the network.  The network then decides on the necessity of the handover based on the reported evaluation result and other conditions, e.g. uplink radio environment and/or availability of network resources, the network may then execute the handover.

Mobile Station A "Mobile Station" (MS) is an entity capable of accessing a set of UMTS services via one or more radio interfaces. This entity may be stationary or in motion within the UMTS service area while accessing the UMTS services, and may simultaneously serve one or more users.

Mobility Management A relation between the mobile station and the UTRAN that is used to set-up, maintain and release the various physical channels.

## N

Node B A logical node responsible for radio transmission / reception in one or more cells to/from the User Equipment. Terminates the Iub interface towards the RNC.

Non-Access Stratum Protocols between UE and the core network that are not  terminated in the UTRAN.

## P

Paging Paging is the act of seeking a User Equipment.

Paging occasions The time instances where it is possible to receive initial paging information.

Peak Power The instantaneous power of the RF envelope which is not expected to be exceeded for [99.9%] of the time.

Physical channel data stream In the uplink, a data stream that is transmitted on one physical channel. In the downlink, a data stream that is transmitted on one physical channel in each cell of the active set.

Physical Channel In FDD mode, a physical channel is defined by code, frequency and, in the uplink, relative phase (I/Q). In TDD mode, a physical channel is defined by code, frequency, and time-slot.

Pico cells "Pico cells" are cells, mainly indoor cells, with a radius typically less than 50 metres.

Power Setting The value of the control signal, which determines the desired transmitter, output Power. Typically, the power setting would be altered in response to power control commands.

Public land mobile network (PLMN) A telcommunications network providing mobile cellular services.

## Q

Quality of Service The collective effect of service performances which determine the degree of satisfaction of a user of a service. It is characterised by the combined aspects of performance factors applicable to all services, such as;

- service operability performance;

- service accessibility performance;

- service retainability performance;

- service integrity performance; and

- other factors specific to each service.

## R

Radio access bearer The service that the access stratum provides to the non-access stratum for transfer of user data between User Equipment and CN.

Radio Access Mode Mode of the cell, FDD or TDD.

Radio Access Network Application Part Radio Network Signalling over the Iu.

Radio Access System UTRA, GSM etc.

Radio Bearer The service provided by the RLC layer for transfer of user data between User Equipment and Serving RNC.

Radio frame A radio frame is a numbered time interval of 10 ms duration used for data transmission on the radio physical channel. A radio frame is divided into 15 time slots of 0.666 ms duration.  The unit of data that is mapped to a  radio frame (10 ms  time interval) may also be referred to as radio frame.

Radio interface The "radio interface" is the tetherless interface between User Equipment and a UTRAN access point. This term encompasses all the functionality required to maintain such interfaces.

Radio link A "radio link" is a logical association between single User Equipment and a single UTRAN access point. Its physical realization comprises one or more radio bearer transmissions.

Radio link addition The procedure where a new radio link is added to the active set.

Radio Link Control;

Radio link removal The procedure where a radio link is removed from the active set.

Radio Network Controller This equipment in the RNS is in charge of controlling the use and the integrity of the radio resources.

Radio Network Subsystem Application Part Radio Network Signaling over the Iur.

Radio Network Subsystem Either a full network or only the access part of a UTRAN offering the allocation and the release of specific radio resources to establish means of connection in between an UE and the UTRAN.
A Radio Network Subsystem is responsible for the resources and transmission/reception in a set of cells.

Radio Network Temporary Identifier (RNTI) A Radio Network Temporary Identifier is an identifier for a UE when an RRC connection exists. It is e.g. used by the MAC protocol on common Transport Channels (RACH, FACH, PCH).

Radio Resource Control

Received Signal Code Power (RSCP) Given only signal power is received, the average power of the received signal after despreading and combining.

Receiver Antenna Gain (dBi) The maximum gain of the receiver antenna in the horizontal plane (specified as dB relative to an isotropic radiator).

Receiver Noise Figure (dB) Receiver noise figure is the noise figure of the receiving system referenced to the receiver input.

Receiver Sensitivity (dBm) This is the signal level needed at the receiver input that just satisfies the required Eb/(No+Io).

Registered PLMN (RPLMN) This is the PLMN on which the UE has performed a location registration successfully.

Registration Area A (NAS) registration area is an area in which the UE may roam without a need to perform location registration, which is a NAS procedure.

Relay Terminal devices capable of ODMA relay communications.

Relay/Seed Gateway Relay or Seed that communicates with the UTRAN, in either TDD or FDD mode.

Relaylink Relaylink is a communications link between two ODMA relay nodes.

Release 99 (R99) A particular version of the UMTS standards produced by the 3GPP project. Also: release 00, release 01, release 02 etc.

Repeater A "repeater" is a radio transceiver used to extend the transmission of a base station beyond its normal range.

Required Eb/(No+Io) (dB) The ratio between the received energy per information bit to the total effective noise and interference power density needed to satisfy the quality objectives.

Roaming The ability for a user to function in a serving network different from the home network.

Root Relay ODMA relay node where communications originate or terminate.

RRC Connection A point-to-point bi-directional connection between RRC peer entities on the UE and the UTRAN sides, respectively. An UE has either zero or one RRC connection.

## S

Seamless handover "Seamless handover" is a handover without perceptible interruption of the radio connection.

Sector A "sector" is a sub-area of a cell. All sectors within one cell are served by the same base station. A radio link within a sector can be identified by a single logical identification belonging to that sector.

Seed Deployed ODMA relay node with or without a display/keypad.

Selected PLMN This is the PLMN that has been selected by the non-access stratum, either manually or automatically.

Service Capabilities Bearers defined by parameters, and/or mechanisms needed to realise services. These are within networks and under network control.

Service feature Standardised building block used to create services.

Services (of a mobile cellular system) The set of unctions that the mobile cellular system can make available to the user.

Serving Network The serving network provides the user with access to the services of home environment.

Service Access Point;

Serving RNS A role an RNS can take with respect to a specific connection between an UE and UTRAN. There is one Serving RNS for each UE that has a connection to UTRAN. The Serving RNS is in charge of the RRC connection between a UE and the UTRAN. The Serving RNS terminates the Iu for this.

Shared Channel;

Signaling connection An acknowledged-mode link between the user equipment and the core network to transfer higher layer information between the entities in the non-access stratum.

Signaling link Provides an acknowledged-mode link layer to transfer the MS-UTRAN signaling messages as well as MS - Core Network signaling messages  (using the signaling connection.

Soft Handover Soft handover is a category of handover procedures where the radio links are added and abandoned in such manner that the UE always keeps at least one radio link to the UTRAN.

SRNS Relocation The change of Iu instance and transfer of the SRNS role to another RNS.

Subscriber The responsibility for payment of charges incurred by one or more users may be undertaken by another entity designated as a subscriber. This division between use of and payment for services has no impact on standardisation.

Suitable Cell This is a cell on which an UE may camp. It must satisfy certain conditions.

Supplementary service Is a service which modifies or supplements a basic telecommunication service. Consequently, it cannot be offered to a user as a standalone service. It must be offered together with or in association with a basic telecommunication service. The same supplementary service may be common to a number of basic telecommunication services.

## T

Teleservice Is a type of telecommunication service that provides the complete capability, including terminal equipment functions, for communication between users according to standardised protocols and transmission capabilities established by agreement between operators.

Terminal A device into which a UICC can be inserted and which is capable of providing access to UMTS services to users, either alone or in conjunction with a UICC.

Test environment A "test environment" is the combination of a test propagation environment and a deployment scenario, which together describe the parameters necessary to perform a detailed analysis of a radio transmission technology.

Traffic channel A "traffic channel" is a logical channel which carries user information.

Transmission Time Interval Transmission Time Interval is defined as the inter-arrival time of Transport Block Sets, i.e. the time it should take to transmit a Transport Block Set.

Transmitter Antenna Gain (dBi) The maximum gain of the transmitter antenna in the horizontal plane (specified as dB relative to an isotropic radiator.

Transport Block Transport Block is defined as the basic unit passed down to L1 from MAC, for L1 processing.  An equivalent term for Transport Block is “MAC PDU”.

Transport Block Set Transport Block Set is defined as a set of Transport Blocks that is passed to L1 from MAC at the same time instance using the same transport channel. An equivalent term for Transport Block Set is  “MAC PDU Set”.

Transport Block Set Size Transport Block Set Size is defined as the number of bits  in a Transport Block Set.

Transport Block Size Transport Block Size is defined as the size (number of bits) of a Transport Block.

Transport channel The channels offered by the physical layer to Layer 2 for data transport between peer L1 entities are denoted as Transport Channels. Different types of transport channels are defined  by how and with which characteristics data is transferred on the physical layer, e.g. whether using dedicated or common physical channels.

Transport Format A Transport Format is defined as a format offered by L1 to MAC for the delivery of a Transport Block Set during a Transmission Time Interval on a Transport Channel. The Transport Format constitutes of two parts – one dynamic part and one semi-static part.

Transport Format Combination A Transport Format Combination is defined as the combination of currently valid Transport Formats on all Transport Channels of an MS, i.e. containing one Transport Format from each Transport Channel.

Transport Format Combination Set A Transport Format Combination Set is defined as a set of Transport Format Combinations to be used by an MS.

Transport Format Combination Indicator (TFCI) A Transport Format Combination Indicator is a representation of the current Transport Format Combination.

Transport Format Identification  (TFI) A label for a specific Transport Format within a Transport Format Set.

Transport Format Set A set of Transport Formats. For example, a variable rate DCH has a Transport Format Set (one Transport Format for each rate), whereas a fixed rate DCH has a single Transport Format.

## U

UMTS IC Card (UICC) An IC card (or 'smartcard') of defined electromechanical specification which contains at least one USIM.

Universal Mobile Telecommunications System (UMTS) The telecommunications system, incorporating mobile cellular and other functionality, that is the subject of standards produced by 3GPP.

Universal Subscriber Identity Module (USIM) An application residing on the UICC used for accessing UMTS services with appropriate security.

Universal Terrestrial Radio Access Network UTRAN is a conceptual term identifying that part of the network which consists of RNCs and Node Bs between Iu an Uu.

Uplink An "uplink" is a unidirectional radio link for the transmission of signals from a UE  to a base station, from a Mobile Station to a mobile base station or from a mobile base station to a base station.

URA updating URA updating is a family of procedures that updates the UTRAN registration area of a UE when a RRC connection exists and the position of the UE is known on URA level in the UTRAN.

User Equipment A Mobile Equipment with one or several UMTS Subscriber Identity Modules(s).

UTRAN Registration Area (URA) The UTRAN Registration Area is an area covered by a number of cells. The URA is only internally known in the UTRAN.

UTRAN access point A conceptual point within the UTRAN performing radio transmission and reception. A UTRAN access point is associated with one specific cell, i.e. there exists one UTRAN access point for each cell. It is the UTRAN-side end point of a radio link.

User Profile Is the set of information necessary to provide a user with a consistent, personalised service environment, irrespective of the user’s location or the terminal used (within the limitations of the terminal and the serving network).

User An entity, not part of UMTS, which uses UMTS services. Example: a person using a UMTS mobile station as a portable telephone.

Uu The Radio interface between UTRAN and the User Equipment.

## V

Value Added Service Provider Provides services other than basic telecommunications service for which additional charges may be incurred.

Virtual Home Environment A concept for personal service environment portability across network boundaries and between terminals.

Visited PLMN of home country This is a PLMN, different from the home PLMN, where the MCC part of the PLMN identity is the same as the MCC of the IMSI.

# Abbreviations

## A

AAL	ATM Adaptation Layer

AAL2	ATM Adaptation Layer type 2

AAL5	ATM Adaptation Layer type 5

ACCH	Associated Control Channel

ACIR	Adjacent Channel Interference Ratio

ACK	Acknowledgement

ACLR	Adjacent Channel Leakage Power Ratio

ACS	Adjacent Channel Selectivity

AESA	ATM End System Address

AI	Acquisition Indicator

AICH	Acquisition Indication Channel

ALCAP 	Access Link Control Application Protocol

AP 	Access preamble

ARP 	Address Resolution Protocol

ARQ 	Automatic Repeat Request

AS	Access Stratum

ASC	Access Service Class

ASN.1	Abstract Syntax Notation One

ATM	Asynchronous Transfer Mode

AWGN	Additive White Gaussian Noise

## B

BCCH 	Broadcast Control Channel

BCFE 	Broadcast Control Functional Entity

BCH	Broadcast Channel

BER	Bit Error Rate

BID	Binding Identity

BLER	Block Error Rate

BPSK	Binary Phase Shift Keying

BS	Base Station

BSC	Base Station Controller

BSS	Base Station System

BTS   	Base Transceiver Station

## C

Control-

CA	Capacity Allocation

CAA	Capacity Allocation Acknowledgement

CB	Cell Broadcast

CBR	Constant Bit Rate

CC	Call Control

CCCH	Common Control Channel

CCH	Control Channel

CCPCH	Common Control Physical Channel

CCTrCH	Coded Composite Transport Channel

CD	Capacity Deallocation or Collision Detection

CDA	Capacity Deallocation Acknowledgement

CDMA	Code Division Multiple Access

CFN	Connection Frame Number

CN	Core Network

CPICH	Common Pilot Channel

CPCH	Common Packet Channel

CPCS	Common Part Convergence Sublayer

CPS	Common Part Sublayer

CRC	Cyclic Redundancy Check

CRNC	Controlling Radio Network Controller

CS	Circuit Switched

CTCH	Common Traffic Channel

CTDMA	Code Time Division Multiple Access

SCTP	S Common Transport Protocol CHECK WITH wg3

CW	Continuous Wave (unmodulated signal)

## D

DC	Dedicated Control (SAP)

DCA	Dynamic Channel Allocation

DCCH	Dedicated Control Channel

DCH	Dedicated Channel

DHO	Diversity Handover

DL	Downlink (Forward Link)

DPCCH	Dedicated Physical Control Channel

DPCH	Dedicated Physical Channel

DPDCH	Dedicated Physical Data Channel

DRNC	Drift Radio Network Controller

DRNS	Drift RNS

DRX	Discontinuous Reception

DS-CDMA	Direct-Sequence Code Division Multiple Access

DSCH	Downlink Shared Channel

DTCH	Dedicated Traffic Channel

DTX	Discontinuous Transmission

## E

EIRP	Equivalent Isotropic Radiated Power

## F

FACH 	Forward Access Channel

FAUSCH	Fast Uplink Signaling Channel

FBI	Feedback Information

FCS	Frame Check Sequence

FDD	Frequency Division Duplex

FDMA	Frequency Division Multiple Access

FEC	Forward Error Correction

FER	Frame Erasure Rate, Frame Error Rate

FN	Frame Number

FP	Frame Protocol

## G

GC	General Control (SAP)

GMSK	Gaussian Minimum Shift Keying

GP	Guard Period

GPRS	General Packet Radio System

GSM	Global System for Mobile communications

GTP	GPRS Tunneling Protocol

## H

HCS	Hierarchical Cell Structure

HHO	Hard Handover

HO	Handover

## I

IMA	Inverse Multiplexing on ATM

IMSI	International Mobile Subscriber Identity

IP	Internet Protocol

IP-M	IP Multicast

ISCP	Interference Signal Code Power

ITU	International Telecommunication Union

## J

JD	Joint Detection

JP	Joint Predistortion

## K

kbps	kilo-bits per second

ksps	kilo-symbols per second

## L

L1	Layer 1 (physical layer)

L2	Layer 2 (data link layer)

L3	Layer 3 (network layer)

LAC	Link Access Control

LAI	Location Area Identity

LCD	Low Constrained Delay

LLC	Logical Link Control

LSA	Local Service Area

## M

MA	Multiple Access

MAC	Medium Access Control

MCC	Mobile Country Code

Mcps	Mega-chips per second

MDS	Multimedia Distribution Service

ME	Mobile Equipment

MEHO 	Mobile evaluated handover

MER 	Message Error Rate

MM	Mobility Management

MNC	Mobile Network Code

MO	Mobile Originated

MOHO	Mobile Originated Handover

MS	Mobile Station

MSID	Mobile Station Identifier

MSC	Mobile Services Switching Center

MT	Mobile Terminated

MTP	Message Transfer Part

MTP3-B	Message Transfer Part level 3

MUI	Mobile User Identifier

## N

NAS	Non-Access Stratum

NBAP	Node B Application Part

NEHO 	Network evaluated handover

NNI	Network-Node Interface

NRT	Non-Real Time

NSAP	Network Service Access Point

Nt	Notification (SAP)

## O

OCCCH	ODMA Common Control Channel

ODCCH	ODMA Dedicated Control Channel

ODCH	ODMA Dedicated Channel

ODMA	Opportunity Driven Multiple Access

O&M	Operation and Management

ORACH	ODMA Random Access Channel

ODTCH	ODMA Dedicated Traffic Channel

OVSF	Orthogonal Variable Spreading Factor

## P

PC	Power Control

PCCC	Parallel Concatenated Convolutional Code

PCCH	Paging Control Channel

PCH 	Paging Channel

PCPCH	Physical Common Packet Channel

PCCPCH	Primary Common Control Physical Channel

PCS 	Personal Communication System

PDH	Plesiochronous  Digital Hierarchy

PDSCH	Physical Downlink Shared Channel

PDU	Protocol Data Unit

PG	Processing Gain

PHS 	Personal Handyphone System

PHY	Physical layer

PhyCH	Physical Channel

PI	Page Indicator

PICH	Page Indication Channel

PID	Packet Identification

PLMN	Public Land Mobile Network

PMD	Physical Media Dependent

PN	Pseudo Noise

PPM	Parts Per Million

PRACH	Physical Random Access Channel

PS	Packet Switched

PSC	Primary Synchronization Code PSCCCH	Physical Shared Channel Control Channel

PSCH	Physical Shared Channel

PTM	Point-to-Multipoint

PTM-G	PTM Group Call

PTM-M	PTM Multicast

PU	Payload Unit

## Q

QoS	Quality of Service

QPSK	Quadrature (Quaternary) Phase Shift Keying

## R

RAB	Radio Access Bearer

RACH	Random Access Channel

RANAP	Radio Access Network Application Part

RF	Radio Frequency

RL	Radio Link

RLC	Radio Link Control

RLCP	Radio Link Control Protocol

RNC	Radio Network Controller

RNS	Radio Network Subsystem

RNSAP	Radio Network Subsystem Application Part

RNTI	Radio Network Temporary Identity

RRC	Radio Resource Control

RRM	Radio Resource Management

RSCP	Received Signal Code Power

RSSI	Received Signal Strength Indicator

RT	Real Time

RU	Resource Unit

RX	Receive

## S

SAAL	Signaling ATM Adaptation Layer

SACCH	Slow Associated Control Channel

SAP	Service Access Point

SAR	Segmentation and Reassembly

SCCH	Synchronization Control Channel

SCCPCH	Secondary Common Control Physical Channel

SCH	Synchronization Channel

SDCCH	Stand-Alone Dedicated Control Channel

SDH	Synchronous Digital Hierarchy

SDU	Service Data Unit

SF	Spreading Factor

SFN	System Frame Number

SIR	Signal-to-Interference Ratio

SMS	Short Message Service

SMS-CB	SMS Cell Broadcast

SP	Switching Point

SRNC	Serving Radio Network Controller

SRNS	Serving RNS

SS7	Signaling System No. 7

SSC	Secondary Synchronization Code

SSCOP	Service Specific Connection Oriented Protocol

SSCF	Service Specific Co-ordination Function

SSCF-NNI	Service Specific Coordination Function – Network Node Interface

SSCS	Service Specific Convergence Sublayer

SSDT	Site Selection Diversity Transmission

SSSAR	Service Specific Segmentation and Re-assembly sublayer

STC	Signaling Transport Converter

STTD	Space Time Transmit Diversity

## T

TC	Transmission Convergence

TCH	Traffic Channel

TDD	Time Division Duplex

TDMA	Time Division Multiple Access

TF	Transport Format

TFC	Transport Format Combination

TFCI 	Transport Format Combination Indicator

TFCS	Transport Format Combination Set

TFI	Transport Format Indicator

TFS	Transport Format Set

TMSI	Temporary Mobile Subscriber Identity

TN	Termination Node

TPC	Transmit Power Control

TrCH	Transport Channel

TSTD	Time Switched Transmit Diversity

TTI	Transmission Timing Interval

TX	Transmit

## U

UARFCN	UTRA Absolute Radio Frequency Channel Number

UARFN	UTRA Absolute Radio Frequency Number

UDD	Unconstrained Delay Data

UDP	User Datagram Protocol

UE	User Equipment

UER	User Equipment with ODMA relay operation enabled

UL	Uplink (Reverse Link)

UMTS	Universal Mobile Telecommunications System

UNI	User-Network Interface

UP	User Plane

URA	User Registration Area

USCH	Uplink Shared Channel

USIM	UMTS Subscriber Identity Module

UTRA	Universal Terrestrial Radio Access

UTRAN	Universal Terrestrial Radio Access Network

## V

VA	Voice Activity factor

VBR	Variable Bit Rate

VC	Virtual Circuit

VHE	Virtual Home Environment

## W

WCDMA	Wideband Code Division Multiple Access

# Equations

|  | Average energy per PN chip for DPCH. |
| --- | --- |
|  | The ratio of the received energy per PN chip of the DPCH to the total transmit power spectral density at the BS antenna connector. |
|  | Average energy per information bit for the PCCPCH, SCCPCH and DPCH, at the UE antenna connector. |
|  | The ratio of combined received energy per information bit to the effective noise power spectral density for the PCCPCH, SCCPCH and DPCH at the UE antenna connector. Following items are calculated as overhead: pilot, TPC, TFCI, CRC, tail, repetition, convolution coding and turbo coding. |
|  | Average energy per PN chip. |
|  | The ratio of the average transmit energy per PN chip for different fields or physical channels to the total transmit power spectral density. |
| Fuw | Frequency of unwanted signal |
|  | The total received power spectral density, including signal and interference, as measured at the UE antenna connector. |
|  | The power spectral density of a band limited white noise source (simulating interference from other cells) as measured at the UE antenna connector. |
|  | The total transmit power spectral density of the Forward link at the base station antenna connector. |
|  | The received power spectral density of the Forward link as measured at the UE antenna connector. |
|  | The effective noise power spectral density at the UE antenna connector. |
|  | Average energy per PN chip for the OCNS. |
|  | The ratio of the average transmit energy per PN chip for the OCNS to the total transmit power spectral density. |
|  | The ratio of the received PCCPCH energy per chip to the total received power spectral density at the UE antenna connector. |
|  | The ratio of the average transmit energy per PN chip for the PCCPCH to the total transmit power spectral density. |
|  | Secondary Common Control Physical Channel. |
|  | Average energy per PN chip for SCCPCH. |

# Annex A (informative):
Change Request History

| TSG_MEETING | TSG_DOC | SPEC | VERS_CURRENT | VERS_NEW | CR | REV | SUBJECT |
| --- | --- | --- | --- | --- | --- | --- | --- |

# History

| Document history |
| --- |
| 0.0.1 | 28.07.99 | First Draft |
| 0.1.0 | October 1999 | Inclusion of complete text of 25.990 Version 3.0.0 |
| 0.1.1 | November 1999 | New Editor, editorial changes |
| Editor |
| Michele Zarri One2One Communications Ltd Tel: +44-208-214-4169 Fax: +44-208-905-1671 GSM: +44-793-200-2114 e-mail michele.zarri@one2one.co.uk |
| This document has been written in Microsoft Word 97 |