TSG-SA Working Group 1 (Services) meeting #7	TSG S1 (00) xxx

Sophia Antipolis, France 7 - 11 February 2000	Agenda Item: 6.4

## Source: 	BT

## Title:	Comment on PS domain feature list

# Introduction

BT is of the believe that the PS domain feature list given in  TR 22.976 version 0.54 should:

- Be in the main body of the text not an annex

- Should be moved to clause  4.6 and maybe replace some of the information in 4.6

- Should be reviewed against the figure given below to identify;

- features in IM/PS domain (Blue)

- features in CS domain (Lavender/Turquoise)

- features in overlap(Green)

- Features only in the CS domain should be removed from the list

- Notes and comments need review and change

Figure 1

## Updating of table

“Changes excepted” has been applied to TR 22.976 version 0.54 to give clean text

The features in the table below has been highlighted in appropriate colours to indicate domains.

The colours in the table are only for developing the table and should not in the final text (difficult to print!)

Inappropriate domains have been deleted.

Comments have been added

### Conclusion

This exercise should be further progressed and the new table put in the main body of the text.

# Annex A		IM/PS Domain feature list evaluation for release 2000 (Normative)

Key to Table

E = Essential for release 00, launch of a commercial all-IP network is not viable with these missing or required in R00 terminal specifications to enable forward compatibility to future releases

D= Desirable for Release 2000, important features to enable a competitive and successful service launch, but could be slipped to Release 2001

R99 = Features already supported in Release 99, shall also be supported as part of Release 2000

R01+ = could wait for these features, but hooks are required in Release 2000 to enable them to be added later

No = Not needed in the PS domain

Note:	Circuit switched domain services are not considered at this annex. S1 has agreed to maintain the existing Release 99 requirements in Release 2000, allowing full service continuity.

Note: All Release 99 features shifted by any reason to Release 2000 shall be included as E R’00 (to be verified feature by feature)

| Feature Name | Short description | R99 | E R00 | D R00 | R01+ | No | Comments/Notes |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DTAP CC | i.e. 04.08 based CC. Seamless support for existing GSM services This set of requirements means 04.08/04.80 CC and SS in PS domain |
|  |  | X |  |  |  |  | . |
| . |  |  |  |  |  |  |  |
| IP CC | e.g. H.323 / SIP related IP multimedia services. |
| IP multimedia services |  |  |  |  |  |  |  |
| IP telephony Name is wrong should be speech | Single medium IP voice call (using H.323 or SIP) with end user perceived quality equal or better than 2G GSM voice call |  |  |  |  |  | MMI must be identical to the standard telephony MMI (dialled digit, off hook, connection, on hook). Including end to end QoS support. |
| Multimedia IP Call | Includes IP telephony, all real time calls single and multi-media, processed by IP CC |  |  |  |  |  | Including end to end QoS support. It is desirable to limit the standard to one protocol only. S2 should decide on the standard protocol. The usage of any additional protocol may be based on the network transport function (bearer service). |
| Emergency Voice Call This is part of a sceech call But with location information Green | Basic emergency voice call over IP |  |  |  |  |  | This must use the existing emergency numbering schemes (22.101). Must be compliant with FCC mandates, European and other regulatory requirements. |
| Group calling Green | This requirement covers various group call services (e.g. PMR/ASCI type of services) |  |  |  |  |  | Service requirements FFS |
| Short message service (CBS) Green | As specified by 23.041. | X |  |  |  |  | No additional standardisation work required for S1 |
| Short message service (SMS PTP) Greeen | As specified by 23.040. | X |  |  |  |  | No additional standardisation work required for S1 |
| Multimedia messages (MMS) Blue | Support of multimedia messaging in PS domain | ? |  |  |  |  | Currently supported in R99 for MS/MS. Need to consider messaging to and from other access. |
| Facsimile service |  |  |  |  |  |  |  |
| Turquoise |  |  |  |  |  |  |  |
| Turquoise |  |  |  |  |  |  |  |
| What does it mean? Turquoise |
| IP bearer services |  |  |  |  |  |  |  |
| Point-to-Point green | As in 22.060 | X |  |  |  |  | No additional standardisation work required for S1 |
| Point-to-Multipoint green | PTM services such as PTM-Multicast, PTM Group Call, IP Multicast, IP Distribution Services (MDS) |  |  |  |  |  | Implementation of PTM services for example as defined within GPRS specifications |
| Asymmetric bearers Green | Separate parameters at the User Interface for the uplink and downlink data rate and QoS. This feature is already within R99 (e.g. TS 23.107) | X |  |  |  |  | No additional standardisation work required for S1 |
| Support of QoS mechanisms for real time services Is this point to point what does it mean here |  | ? |  |  |  |  | QoS is also part of R99, but the features for real time conversational services might be delayed |
| Multicall capability | Support of multiple active PS sessions (TS 22.060) | X |  |  |  |  | No additional standardisation work required for S1 |
| Tile does not mach the defination |
| Interworking |  |  |  |  |  |  | Including end to end QoS support |
| IPv4 interworking Blue |  | X |  |  |  |  | Same reqs as Rel 99 GPRS Need work |
| IPv6 interworking Blue |  | X |  |  |  |  | Same reqs as Rel 99 GPRS(?) Need work |
| Speech to/from PSTN / ISDN / 2G CS mobile / 3G CS mobile Green | Full interoperability between corresponding services in PSTN/GSM environment and UMTS rel00 environment Clarify as speech bearer |  |  |  |  |  |  |
| Multimedia to/from Internet-H.323 Blue | H.323 protocol interworking |  |  |  |  |  | Incl. Intranet. |
| Multimedia to/from Internet –SIP Blue | SIP protocol interworking |  |  |  |  |  | Incl. Intranet. |
| Modem and ISDN interworking | Access to PSTN / ISDN dial up –data services |  |  |  |  |  | Removed from R99 at SA1#6 |
| Interworking with ISDN multimedia applications | Service compatibility between real time single/multimedia N-ISDN applications and single/multimedia UMTS rel 00 applications including H.324 |  |  |  |  |  |  |
| Interworking with other access networks (e.g. cable) What does it mean? |  |  |  |  |  |  |  |
| Interworking with intranets (including VPNs) | VPN functionality (firewall bypass) shall be supported Does this really mean bypass – this word could be misinterpreted |  |  |  |  |  | May possibly be supported at the application layer. |
| User Roaming | Editor's note: Roaming section not reviewed |  |  |  |  |  |  |
| CS/PS GSM/UMTS R99 user to R00 PS/IM Green |  |  |  |  |  |  | (U)SIM and Multimode terminal Roaming. Roaming should be possible for both R99 and pre R99 GSM/GPRS networks. (Note: roaming to R00 CS is included but not within the scope) |
| R00 PS to GSM/GPRS Green |  |  |  |  |  |  | (U)SIM and Multimode terminal roaming. Roaming should be possible for both R99 and pre R99 GSM/GPRS networks. |
| ANSI-41 to R00 PS Green |  |  |  |  |  |  |  |
| R00 PS to ANSI-41 Green Should also include R000PS /IM to R99/R00CS Green |  |  |  |  |  |  |  |
| Handover Assuming intra domain is supported | Editor's note: Handover section not reviewed For any of the services the qos for then need to be maintained during the session. |  |  |  |  |  | QoS should be maintained thoughtout the duration of a session including change of network nodes e.g SGSN to SGSN |
| Speech from PS/IM Domain to CS-GSM /UMTS |  |  |  |  |  |  |  |
| Speech from CS-GSM /UMTS to PS/IM Domain |  |  |  |  |  |  |  |
| Handover of parallel sessions/calls (with different QoS) |  |  |  |  |  |  |  |
| Multimedia handover between R00 UTRAN and GERAN |  |  |  |  |  |  | To include real-time services in addition to R99 “best effort” |
| Multimedia services to/from alternative access technologies (e.g. HIPERLAN/2) |  |  |  |  |  |  | Alternative access technologies to include HIPERLAN/2 |
| Supplementary Services (PS Domain) |  |  |  |  |  |  | IP Multimedia / IP Telephony aware supplementary services to be considered only from end-user need view point. (Standardization, service capabilities and implementation FFS). S2 choice of MM CC protocol may support some MM services implicitly. Some of the following services can be provided at the application level (i.e. no standardisation required). The H.450 standards defines supplementary services for H.323, and SIP provides tools to build supplementary services. |
| Multimedia Call Barring Blue | Enables mobile subscriber to have barring of certain categories of outgoing multimedia calls. |  |  |  |  |  | Also includes incoming multimedia calls and barring when roaming. |
| Network Barring Green | Editor's note: Description and justification to be supplied by Horst Rauch (T-Mobil) |  |  |  |  |  | FFS |
| Session Barring | Editor's note: Description and justification to be supplied by Horst Rauch (T-Mobil) |  |  |  |  |  | FFS |
| Bearer Barring | Editor's note: Description and justification to be supplied by Horst Rauch (T-Mobil) |  |  |  |  |  | FFS. Might be based on the QoS parameters. |
| Multimedia Call Forwarding | Forwarding of multimedia call (e.g. triggered by conditions of Unconditional, Busy, No Reply, Not Reachable etc). Triggers/activation will be different and more detailed in a MM environment for the different media components. |  |  |  |  |  | Conditions require to be evaluated. |
| Multimedia Call Transfer | Enables served mobile subscriber who has a multimedia call, to connect the other parties in the multimedia call and release the served mobile subscriber’s own connection. |  |  |  |  |  |  |
| Multimedia Call Deflection Service | Enables the served mobile subscriber to respond to an incoming multimedia call offered by the network by requesting redirection of this multimedia call to another address or location. |  |  |  |  |  |  |
| Multimedia Call Holding | Allows served mobile subscriber to interrupt communication on an existing active multimedia call and then subsequently re-establish communication |  |  |  |  |  |  |
| Multimedia Call Waiting | Permits mobile subscriber to be notified of an incoming multimedia call while the mobile subscriber is engaged in other multimedia call(s). Subscriber can either accept, reject, ignore, or deflect the incoming multimedia call. |  |  |  |  |  |  |
| Advice of Charge | Supply user sufficient information to allow real-time estimate of the call charge. |  |  |  |  |  |  |
| Caller Identification and restriction | Similar to CLIP, CLIR, CNAP and CNAR. Editor's note: add to abbreviations |  |  |  |  |  | Could include additional IP related information such as IP address. Need to support European, FCC and other regulatory requirements. |
| Connected Line Identification and restriction | Similar to COLP and COLR Editor's note: add to abbreviations |  |  |  |  |  | Could include additional IP related information such as IP address. Need to support European, FCC and other regulatory requirements. |
| Multimedia conferencing | Similar to Multiparty but is applicable to multimedia calls. |  |  |  |  |  |  |
| Multimedia call-back when free / CCBS | Editor's note: definition required in the MM case |  |  |  |  |  |  |
| Closed user group (CUG) / community of interest | Editor's note: definition required in the MM case |  |  |  |  |  |  |
| Precedence and Pre-emption service | Editor's note: definition required in the MM case |  |  |  |  |  |  |
| Network Services |  |  |  |  |  |  |  |
| Operator Determined Barring (ODB) Green | Allows service providers to regulate subscriber access to services by the barring of certain categories of outgoing or incoming multimedia calls and packet services. ODB could terminate ongoing multimedia calls and could bar future multimedia calls and packet services. | ? |  |  |  |  |  |
| CAMEL Support for Multimedia Services Green | Provides mechanisms to support multimedia services consistently & independently of the serving network. |  |  |  |  |  | CAMEL enhancements, but additionally needs to support multimedia calls. Implementation is FFS. Editor's note: DeWayne Sennet (AWS) to WIN support proposal |
| (U)SIM Toolkit | Feature provides a set of facilities which allow the (U)SIM to interact with external entities (e.g. the network, the Mobile Equipment, or the user) to enable value-added multimedia applications to exist in the (U)SIM. |  |  |  |  |  |  |
| OSA for new elements What does this mean | Provision of an API for controlled, secure and accountable access to multimedia service capability features by applications, based on the user profile |  |  |  |  |  | E.g. H.323/SIP CSCF. |
| LCS for GPRS/PS domain Green | Support of LCS on the PS domain required to meet regulatory and commercial requirements (e.g., 3GPP 22.071) |  |  |  |  |  | Exact work required is for FFS. Need to support European, FCC and other regulatory requirements. |
| SoLSA Green | SoLSA shall facilitate user-dependent radio resource selection based on LSA (e.g. when user is located at his office, radio coverage provided with indoor radio solutions should be preferred). |  |  |  |  |  |  |
| Lawful Surveillance / Intercept Green |  |  |  |  |  |  | Need to support European, FCC and other regulatory requirements. |
| Number Portability Green | Ability for subscriber to change service providers while retaining the original directory number. Includes mobile to mobile, mobile to landline, & landline to mobile number portability scenarios. |  |  |  |  |  | Need to support European, FCC and other regulatory requirements. |
| Mobile Station Application Execution Environment (MExE) | Provides standardized execution environment in an MS, and an ability to negotiate its supported capabilities with a MExE service provider, allowing applications to be developed independently of any MS platform. |  |  |  |  |  |  |
| Personalization of Mobile Equipment (ME) Not relavent | Storage of information in the ME which limits the SIMs which will operate with the ME. | X |  |  |  |  | No standardisation work required for R99 |
| Advanced Addressing Blue | Support of symbolic and advanced addressing |  |  |  |  |  | Addressing depends on applications, e.g. e-mail addresses are used for e-mail, E.164 is used for telephony, ICQ uses IP addresses. This does not require standardisation by 3GPP. |
| System Selection Green Needs looking at | Ability for the mobile equipment to choose a preferred service provider, based upon geographic location, frequency band preferences, available operators, etc. Also the ability to force a mobile station to "disallow" service from a "forbidden" service provider, and to force a mobile station to use "home" services. Service provider lists must be downloadable over-the-air. The possibility for operators with multimode networks, e.g. with GSM and UMTS radio access networks, to control which RAN a user accesses. |  |  |  |  |  | Similar to ANSI-136 Intelligent Roaming. Why?? |
| Over-the-Air Service Provisioning | Ability to download parameters to either the SIM or ME for provisioning of services. This includes both subscription parameters as well as operator-specific parameters. |  |  |  |  |  | Similar to ANSI-136 OTASP and OTAPA. |
| Charging |  |  |  |  |  |  |  |
| Implementation of on-line charging mechanisms for the support of Pre-paid services | Definition of charging mechanisms for the support of IP multimedia pre-paid services |  |  |  |  |  |  |
| Event/transaction based charging mechanisms (e.g. content based) Relates to OSA blue | Definition of charging mechanisms for the provisioning of IP based Value Added Services |  |  |  |  |  |  |
| Charging aspects – need to charge for each PDP context (PS sessions) independently Blue |  |  |  |  |  |  |  |