| 3GPP SA Working Group 1 Meeting #7 | Document | S1-000065 |
| --- | --- | --- |
| Sophia Antipolis, 09 Feb - 11 Feb 2000 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 22.078 | CR |  | Current Version: | 3.2.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: |  | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio |  | Core Network | x |
| (at least one should be marked with an X) |
| Source: | NTT DoCoMo | Date: | 7/2/00 |
| Subject: | In-band user interaction for dialled services in CAMEL ph3 |
| Work item: | CAMEL Phase 3 |
| Category: | F Correction | x | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | x |
|  |  |  |  | Release 00 |  |
| Reason for change: | Clarify the scope of CAMEL phase 3. It is necessary to provide In-band user interaction capability for the dialled service (subscribed and serving network) as the user interaction capability is essential for CAMEL supported services. There is no clear reason to exclude this capability from CAMEL ph3, except for service interaction comes from previously invoked service. This is also mentioned for stage 2/3 specification. In addition, the allowed instruction for the dialled service is too restrictive, so it is also proposed to remove such restriction. |
| Clauses affected: | 5.3.2.2, 7.2 |
| Other specs | Other 3G core specifications | x | ( List of CRs: | 23.078 |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

### ---------- First modified section ----------

There shall be no restriction regarding the order of the above instructions or the number of times each of the above instructions can be repeated. Once the CSE has concluded issuing the above instructions, it shall issue one and only one of the following instructions:

-	bar the call (i.e. release the call prior to connection);

-	allow the call processing to continue unchanged;

-	allow the call processing with modified information. The CSE shall have the possibility to send the information listed in table: A-2 (Call set up request procedure 1).

### 5.3.2	Procedure for subscribed dialled services $(CAMEL3$)

The purpose of this procedure is to detect a call set-up request at the point where the called party number has been compared with the dialled services information, and allow the CSE to modify the handling of the call set-up request. Triggering of this procedure shall happen immediately after the procedure when dialled digits have been collected.

#### 5.3.2.1	Initiation of contact with the CSE

If (according to the CSI):

-	the subscriber is provisioned with a CAMEL based originating service; and

-	the call set-up request occurs; and

-	the criteria are satisfied.

Then the VPLMN shall suspend call processing, make contact with the CSE and await further instructions.

Note that contact to the CSE shall (if necessary) be made in this manner before network dialled services are invoked;

For mobile originated calls the information listed in table: A-1 (Call set-up request procedure 3) shall be provided to the CSE if available.

For forwarded calls the information listed in table: A-1 (Call set-up request procedure 4) shall be provided to the CSE if available.

#### 5.3.2.2	Further processing of the call

When the VPLMN has made contact with the CSE (or reported events to the CSE when contact has already been established), the CSE shall be able to instruct the VPLMN to act as described below:

-	allow the call processing to continue unchanged;

-	allow the call processing with modified information. The CSE shall have the possibility to send the information listed in table: A-2 (Call set up request procedure 2).

-	release the call;

-	perform charging activities.

-	order in-band user interaction. (Interaction between the service triggered from previous triggering may be needed to avoid duplicated guidance etc.)

Further processing of the call continues as detailed in Sections 5.3 to 5.8, and the CSE contact initiated at this procedure is terminated.

### ---------- Second modified section ----------

## 7.2	Further processing of the call

When the serving network has made contact with the CSE, the CSE shall be able to instruct the serving network to act as described below:

-	allow the call processing to continue unchanged;

-	allow the call processing with modified information. The CSE shall have the possibility to send the information listed in table: A-2 (Procedures for serving network dialled services 2).

-	release the call;

-	perform charging activities.

-	order in-band user interaction. (Interaction between the service triggered from previous triggering may be needed to avoid duplicated guidance etc.)

Further processing of the call continues as detailed in Sections 5.3 to 5.8, and the CSE contact initiated at this procedure is terminated.