| 3GPP TSG-SA WG1 Meeting #7 | Document | S1000148 |
| --- | --- | --- |
| Sophia-Antipolis, France, 9th – 11thFeb, 2000 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 22.060 | CR |  | Current Version: | 3.2.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: |  | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio | X | Core Network | X |
| (at least one should be marked with an X) |
| Source: | NTT DoCoMo, Lucent Technologies | Date: |  |
| Subject: | The support of Push Services for GPRS |
| Work item: |  |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 |  |
|  |  |  |  | Release 00 | X |
| Reason for change: | S1 requests to use dynamic IP address for push service. S1 would like to realize push service in inactive, although it is one of the ways to be always in active. |
| Clauses affected: | 6.7 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

## 6.7	Activation

The subscriber shall be able to activate each of the registered interworking profiles independently within the limitations of the subscription profile.  As an option the GPRS network may request the activation of a specific interworking profile for a GPRS attached mobile, when a mobile terminated packet or activation request from external data network with user-ID (e.g. MSISDN) is received even if a mobile is inactive.  This option may be available for one or more PDP.  The activation of the inter-working profile(s) may be performed automatically by the MS immediately after GPRS Attach.  When an interworking profile  is activated a dynamic binding between the GSM/GPRS identity of the MS and the external data network user-ID and/or address is made by the system, and the appropriate service parameters are applied thus establishing a virtual connection  between the MS and the GPRS network. Activation of an interworking profile results in a dynamic binding until de-activation is performed.

## 6.8	De-activation

The subscriber shall be able to de-activate the previously activated interworking profiles independently within the limitations of the subscription profile thus releasing the previously established virtual connection. An interworking profile(s) shall be automatically de-activated if the provision for the supporting GPRS service is withdrawn. Interworking profiles are deactivated automatically upon GPRS detach..

De-activation of a particular interworking profile shall abort all presently on-going communication between the MS and the external data network. Any previously negotiated schedule for the PTM-M service shall remain unaffected.