TSG-SA Working Group 1 (Services) meeting #8	TSG S1 (00) 205

Beijing, China: 10-14th April 2000	Agenda Item:

| 3GPP TSG-CN-WG1, Meeting #11 28 February - 03.March. 2000 Umea, Sweden | Tdoc N1-000452 |
| --- | --- |

Title:	Response on Liaison statement concerning the change of 
title of 23.060

Source:	3GPP TSG CN WG1

TO:	3GPP TSG SA WG2

Cc:	3GPP TSG SA WG1

Contact Person:

Name:	Lars Ekeroth, Ericsson Mobile Data Design AB

E-mail:	lars.ekeroth@erv.ericsson.se

Tel.: 	+46 31 703 6566

Date:	2000-03-02

___________________________________________________________________________

N1 wants to thank S2 for the Liaison statement concerning the change of title of 23.060 (Tdoc S2-000314).

N1 has in earlier meetings discussed and agreed on the terminology to be used within N1. The attached CR on TS 24.008 (N1-99D81) shows the terminology agreed. Changing the title of TS 23.060 is not in line with this.

N1 propose S2 not to change the title of TS 23.060 and instead consider adapting TS 23.060 to use the same terminology as agreed by N1.

| 3GPP/SMG Meeting TSG-CN WG1 | Document | N1-99D81 |
| --- | --- | --- |
| Bad Aibling, Germany, 30.11.-3.12.1999 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 24.008 | CR | 069 | Current Version: | 3.1.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | CN#9 | For approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME | X | UTRAN / Radio |  | Core Network | X |
| (at least one should be marked with an X) |
| Source: | Ericsson, Siemens, Nokia | Date: | 99-11-25 |
| Subject: | 24.008 Vocabulary |
| Work item: | GSM-UMTS Interworking |
| Category: | F Correction | X | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  |  | Release 00 |  |
| Reason for change: | TS 24.008 is based on GSM TS 04.08 and consequently the terminology has been defined for GSM and GPRS environment. For UMTS the common Core Network specification will need to cover the requirements of GSM, UMTS and GSM-UMTS multimode. If agreed the originators of this CR are volunteering to provide the CRs that are necessary to take these definitions to 24.008 CC, MM, SM and GMM sections. |
| Clauses affected: | Vocabulary |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

### 2.2.2	Vocabulary

The following terms are used in this Technical Specification:

-	idle mode: In this mode, the mobile station is not allocated any dedicated channel; it listens to the CCCH and the BCCH;

-	group receive mode: (only applicable for mobile stations supporting VGCS listening or VBS listening) In this mode, the mobile station is not allocated a dedicated channel with the network; it listens to the downlink of a voice broadcast channel or voice group call channel allocated to the cell. Occasionally, the mobile station has to listen to the BCCH of the serving cell as defined in TS 23.022 and 05.08;

-	dedicated mode: In this mode, the mobile station is allocated at least two dedicated channels, only one of them being a SACCH;

-	group transmit mode: (only applicable for mobile stations supporting VGCS talking) In this mode, one mobile station of a voice group call is allocated two dedicated channels, one of them being a SACCH. These channels can be allocated to one mobile station at a time but to different mobile stations during the voice group call;

-	packet idle mode: (only applicable for mobile stations supporting GPRS) In this mode, mobile station is not allocated any radio resource on a packet data physical channel; it listens to the PBCCH and PCCCH or, if those are not provided by the network, to the BCCH and the CCCH, see GSM 04.60.

-	packet transfer mode: (only applicable for mobile stations supporting GPRS) In this mode, the mobile station is allocated radio resource on one or more packet data physical channels for the transfer of LLC PDUs.

-	main DCCH: In Dedicated mode and group transmit mode, only two channels are used as DCCH, one being a SACCH, the other being a SDCCH or a FACCH; the SDCCH or FACCH is called here "the main DCCH";

-	A channel is activated if it can be used for transmission, in particular for signalling, at least with UI frames. On the SACCH, whenever activated, it must be ensured that a contiguous stream of layer 2 frames is sent;

-	A TCH is connected if circuit mode user data can be transferred. A TCH cannot be connected if it is not activated. A TCH which is activated but not connected is used only for signalling, i.e. as a DCCH;

-	The data link of SAPI 0 on the main DCCH is called the main signalling link. Any message specified to be sent on the main signalling link is sent in acknowledged mode except when otherwise specified;

-	The term "to establish" a link is a short form for "to establish the multiframe mode" on that data link. It is possible to send UI frames on a data link even if it is not established as soon as the corresponding channel is activated. Except when otherwise indicated, a data link layer establishment is done without an information field.

- “channel set” is used to identify TCHs that carry related user information flows, e.g., in a multislot configuration used to support circuit switched connection(s), which therefore need to

- be handled together.

-	A temporary block flow (TBF) is a physical connection used by the two RR peer entities to support the uni-directional transfer of LLC PDUs on packet data physical channels, see GSM 04.60.

-	RLC/MAC block: A RLC/MAC block is the protocol data unit exchanged between RLC/MAC entities, see GSM 04.60.

-	A GMM context is established when a GPRS attach procedure is successfully completed.

--	Network operation mode

The three different network operation modes I, II, and III are defined in TS 23.060 [74].

The network operation mode shall be indicated as system information. For proper operation, the network operation mode should be the same in each cell of one routing area.

--	GPRS MS operation mode

The three different GPRS MS operation modes A, B, and C are defined in TS 23.060 [74].

- Anonymous access refers to limited service provisioning to an MS whose identity is unknown in the network.

- RR connection: A RR connection is a dedicated physical circuit switched domain connection used by the two RR or RRC peer entities to support the upper layers' exchange of information flows.

- PS signalling connection is a peer to peer UMTS connection between MS and CN packet domain node.

- Inter-System change is a change of radio access between GSM and UMTS.

- GPRS: Packet Services for GSM and UMTS system.

- The label (GSM only) indicates this section or paragraph applies only to GSM system. For multi system case this is determined by the current serving radio access network.

- The label (UMTS only) indicates this section or paragraph applies only to UMTS system. For multi system case this is determined by the current serving radio access network.

- In GSM,... Indicates this paragraph applies only to GSM System. For multi system case this is determined by the current serving radio access network.

- In UMTS,... Indicates this paragraph applies only to UMTS System. For multi system case this is determined by the current serving radio access network.

- SIM, Subscriber Identity Module (see TS GSM 02.17). This specification makes no distinction between SIM and USIM.

- MS, Mobile Station. This specification makes no distinction between MS and UE.