| 3GPP SA1 | Document | S1-00236 |
| --- | --- | --- |
| Sophia Antipolis, France, 5-6 April 2000 |  | Agenda Item 6.2 |
| CHANGE REQUEST |  |
|  | 22.078 | CR | xxx | Current Version: | 3.3.0 |  |
| For submission to: |  | for approval | X |  | strategic |  |  |
|  | for information |  |  | non-strategic |  |  |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio |  | Core Network | x |
| Source: | Ericsson | Date: | 04/04/2000 |
| Subject: | Mobility Management triggers for CAMEL Phase 4 |
| Work item: | CAMEL Phase 4 |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
|  | B Addition of feature | X |  | Release 97 |  |
|  | C Functional modification of feature |  |  | Release 98 |  |
|  | D Editorial modification |  |  | Release 99 |  |
|  |  |  |  | Release 00 | X |
| Reason for change: | The present CR proposes to add the following Mobility Management triggers: Idle to Busy transition A notification shall be sent to the CSE if the Mobile Station makes a transition from the Idle state to the Busy state. Busy to Idle transition A notification shall be sent to the CSE if the Mobile Station makes a transition from the Busy state to the Idle state. The rationale of these additional mobility management triggers is explained in the ‘Reason for change’ of this CR. |
| Clauses affected: |  |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |

| Other comments: | There are two types of service applications that require notifications on Idle to Busy transition and Busy to Idle transition: “Notify when available” These types of services need to receive a notification when a subscriber is available, ie. the subscriber has made a transition from Busy to Idle. This information can be used by this service to trigger a set of actions when the subscriber has become available. “Show Status” These types of services need to receive all mobility management notifications from a subscriber, including notifications for Idle to Busy transition and Busy to Idle transition. These notifications are used by these types of services to present a status overview of the subscxribers of a PLMN. Underneath picture presents a graphical overview of above mentioned functionality. |
| --- | --- |

****First Modified Section ****

# 12	Notifications of non-traffic events to the CSE  $(CAMEL3$)

## 12.1	Mobility management $(CAMEL3$)

It shall be possible to mark for a subscriber that a notification shall be sent to the CSE when the VPLMN has completed the processing of any of the following mobility events:

- Location update to a different VLR service area;

- Location update within the same VLR service area;

- MS-initiated detach (MS switched off);

- Network initiated detach (periodic location update of MS failed);

- Attach of MS (MS switched on, successful location update after network initiated detach);

- Idle to Busy transition of the Mobile Station $(CAMEL4$)

- Busy to Idle transition of the Mobile Station $(CAMEL4$)

The notification shall contain the following information if available:

-	Event met;

- Service Key;

-	IMSI;

-	Basic MSISDN;

-	Location information;

-	LSA identity;

-	CAMEL phases supported at the VPLMN.

## 12.2	Notification to CSE of change of subscriber data $(CAMEL3$)

It shall be possible to mark for a subscriber that a notification shall be sent to the CSE when any of the following subscriber data are changed as a result of a request from any entity except the CSE to which the notification shall be sent:

-	CF SS data

-	CB SS data;

-	ODB data;

-	CAMEL subscription information

One ore more CSEs may be defined to which the notification shall be sent.

## 12.3	Supplementary service invocation notification to CSE $(CAMEL2$)

It shall be possible to mark for a subscriber that a notification shall be sent to the CSE when any of the following supplementary services are invoked:

-	ECT

-	CD

-	MPTY

-	CCBS - $(CAMEL3$)