TSG-SA Working Group 1 (Services) meeting #8	TSG S1 000355

Beijing, 10 - 14 April 2000	Agenda Item:

## Source: 	BT

## Title:	Delay Value for Voice Services in TS22.105

## Introduction

## In section 5.5 of TS 22.105, Supported End User QoS, The end to end delay values are specified as:

‘<150 msec preferred and <400 msec limit’

It should be noted that if a services is offered where the delay approaches this upper limit then the user perception of the service may be poor.

The maximum figure defined should only applied in the worst case namely that the call is mobile to mobile. In the case of mobile to fixed calls this figure should be halved to 200ms.

Proposal

A change request is submitted to clarify the meaning of the maximum delay by adding a note to the table.

| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- |
|  | 22.105 | CR |  | Current Version: | 3.8.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | SA#8 | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic | X | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio | X | Core Network | X |
| (at least one should be marked with an X) |
| Source: | BT | Date: | 13/4/00 |
| Subject: | Clarification of requirement in TS22.105 |
| Work item: |  |
| Category: | F Correction | X | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  |  | Release 00 | X |
| Reason for change: | Clarification of requirement by addition of explanatory note |
| Clauses affected: | 5.5 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

## Supported End User QoS

This section outlines the QoS that shall be provided to the end user / applications. This section defines QoS requirements from end to end. The values in the tables are end to end, including mobile to mobile calls and satellite components. Figure 2 below summarises the major groups of application in terms of QoS requirements. Applications and new applications may be applicable to one more groups.

# The following tables further elaborate UMTS end user / application QoS requirements.

### Table 1: End-user Performance Expectations - Conversational / Real-time Services

| Medium | Application | Degree of symmetry | Data rate | Key performance parameters and target values |
| --- | --- | --- | --- | --- |
|  |  |  |  | One-way Delay | Delay Variation | Information loss |
| Audio | Conversational voice | Two-way | 4-25 kb/s | <150 msec preferred <400 msec limit note 1 | < 1 msec | < 3% FER |
| Video | Videophone | Two-way | 32-384 kb/s | < 150 msec preferred <400 msec limit note 1 Lip-synch : < 100 msec |  | < 1% FER |
| Data | Telemetry - two-way control | Two-way | <28.8 kb/s | < 250 msec | N.A | Zero |
| Data | Interactive games | Two-way | < 1 KB | < 250 msec | N.A | Zero |
| Data | Telnet | Two-way (asymmetric) | < 1 KB | < 250 msec | N.A | Zero |

Note 1 	This maximum delay applies to the worst case namely for a mobile to mobile call. In the case of a mobile to fixed call the delay should be half this figure i.e. 200msec.