| 3GPP SA1 | Document | S1-000251 |
| --- | --- | --- |
| Sophia Antipolis, France, 5-6 April 2000 |  |  |
| CHANGE REQUEST |  |
|  | 22.078 | CR | xxx | Current Version: | 3.3.0 |  |
| For submission to: |  | for approval | X |  | strategic |  |  |
|  | for information |  |  | non-strategic |  |  |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio |  | Core Network | x |
| Source: | Ericsson | Date: | 05/04/2000 |
| Subject: | Correction to description of subscribed dialled services |
| Work item: | CAMEL Phase 3 |
| Category: | F Correction | x | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
|  | B Addition of feature |  |  | Release 97 |  |
|  | C Functional modification of feature |  |  | Release 98 |  |
|  | D Editorial modification |  |  | Release 99 | x |
|  |  |  |  | Release 00 |  |
| Reason for change: | Section 5.3.2.2 needs correction to correctly reflect the CSE capabilities for subscribed dialled services. The current wording may lead to confusion and/or misinterpretation. |
| Clauses affected: | 5.3.2.2 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

****First Modified Section ****

### 5.3.2	Procedure for subscribed dialled services $(CAMEL3$)

The purpose of this procedure is to detect a call set-up request at the point where the called party number has been compared with the dialled services information, and allow the CSE to modify the handling of the call set-up request. Triggering of this procedure shall happen immediately after the procedure when dialled digits have been collected.

#### 5.3.2.1	Initiation of contact with the CSE

If (according to the CSI):

-	the subscriber is provisioned with a CAMEL based originating service; and

-	the call set-up request occurs; and

-	the criteria are satisfied.

Then the VPLMN/IPLMN shall suspend call processing, make contact with the CSE and await further instructions.

Contact to the CSE shall (if necessary) be made in this manner before network dialled services are invoked.

For mobile originated calls the information listed in table: A-1 (Call set-up request procedure 3) shall be provided to the CSE if available.

For forwarded calls the information listed in table: A-1 (Call set-up request procedure 4) shall be provided to the CSE if available.

#### 5.3.2.2	Further processing of the call

When the VPLMN/IPLMN has made contact with the CSE, the CSE shall be able to instruct the VPLMN/IPLMN to act as described below:

-	perform charging activities 
The CSE is only allowed to send e-parameters (refer to sect. 15.1, ‘CSE controlled e-values’) and include free format data in Call Data Records (refer to sect. 15.2, ‘Inclusion in charging records of information received from the CSE’);

-	order in-band user interaction. (Interaction between the service triggered from previous triggering may be needed to avoid duplicated guidance etc.).

Once the CSE has concluded issuing the above instructions, it shall issue one and only one of the following instructions:

-	allow the call processing to continue unchanged;

-	allow the call processing with modified information. The CSE shall have the possibility to send the information listed in table: A-2 (Call set up request procedure 2);

-	release the call;