## Slide 1
DP on New miniWID on Integration of E-UTRA satellite access into 5G system
China Telecom
S1-253108 - 3GPP TSG-SA WG1 Meeting #111, 25-29 August 2025, Goteborg, Sweden
© 3GPP 2025

## Slide 2: Problem statement
As the IoT rapidly expands, it is becoming increasingly vital to bridge the gap between CIoT devices accessing the 5GC via E-UTRA satellite access to fully realize the potential of 5G technology.
From a technical perspective, the EPC is no longer evolving in 3GPP and lacks support for advanced 5G capabilities such as network slicing and edge computing. Furthermore, IoT deployments based on E-UTRA satellite access with EPC cannot seamlessly migrate to 5GC, constraining long-term scalability and evolution.
From a market perspective, deploying two separate core networks, i.e., the 5GC and EPC increases operator management complexity, raises both capital expenditures (CAPEX) and operating expenditures (OPEX), and limits the scope of service offerings such as satellite connectivity.

## Slide 3: Proposal
Existing work analysis:
  From the terminal’s perspective, R16 defined cellular IoT device already supports 5G NAS.
  From eNB’s perspective, there exists eNB evolved to ng-eNB accessing 5GC via NG interface.
  From 5GC’s perspective, the majority managements of NR NTN can be reused for IoT NTN.
Proposal:
The considered architecture is shown below:
The objective of this work is to specify the requirements for integrating E-UTRA satellite access into 5GC.

## Slide 4
Thank you