3GPP TSG SA WG1 Messaging SWG	Tdoc S1-021318

Rome, Italy,  8th – 12th, July, 2002

Source: 	dynamicsoft

Title: 	Messaging Filters

Agenda item:

Document for:	Discussion and decision

# 1.	Introduction

At the previous meeting in St Albans there was some discussion regarding filtering of messages and an editor’s note was added to clause 6.7 This contribution proposes to add an new message filtering clause containing the requirements for message filters to TR 22.940.

## 2.  Proposal

It is proposed to make the following changes to TR 22.940.

## 6.7	Message delivery requirements

Following requirements define the message delivery in IMS messaging. The requirements apply to all messaging types unless otherwise stated.

a)	Message delivery shall be immediate in immediate and group messaging i.e. messages are transported by the IMS system to the recipient's terminal (without notifications) subject to message filtering settings defined by the recipient or by the recipient's IMS service provider.

b)	Immediate and group messages shall not be stored by the network. If supported by the recipient's network as an application option immediate and group messages may be stored in the recipients network.

c)	It shall be possible for the sender to receive delivery acknowledgements (success/failure) for sent messages.

d)	It shall be possible for the recipient to request for message (and notification) screening subject to the capabilities of the network (e.g. automatically delete “junk mail”, anonymous messages without delivery to the recipient’s terminal). [These requirements should be incorporated to the filtering part]

## 6.8	User privacy requirements

Following requirements define user privacy in IMS messaging. These requirements apply to all messaging types.

a)	It shall be possible for the recipient to see the public ID of the sender of the message unless the sender has requested to hide it.

b)	It shall be possible for the sender of the message to request to hide its public ID from the recipient (anonymous sender). 
The sender's public ID shall not be delivered to the recipient. The capability of public ID hiding is an IMS service provider and legislation issue and it may or may not be available.

c)	It shall be possible for the sender to use nickname when sending messages.
In case of nickname the recipient shall only be able to see the nickname but not the real address from which the message came from. It shall be possible to use nicknames for public and private messages. It shall be possible for the recipient to reply to the message sent with a nickname.

## 6.10	Message Filtering

It shall be possible for a subscriber to set up filters in the network of the subscriber’s IMS service provider, in order to control the treatment of a message by the network when either an immediate or deferred message is received when the subscriber is either unavailable or when the subscriber does not currently want to receive messages. The filters shall also support the ability of the subscriber to specify the maximum size and type of message content etc that they are or are not willing to accept. The filters shall also support the ability of the subscriber to block (and unblock) messages from specific senders or anonymous senders.

Following specific requirements define the message filtering capabilities of the recipient.

a)	It shall be possible to define specific message treatment based on following criteria

i)	sender address (including anonymous senders);

ii)	message size;

iii)	message content type (e.g. video, audio, …)

message class (e.g. advertisement, private…);
Message subject

iv)	message priority;

v)	message content format (e.g. jpg, mpg);

vi)	message type e.g. notification, immediate message, deferred delivery message.

b) It shall be possible to specify the following message treatments in a filter:

- Reject the message with notification to sender
Reject the message without notification to sender.

- Store message content and notify recipient,

- Store message content for a specific time or until the recipient requests delivery.

- Push message content to recipient when available.

- Send the MSG to some other server that performs the advanced analysis…

The IMS service provider shall also be able to set and control the filter settings either on behalf of the subscriber or based on policy.