3GPP TSG-SA1 #41 	S1-082337

Sophia Antipolis, France, 21 - 25 July 2008

Title:	LS on HNB/HeNB Open Access Mode

Release:	Rel-9

Work Item:	EHNB

Source:	3GPP SA WG1

To:	RAN2

Cc:	CT1

Contact Person:

#### Name:	Ivan Ivanov, Michele Zarri

Tel. Number:	+44 7918 755051

E-mail Address:	Ivan Ivanov(at)samsung.com, Michele.Zarri(at)t-mobile.co.uk

Attachments:

1. Overall Description:

SA1 has discussed the notion of introducing an Open Access Mode of operation for HNB/HeNB in Release 9.

The following definitions and requirements were discussed.

Open Access Mode:  An HNB/HeNB where subscriber access is not limited to UEs that include the CSG identity of the HNB/HeNB in the CSG identities white list.

Closed Access Mode: Subscriber access is limited to UEs that include the CSG identity of the HNB/HeNB in the CSG identities white list.

Editors Note: The definition of Closed Access Mode need more clarified if it is used somewhere in the specification.

4.3.x Open Access Mode

The following requirements shall apply in the Open Access Mode:

- Subject to operator and registered owner agreement, the network operator shall be able to re-configure the HNB/HeNB to provide service to subscribers of any PLMN not belonging to the CSG subject to roaming agreement.

- It shall be possible for a UE to give priority to HNB/HeNB in open access mode.

Editors note: The above requirements needs to be checked against impacts from RAN2.

Before including these requirements into the TS22.220 (draft) SA1 would like to obtain clarifications on the following points:

- Is any negative impact on the UE to be expected in discovering the presence of a HNB/HeNB operating in Open Access Mode (e.g. on battery life)?

- Is there a need to modify the specifications in order to increase the “visibility” of CSG cells in Open Access Mode?

- Is there a need to modify the specifications in order to fulfil the requirement that the UE gives priority to the HNB/HeNB in Open Access Mode?

- Can the user be notified that the UE is under coverage of a CSG cell operating in Open Access Mode when such cell is part of a CSG present in the user’s white list?

2. Actions:

To RAN2 group.

ACTION: 	SA1asks RAN2 to provide clarification on this issue.

3. Date of Next TSG-SA WG1 Meetings:

SA1#42   	13 – 17 October 2008	Seoul, South Korea
SA1#42-bis	17 – 21 November 2008	North America