## Slide 1
Discussion on Long Range Cell Operation for Public Safety
Yi-Hsueh Tsai, lucas@iii.org.tw Hsuan-Li Lin, Tsung-Yu Tsai, Terng-Yin Hsu, Jian-Ya Chu
Shubhranshu shubhranshu@itri.org.tw Zheng Yan-Xiu zhengyanxiu@itri.org.tw
3GPP TSG-SA WG1 Meeting #66 S1-141008 Sapporo, Japan, 12-16 May 2014
Agenda Item 5.2 - New Study and Work Items (including related contributions)
Source: III, ITRI

## Slide 2: Tentative Time Scale
SA1 #66: Propose LCOPS work item
SA1 #66: Approved CRs for LCOPS
SP #64: Approved LCOPS work item
SA1 #67: Unresolved issues for LCOPS
SP #65: Release 13 Stage 1 Freeze
Time Line
SP
#62
SA1
#69
SA1
#64
SA1
#65
SA1
#66
SP
#64
Dec ‘13
June ‘14
SA1
#67
SA1
#68
SP
#65
Sep ‘14

## Slide 3: Long Range Cell Operation
Possible usage scenarios of Long Range Cell Operation (e.g. 10-100km [1][2][3])
Difficulty deployment territory
  In areas such as mountain areas, jungles, deserts, or islands, long range cell can provide broadband wireless access solution with good coverage under reasonable cost.
Disaster first responder (Public Safety)
  In major disaster, the ground based communication infrastructure may suffer a severe destruction. In such cases, long range cell could be quickly deployed to temporarily replace the ground communication infrastructure and fast recover the wireless networks to enable critical information access such as the communication for rescue mission, or emergency services.

## Slide 4: Example Scenario #1: LCOPS for ProSe
Partial Network Coverage Area: A network coverage area where UE can only listen to the eNB.
ProSe Communication
Oscar
Dashed line shows effective uplink coverage contour
eNB with limited backhaul such as satellite link
Infrastructure Communication
Roger
Peter
UE-to-network relay does not need to relay the downlink traffic in order to efficiently utilize the radio resource
UE outside the uplink coverage contour could receive synchronization signal, system information block, and semi-persistent resource management information for establishing ProSe communication
Partial network coverage area

## Slide 5: Example Scenario #2: LCOPS for GCSE
Oscar
Dashed line shows effective uplink coverage contour
eNB with limited backhaul such as satellite link
Infrastructure Communication
Roger
Peter
Partial network coverage area
Partial Network Coverage Area: A network coverage area where UE can only listen to the eNB.
UE outside the coverage contour could still listen to the message transmitted from long-rang base station and quickly join an ongoing group call
Oscar is talking
Smith

## Slide 6: Example Scenario #3: LCOPS for GCSE
Oscar
Dashed line shows effective uplink coverage contour
eNB with limited backhaul such as satellite link
Infrastructure Communication
Roger
Peter
Partial network coverage area
Partial Network Coverage Area: A network coverage area where UE can only listen to the eNB.
UE outside the coverage contour could still listen to the message transmitted from long-rang base station and quickly join an ongoing group call
Peter is talking
Smith
ProSe Communication
Oscar’s UE act as UE-to-network relay

## Slide 7: Example Scenario #4: LCOPS for GCSE
Oscar
Dashed line shows effective uplink coverage contour
eNB with limited backhaul such as satellite link
Infrastructure Communication
Roger
Partial network coverage area
Partial Network Coverage Area: A network coverage area where UE can only listen to the eNB.
Smith
Peter
Local routed the group-cast media transport via X2 interface between eNBs
macro eNB
Peter is talking

## Slide 8: Expected Output
Spec No. | CR | Subject | Approved at plenary# | Comments
22.278 | 0199 | Support Long Range Cell Operation for ProSe | SA#64 (June 2014) | S1-141010
22.468 | 0002 | Support Long Range Cell Operation for GCSE | SA#64 (June 2014) | S1-141012

## Slide 9: Proposed WID
S1-141013
Long Range Cell Operation for Public Safety (LCOPS)

## Slide 10: References
International Telecommunication Union (ITU), “Radio Communications for Emergency Response and Disaster Relief” (http://www.itu.int/ITU-D/asp/CMS/Events/2012/NBTC-disaster/S6_MrBhatia.pdf)
REV-090003-r1, “LTE-Advanced Physical Layer”
LTE The UMTS Long Term Evolution from Theory to Practice Ed2