## Slide 1: 5G system and LAN: Potential Architecture Realization
3GPP TSG-SA WG1 Meeting #79

## Slide 2: Motivation
Industrial control networks typically based on Ethernet fieldbuses, e.g., PROFINET
  Deployment and maintenance of cables is expensive
  Cabling may be a hazard with moving machinery
  Factory reconfiguration could be easier with wireless access
Desire for replacement of wired links with wireless
  Challenge 1: High performance requirements - low latency, high reliability, high redundancy, high determinism
  Challenge 2: Wireless system must interoperate with existing networks/end devices without any modification
    Example: PROFINET performs Ethernet frame routing at Data Link Layer instead of IP Layer
    Requires wireless system to interoperate with Ethernet Data Link Layer
Industrial technologies considered
  PROFINET: Ethernet based fieldbus, considered to be state-of-the-art today
  Time Sensitive Networking: IEEE standard to support industrial automation and automotive use cases requiring low latency and jitter, and high reliability.

## Slide 3: Existing System Architecture (topics for SA2)
High level model of user plane [1], [2] shown above
UPF is connected to DN through N6
  In [2], Point-to-point (PtP) tunneling based on UDP/IP encapsulation is defined for unstructured data
  Similar PtP tunneling can be defined for Ethernet PDU Session Type; UDP/IP tunnel between UPF and DN
  One-to-one mapping between an Ethernet PDU Session and a UDP/IP tunnel
Downlink processing
  DN sends the Ethernet frame over the appropriate UDP/IP tunnel
  UPF decapsulates the frame, and sends it over the appropriate Ethernet PDU Session
Uplink processing
  UE sends the Ethernet frame over an Ethernet PDU Session
  UPF receives the Ethernet frame and sends it over the appropriate UDP/IP tunnel
UE
UPF
DN
N6
gNB
[1] 3GPP TS 23.501, “System Architecture for the 5G System,” Release 15, 2017.
[2] 3GPP TS 29.061, “Interworking between the Public Land Mobile Network (PLMN) supporting packet based services and Packet Data Networks (PDN),” Release 14, 2017.

## Slide 4: Potential Architecture Realization (for SA2)
Ethernet Adapter (EA) connects UPF to an Ethernet device
  Encapsulates Ethernet frame into UDP/IP tunnel for DL traffic, and decapsulates for UL traffic
  EA is an edge node in the Data Network (DN)
An alternate approach would be to introduce a native Ethernet interface at UPF
UE supports an Ethernet interface
SA1 can define which Ethernet LAN features should be supported.
UPF
Ethernet Switch S
Ethernet Device C
Ethernet Device D
Ethernet
Ethernet Device A
Ethernet Device B
Ethernet Switch T
Ethernet Device E
UE 1
UE 2
gNB
Ethernet
Ethernet Adapter

## Slide 5: Architecture Realization: Topics for further study
How is an Ethernet frame be mapped to a UDP/IP tunnel?
How should an Ethernet broadcast frame be handled?
How should VLAN tags be handled?
Does the 5G system introduce loops in the LAN networks? How should that be resolved?
Choice of 5QI based on Ethernet headers – which entity performs this function? How is QoS configured in 5G system?
UPF
Ethernet Switch S
Ethernet Device C
Ethernet Device D
Ethernet
Ethernet Device A
Ethernet Device B
Ethernet Switch T
Ethernet Device E
UE 1
UE 2
gNB
Ethernet
Ethernet Adapter

## Slide 6: Backup

## Slide 7: VLAN Tagging and Ethertype
When a VLAN Tag is added to an Ethernet frame, the tag is inserted between the source MAC address and the Ethertype
  This results in more than one Ethertype being present in a frame
  We distinguish these as Outer and Inner Ethertype
Furthermore, frame can have multiple tags (e.g., double-tagged VLAN)
Preamble
Destination MAC address
Source MAC address
Ethertype
0xABCD
Payload
CRC
Preamble
Destination MAC address
Source MAC address
Ethertype
0xABCD
Payload
CRC
802.1Q Header
VLAN Ethertype
0x8100
PCP
DEI
VLAN ID
VLAN Tag addition
Original Ethernet frame
Tagged Ethernet frame
Outer Ethertype
Inner Ethertype

## Slide 8: Fieldbus Networking Model
Majority of fieldbuses operate according to a reduced three-layer networking model
  All fieldbuses defined in IEC 61158 use this model
Motivation for using fewer layers:
  Reduce delays associated with passing information between layers
  Reduce delays due processing at each layer
In the reduced model, network layer functionality such as routing can be implemented in either Data Link Layer or Application Layer
  Example: Ethernet Link Layer may perform routing in a LAN
Physical
Data Link
Network
Transport
Session
Presentation
Application
Physical
Data Link
Application
OSI Reference Model
Fieldbus Reference Model

## Slide 9: LAN Feature Requirements (PROFINET)
Requirement | Comment
Ethernet frame over 5G | Ethernet frame transport over 5G system
QoS for Ethernet flows | Standardized QoS identifiers to support industrial use cases Prioritization of real-time traffic
Learning bridge | Basic Layer 2 bridging functionality
Rapid Spanning Tree Protocol | 
Broadcast handling | 
IEEE 802.1AS | Precise time synchronization with 5G
IEEE 802.1Q | VLAN tags and prioritisation of data with VLAN tag priority 6
IEEE 802.1D | Auto-negotiation for 100 Mb/s link. Needed in case 5G device also has a standard LAN port.
LLDP (IEEE 802.1AB) | No forwarding of discovery messages
SNMP | MIB for PROFINET network diagnostics
MRP/MRPD | Use for higher availability in ring topologies; see IEC 61158

## Slide 10: LAN Feature Requirements (TSN)
Feature | IEEE Spec.
Time synchronization (gPTP) | 802.1AS
Distributed Stream Reservation Protocol 802.1Qcc has enhancements for SRP | 802.1Qat 802.1Qcc
Forwarding and Queuing Enhancements (FQTSS, CBS) | 802.1Qav
Enhanced Transmission Selection | 802.1Qaz
Priority Based Flow Control | 802.1Qbb
Time Aware Queuing | 802.1Qbv
Cyclic Queuing | P802.1Qch
Frame Preemption | 802.1Qbu
Input Gating | P802.1Qci
Seamless Redundancy | P802.1CB
Interspersing Express Traffic | 802.3br
TSN: Time Sensitive Networking