## Slide 1: 3GPP based Wireless Sensing Services
-Motivations, Use cases and Objectives
S1-214101
Revision of S1-213078
3GPP TSG-SA1 Meeting #96e Electronic Meeting, 08 November - 18 Nov 2021

## Slide 2: Traditional wireless sensing technology
Traditional wireless sensing technology, in which reflected radio wave from transmitter is used to detect the target objects information, such as shape, size, speed, location, air quality, etc., has been wildly applied in Radar, LiDAR, WiFi Sensing and so on.
Issues of the traditional wireless sensing technology
  Interference among devices using same spectrum
  Limitation of sensing range, i.e. distance and angles
  High Cost for dedicated components e.g., Radar/LiDAR device
  Operators can only provide connectivity for sensing data transmission from UE
  Overlay network for the communication among wireless sensing devices
  Dedicated system, separated from service applications
Transmitter/Receiver
Reflective Object

## Slide 3: 3GPP based wireless sensing service
3GPP based wireless sensing service, is aim to enable 3GPP system to detect the target information (e.g., shape, size, speed, location, air quality, etc.) of an object who doesn’t transmit signal, i.e., elements of 3GPP system acting as transmitter and receiver
Advantages:
  Minimized interference, due to spectrum/Resource management by 3GPP system
  Wide range sensing via the cellular network, complementary to Lidar, mmWave Radar and ToF camera by providing the sensing service in wider range
  Lower cost by reusing 3GPP RF module
  Native networking to enable communication among wireless sensing devices
  Easy exposure to service applications
  Potential new business opportunities for operators to
  deploy the sensing services

## Slide 4: Use cases (1): Auto driving
A UE on board car for motion detection, e.g.,
      Blind Spot Detection
      Collision Warning
      Automatic Distance Control

## Slide 5: Use cases (2): Smart Home and live
Sensing based AR/VR gaming, e.g.,
      Detecting players movement without any wearable device
Home devices controlled by gestures, e.g.,
      Switch on/off TV, switch channels
      Turn on/off, adjust lights
      Intruder detection

## Slide 6: Use case (3): Smart Transport & Dynamic 3D maps
The UEs on board car and the base stations can detect the sensing information of the surrounding cars, e.g. distance and velocity, to report to the traffic center for further processing, e.g. to build up the traffic map, to predict traffic, to enable traffic management, and to notify the cars
With the coordination of multiple UEs/gNBs to perform sensing on one and multiple objects, either static or dynamic, a dynamic 3D map can be built up based on the aggregated sensing information of the objects in a specific area or a city

## Slide 7: Definition and Roles
Definition
  Based on the request or subscription, a receiver is aware of the sensing information of the target object by receiving reflections of the signal sent from the transmitter.
Roles
  Reflective Object: the target object who’s information is sensed. It is out of scope of 3GPP.
  Transmitter: the device who transmits the radio signal to the target object. It can be either a UE or a gNB.
  Receiver: the device who detects sensing information based on the reflections of the radio signal from the target object. It can be either a UE or a gNB.
  Initiator: An authorized device which requests from or subscribes to one or multiple receivers for the sensing information. It can be either a UE or an NF. It is usually the device which collects the sensing information.
  Consumer: consuming the output calculated from sensing information, e.g., could be UE application, or Sensing application Server.
  Note: Transmitter, Receiver, Initiator and Consumer may be pairwise or all collocated together

## Slide 8: 3GPP Sensing Service Modes Examples
Mode 1: one UE as transmitter/Receiver
Sensing Signal
Reflected Signal
STx/SRx UE
RO
STx UE-1
SRx UE-2
RO
Sensing Signal
Reflected Signal
Mode 2: one UE as transmitter, another UE as Receiver
Mode 3: one gNB as transmitter and Receiver
STx gNB-1
SRx gNB-2
Sensing Signal
Reflected Signal
Mode 4: one gNB as transmitter, another gNB as Receiver
RO
Sensing Signal
Reflected Signal
STx/SRx gNB
RO
Mode 5: gNB as Transmitter, UE as Receiver
Sensing Signal
Reflected Signal
STx gNB
SRx UE
RO
Model 6: UE as Transmitter, gNB as Receiver
Sensing Signal
Reflected Signal
STx gNB
SRx UE
RO

## Slide 9: Information, methods and access technology
Sensing Information: e.g. Distance, Elevation Angle and Azimuth Angle, speed, motion, etc.
Sensing Methods
  TOF (Time of Flight): sensing information is derived by comparing the transmitting signal and the echo signal
  PAC (Path Attenuation Compensation): sensing information is derived by analysing the changing history of phase and amplitude of the received signal
Access Technology: 5G NR, WLAN

## Slide 10: Sensing data collection
  Sensing information can be derived at UE or network side，based on sensing data collected from multiple sources
Sensing information aggregation & processing at network
Sensing information aggregation & processing at UE

## Slide 11: Relationship with Stage 2 R18 proposal on sensing
Stage 2 R18 proposal “5G Architecture enhancements for Harmonized Communication and Sensing service” (S2-2107636)
  Only focusing on the support of specific use cases (e.g. UAV/UFO intrusion into the forbidden area, Occupy Emergency lane and Railway Intrusion Detection, etc.)
  Based on network based sensing over existing communication system and measurements
  no impact to UE
  no impact to RAN1/RAN2 work
  This R19 SID studies use cases, scenarios and service requirements without any restrictions, with the expectation of potential RAN, CN and UE enhancements.

## Slide 12: Objectives and requirements
The objective of this study item is to identify the use cases and potential requirements for 5GS support of enhanced services and communication utilizing sensing capabilities available in 5G devices and/or networks.. Aspects to be studied include:
identification of new use cases and enhanced sensing services
identification potential requirements pertaining to sensing and communication, including:
  discovery, authorization and provisioning/control of sensing service and entities involved in cooperative sensing
  Configuration of sensing related information to be collected and/or exchanged, e.g. about the object(s) to be detected, sensing availability, other sensing parameters
  Communication and sensing performance requirements, e.g.,
    Sensing distance, angle, motion, velocity, image resolution, frequency, latency, accuracy, energy efficiency,
    Communication requirements for transferring sensing information and/or enabling enhanced sensing services
Other aspects: security and privacy, charging, use of radio resources

## Slide 13: Objectives and requirements
The following scenarios and options should be considered:
5G-based wireless sensing and/or other type of sensors can be used (radar, lidar, ultrasound, cameras, motion sensors, etc.)
Sensing could be provided directly by the UE and/or gNB and/or other devices/entities;
Other sensors can be connected to the UE and/or network using 5G connectivity.