## Slide 1: Discussion paper of new SID on enhancing 5G system integrating with satellite
China Telecom, CATT
S1-214107

## Slide 2: Background
5G system over satellite is now very promising, e.g. there will be many satellites enable NG-RAN nodes in the space, and 5G networking based on inter-satellite link and satellite backhaul, etc.
TS22.261 has some requirements for satellite access and satellite backhaul in the 5G system. But some new use cases and requirements are required to discuss in REL 19.
Satellite Backhaul
Satellite Access

## Slide 3: New Use Case 1: Temporary networking
In some scenarios (such as scientific expeditions or disasters etc.) ，the end users are expected to only access local data center rapidly, e.g., to rapidly visit isolated resources or transfer some privacy data to local data center.
A small temporary 5G network is expected to be deployed locally by light satellite gateway (e.g., vehicle mounted satellite gateway, etc.), and a light 5G core network authorized by the operator.
  User authentication and authorization;
  Operational requirements on constructing a standalone 5G network
  Network configuration provision

## Slide 4: New Use Case 2: Navigation enhancement
During RAN#93E, Rel-18 NTN related topics has been discussed and the summary could be found in RP-211658. The moderator recommends starting the Rel-18 work with a study item to determine how the network can determine the UE location without relying on UE GNSS measurements or support.
The positioning requirements of commercial use cases where UE without/with GNSS using NTN access have not been discussed by RAN. Further, the requirements regarding high accuracy and low latency for positioning via NTN access have not been discussed, either.

## Slide 5: New Use Case 3: Integration with non-3GPP satellite access
It is not possible to deploy enough satellites to provide full 5G coverage over the earth for quite a long time, and there are already legacy satellite systems in the world which are non-3GPP systems, e.g., DVB, etc.
The 5G system integrating with NR satellite access should also consider to support non-3GPP satellite access to comprehensively use satellite resources and improve system performance, e.g., in the specific area or time period, the 5G system can offload the UE traffic from NR satellite access to non-3GPP satellite access.
  network selection
  routing policy
  Security related issue
Notes: Even though many satellite operators would like satellites to support 5G NR access, it is not possible to deploy eough satellites to provide full 5G coverage over the earth for quite a long time, especially considering there are already legacy satellite systems in the world which are non-3GPP systems, e.g., DVB, etc.
Therefore,

## Slide 6: New Use Case 4: Coordination with satellite system
Satellite access is used to serve kinds of users that have different requirements, e.g., on QoS, on security, etc., the 5G network shall be able to identify them, and satisfy their requirements accordingly
Since the user’s requirements is agnostic to the satellite operation center, the satellite operation center may not schedule enough satellite resources (e.g., satellite beams, network slicing) to serve users
It is expected to enhance the 5G system to interact with satellite system for provision of better network services.

## Slide 7: New Use Case 5: Deterministic transmission scenarios
The network with satellite access shall ensure the packet arrived at the target at the deterministic time, e.g., the time of stock market transactions is determined, so it is also necessary to transmit stock market transaction information through satellites within a determined time.
  time compensation considering dynamical latency over satellite

## Slide 8: objective
Studying use cases and requirements for new service and enhancement based on 5G system over satellite, including:
  Temporary networking usingsatellite access, such as scientific expeditions and disaster cases;
  commercial use cases and their requrirements for positioning UE not relying on GNSS, use cases for high accuracy and low latency for positioning via NTN access;
  UE accesses the 5G system through the different satellite system, e,g the DVB satellite system;
  Coordination with satellite system, such as the specific geographic area limitation etc.
  Deterministic transmission scenarios, e,g, packets arrive at the target at a specific time, etc.