## Slide 1: Motivation of supporting passive IoT
Alibaba
S1-220135

## Slide 2: Motivation of supporting Passive IoT
Nowadays, passive IoT with extremely low cost has been deployed in many use cases, such as Smart Logistics. However, existing solution has several issues listed below:
limited transmission range and interference caused by other passive IoT devices nearby;
Lack of well-defined networking infrastructure to support data transmission to a remote application server;
Integrating passive IoT into 5GS, typically non-public network, is an effective way to solve the aforementioned issues and bring more value to the 5GS.
The requirement of integrating passive IoT into NPN need to be investigated. Several aspects need to be studied. For example, the requirement of deployment using unlicensed band, registration/ authentication/ authorization management for passive IoT in NPN, etc.

## Slide 3: Motivation of supporting Passive IoT
There are several reasons for integrating passive IoT into NPN.
In some area for Logistics, there is no support of public network;
The service provider for Logistics may consider localized management and consider NPN as the local hosting network.

## Slide 4: Use case 1: Cargo warehousing registration
Passive RFID device
Passive RFID Relay
With the passive IoT device, the service provider of logistics wishes to build its own SNPN and to implement cargo warehousing registration within it own NPN. Different frequency band (e.g. unlisenced band) for different deployment scenarios can be applied.
In the case of cargo warehousing registration, there are tons of goods waiting for registration (more than 15,000 good per m2). A pallet is used for carrying good (each pallet for more than 150 goods) and each pallet passes through a scanning gun which can scan all the good on the pallet and complete the registration for these goods. The time interval for two neighboring pallet to pass through the scanning gun is usually short (less than 3min).
All the good can communicate directly with the scanning gun or send the data to the scanning gun through a passive RFID relay.
The efficiency of cargo warehousing registration will be increased dramatically.

## Slide 5: Use case 2: Cargo Tracking
A wagon carries many pallet with goods (more than 10 pallet per wagon) and travel to the destination. In order to track the goods within the wagon, several portal frames are set up among the route of the wagon. Whenever the wagon passes through the portal frame, the data of goods are required to be sent to the portal frame which can then forward the data to the proper application server for tracking.
The service provider of logistics may set up the tracking equipment on certain portal frame to track the data of the goods carried by wagons.
The efficiency for tracking the goods carried by wagon will be dramatically increased.
Active RFID Relay

## Slide 6: Thank you!