TITLE:	TR 22.976: Scope clarification to reflect phased approach

DATE:	29 February 2000

SOURCE:	Randolph Wohlert

Pacific Bell Wireless

Email address:		rwohlert@tri.sbc.com

Office Phone #:		+1 512 372 5838

Mobile Phone #:		+1 925 598 1224

FAX #:			+1 512 372 5891

The scope of 22.976 indicates "The All-IP network option will be developed in a phased approach.  The scope of the first phase of the All-IP network option (as part of 3GPP Release 2000) is described."

This is consistent with the general consensus of the 3GPP SA workshop held February 7-9, 2000 in Nice, France, where it was agreed standardization of the All IP Network Option would take place following a phased approach.  It was furthermore the consensus of that workshop that the first Phase would involve a hybrid network.  This contribution proposes restructuring the Scope section text, and adding additional text to clarify the phased approach.

1	Scope

This Technical Report provides background information, motivations, descriptions of service drivers, and concepts regarding general service requirements and service features of the All-IP network option. The All-IP network option will be developed in a phased approach.  The scope of the first phase of the All-IP network option (as part of 3GPP Release 2000) is described.  This TR provides the basis for the detailed Stage 1 specification work.

The focus of the TR is:

- High level vision

- Potential Service Drivers

- New service capabilities and end user benefits

- Case study of realisation of a some services e.g. CFU

- Evaluation of what does and does not need to be standardised

- Release roadmap

- Feature List

- Time of delivery expectations for standards and products (now indented)

- Division of responsibility between S1 and S2, dialogue between the two groups is required. There is a need to set expectations.

This TR has been created to ease the development of the All IP network option, and this document can be used to guide 3GPP in the creation of new specifications and CRs to existing specifications for the realisation of mobile communications services based on the Release 2000 specifications.

The All-IP network option will be developed in a phased approach.  The scope of the first phase of the All-IP network option (as part of 3GPP Release 2000) is described.  The following provides an overview of the scope of Phase 1.

All IP Network Option Phase 1

- Hybrid Architecture

- Smooth Network Evolution Path

- New Capabilities

- IP based call control

- Realtime (including Voice) services over IP with end-to-end QoS

- GERAN (support for EDGE radio in UTRAN)

- Services Provided Using Only Toolkits (CAMEL, MExE, SAT, VHE/OSA)

- Backwards Compatibility with Release 99 Features

- No degradation in QoS, Security, Authentication, Privacy

- Support for Inter-Domain Roaming and Handover