## Slide 1
Why we need TTFT in SA1 for 6G AI inference service
S1-254519
(was S1-254230r2)
3GPP TSG-SA WG1 Meeting #112
17-21 November 2025, Dallas, Texas, USA
Source: Huawei, HiSilicon, China Mobile
Draft TS/TR: 3GPP TR 22.870 v0.4.1
Agenda item: 8.1.3.2
Contact: Shuang ZHANG, zhang.shuang2 AT Huawei DOT com

## Slide 2
Definition[1][2]
Time to First Token (TTFT): The time a model takes to generate the first token after a request is sent. It reflects how fast the model can start responding, it includes the tokenization of input prompts and the model's initial computations(forward propagation) to generate the first output token.
Time per Output Token (TPOT): The average time interval between generating each subsequent tokens (excluding TTFT). A lower TPOT means the model can produce tokens faster, leading to higher throughput. For a single request, TPOT is equivalent to the average Inter-Token Latency (ITL)
[1] https://bentoml.com/llm/inference-optimization/llm-inference-metrics
[2] https://docs.nvidia.com/nim/benchmarking/llm/latest/metrics.html
ITL: Latency between successive token generations
TTFT: both the tokenization and de-tokenization steps for the first output token
joint E2E latency: the performance parameter for 6G AI Service when performing AI inference, comprised of round-trip communication latency (e.g. communication latency for UE transferring inference input to AI model in Service Hosting Environment, as well as the communication latency for transferring inference result from the AI model back to the UE), plus the AI inference latency (e.g. TTFT in some cases) inside the Service Hosting Environment.

## Slide 3
TTFT is a very important metric for LLM inference
Many AI applications demand low latency to enable timely feedback to user/UE input, which directly affects users' perception of a system's responsiveness. e.g., multimodal AI models (with inputs to the AI model including video, images, voice, and text).
On top of such responsiveness, many of these AI applications require input/output data transfer in streams (facilitated by bi-directional communication) to make the service interactive, smooth, and meaningful for the users.
One obvious category of use cases, (e.g. TR 22870 UC 6.49): In the context of embodied AI interacting with the real world, two key characteristics underscore the critical role of TTFT in user experience:
  The output is structured, such that a single output token functions as an executable action unit. The robot can act once the first token has been generated.
  Certain VLA models (e.g.π0) inherently only take one forward propagation per inference cycle. In such cases, the inference latency contributing to the joint E2E delay is equivalent to TTFT.
Differently, other types of use cases utilize streaming responses (involving TTFT, TPOT), the joint E2E latency will additionally consider TPOT contribution. However, TTFT is still especially critical for the following reasons.
  TTFT reflects the time for the system's first response, i.e., the system's response time.
  It is typically much more computationally intensive and longer to generate the first token than the subsequent ones. TTFT reflects the system's computationally intensive time, and thus the computational capacity.
Prompt
Large AI model in SHE
UE
E2E RTT (TTFT)
Queue + Inference time
TPOT(time per output token)
First packet
Token
Token
Speech: What is he doing?
Video/Image:
Per packet
Token
Token
First Token
Buffer
Receive all packet
joint E2E latency (when inference latency==TTFT): UL transmission delay + TTFT + DL transmission delay, we can treat the E2E TTFT as Initial Response Time by assuming that the system could response with one token
joint E2E latency (in case TPOT applies): UL transmission delay + TTFT + TPOT*（M-1） + DL transmission delay, where M is the number of total generated tokens
Example
e.g. continuous input (e.g. video streaming); output (e.g. timely, recurring statement/update of the subject’s observed actions)

## Slide 4
Two different cases related to “joint E2E latency”?
Item | joint E2E latency (in case of TTFT only) | joint E2E latency (in case TPOT applies)
Ability to reflect user experience | Reflects the first response generated by AI models | Reflects the total responses generated by AI models. Joint E2E latency = TTFT + N × TPOT
Composition | UL latency + model prefill time + first token DL latency | UL latency + model prefill time + first token DL latency + decoding time + subsequent tokens' DL latency
Parallelism | No parallelism available; the above steps are executed serially | Multiple parallelism options exist, such that actual end-to-end latency is significantly affected by parallel configurations (e.g., parallelism between decoding and subsequent tokens' DL). Eg. the parallelism configs in UC 6.26
Factors | Transmission capability and computational capability (including concurrent conflicts) | Output token quantity; Parallelization setups; Transmission capability and computational capability (including concurrent conflicts)
Order of magnitude | ~hundreds of ms | If N~1000, the joint E2E latency can be on the order of seconds
P.S.
joint E2E latency (in case TPOT applies) depends far more on the application’s output configuration than on computational capability. UE can easily adjust it by modifying the number of output tokens per step (N), and this adjustment will mask the effectiveness of network optimization efforts aimed at improving KPIs.
GPT4o
UE
GPT4o
UE
Decoding time > Transmission time
Decoding time < Transmission time

## Slide 5
Sources:
[1] https://www.physicalintelligence.company/research/real_time_chunking
[2] https://humanbenchmark.com/tests/reactiontime
UC 6.49: In the context of embodied AI interacting with the real world, two key characteristics underscore the critical role of TTFT in user experience:
1. The output is structured, such that a single output token functions as an executable action unit. The robot can act once the first token has been generated.
2. Certain VLA models—such as π0—inherently only take one forward propagation per inference cycle.
According to Physical intelligence, the Reaction delay requirement for sport scenes is 200-300nms, similar scenario of the clothes-folding by openAI Pi0 model requires a of joint E2E latency (in case of TTFT only) for successful task completion is approximately 200ms[1]
Human reaction
Explain TTFT in two UCs
For other cases such as UC 6.26 or other models(eg RT-2) for UC 6.49, we need TTFT because：
joint E2E latency(in case of TTFT only) is more robust and directly related to the system's transmission and computational capabilities.
P.S.
Many GenAI applications produce output typically intended for humans to read (or listen to, in the case of voice output), the GenAI models generate large amounts of tokens.
Human beings have limited reading speed, so it is not reasonable to output all tokens only after all are generated. The average human reaction latency is approximately 200ms[2].

## Slide 6
Proposals
Proposal 1: Introduce the definition of joint E2E latency, being round-trip communication latency, and AI inference time (e.g. TTFT in some cases) in Service Hosting Environment).
Proposal 2: consider to extend the captured performance requirement of joint E2E latency with TTFT. E.g., for KPIs in UC 6.49 (joint E2E latency being less than 200ms to meet the requirement of basic human brain reaction time), the AI inference contribution to the joint E2E latency is TTFT.