## Slide 1: SA 1 input for joint SA 1+4 session
5/2/2016
Fukuoka, Japan
S1-180223

## Slide 2: SA 1 discussion topics
Review of 5G multimedia related KPIs in TS 22.261
Bandwidth and bandwidth classification of 5G media
SA 4 review of S1-180293 and S1-180294 (clarifications of video related V2X use cases)

## Slide 3: TS 22.261 multimedia KPIs 1/5
Clause 6.13.2 (multimedia broadcast)
  The 5G system shall support operation of a downlink only broadcast/multicast system over a wide geographic area in a spectrally efficient manner for stationary and mobile UEs.
  The 5G system shall be able to support broadcast/multicast of UHD streaming video (e.g., 4K/8K UHD).
    NOTE: Taking into account the bandwidth needs for different streaming video resolution.
  The 5G network shall allow the operator to configure and broadcast multiple quality levels (i.e., video resolutions) of broadcast/multicast content for the same user service in a stand-alone 3GPP based broadcast/multicast system.
  The 5G network shall support parallel transfer of multiple quality levels (i.e., video resolutions) of broadcast/multicast content for the same user service to the same UE taking into account e.g., UE capability, radio characteristics, application information.

## Slide 4: TS 22.261 multimedia KPIs 2/5
Clause 6.17.2 (voice latency for long range coverage)
  The 5G system shall support the extreme long range coverage (up to 100 km) in low density areas (up to 2 user/km2).
  The 5G system shall support a minimum user throughput of 1 Mbps on DL and 100 kbps on UL at the edge of coverage.
  The 5G system shall support a minimum cell throughput capacity of 10 Mbps/cell on DL (based on an assumption of 1 GB/month/sub).
  The 5G system shall support a maximum of [400] ms E2E latency for voice services at the edge of coverage.

## Slide 5: TS 22.261 multimedia KPIs 3/5
Table 7.1-1 (high data rate and traffic density scenarios)
 | Scenario | Experienced data rate (DL) | Experienced data rate (UL) | Area traffic capacity (DL) | Area traffic capacity (UL) | Overall user density | Activity factor | UE speed | Coverage
1 | Urban macro | 50 Mbps | 25 Mbps | 100 Gbps/km2 (note 4) | 50 Gbps/km2 (note 4) | 10 000/km2 | 20% | Pedestrians and users in vehicles (up to 120 km/h | Full network (note 1)
2 | Rural macro | 50 Mbps | 25 Mbps | 1 Gbps/km2 (note 4) | 500 Mbps/km2 (note 4) | 100/km2 | 20% | Pedestrians and users in vehicles (up to 120 km/h | Full network (note 1)
3 | Indoor hotspot | 1 Gbps | 500 Mbps | 15 Tbps/km2 | 2 Tbps/km2 | 250 000/km2 | note 2 | Pedestrians | Office and residential (note 2) (note 3)
4 | Broadband access in a crowd | 25 Mbps | 50 Mbps | [3,75] Tbps/km2 | [7,5] Tbps/km2 | [500 000]/km2 | 30% | Pedestrians | Confined area
5 | Dense urban | 300 Mbps | 50 Mbps | 750 Gbps/km2 (note 4) | 125 Gbps/km2 (note 4) | 25 000/km2 | 10% | Pedestrians and users in vehicles (up to 60 km/h) | Downtown (note 1)
6 | Broadcast-like services | Maximum 200 Mbps (per TV channel) | N/A or modest (e.g., 500 kbps per user) | N/A | N/A | [15] TV channels of [20 Mbps] on one carrier | N/A | Stationary users, pedestrians and users in vehicles (up to 500 km/h) | Full network (note 1)
7 | High-speed train | 50 Mbps | 25 Mbps | 15 Gbps/train | 7,5 Gbps/train | 1 000/train | 30% | Users in trains (up to 500 km/h) | Along railways (note 1)
8 | High-speed vehicle | 50 Mbps | 25 Mbps | [100] Gbps/km2 | [50] Gbps/km2 | 4 000/km2 | 50% | Users in vehicles (up to 250 km/h) | Along roads (note 1)
9 | Airplanes connectivity | 15 Mbps | 7,5 Mbps | 1,2 Gbps/plane | 600 Mbps/plane | 400/plane | 20% | Users in airplanes (up to 1 000 km/h) | (note 1)
NOTE 1: For users in vehicles, the UE can be connected to the network directly, or via an on-board moving base station. NOTE 2: A certain traffic mix is assumed; only some users use services that require the highest data rates [2]. NOTE 3: For interactive audio and video services, for example, virtual meetings, the required two-way end-to-end latency (UL and DL) is 2‑4 ms while the corresponding experienced data rate needs to be up to 8K 3D video [300 Mbps] in uplink and downlink. NOTE 4: These values are derived based on overall user density. Detailed information can be found in [10]. NOTE 5: All the values in this table are targeted values and not strict requirements. |  |  |  |  |  |  |  |  | 

## Slide 6: TS 22.261 multimedia KPIs 4/5
Clause 7.2.3 (VR, interactive voice)
  To support VR environments with low motion-to-photon capabilities, the 5G system shall support:
    motion-to-photon latency in the range of 7-15ms while maintaining the required user data rate of [1Gbps] and
    motion-to-sound delay of [<20ms].
  To support interactive task completion during voice conversations the 5G system shall support low-delay speech coding for interactive conversational services (100 ms, one way mouth-to-ear).
  To support VR environments the 5G system shall support audio-video synchronisation thresholds:
    in the range of [125ms-5ms] for audio delayed and
    in the range of [45ms-5ms] for audio advanced.

## Slide 7: TS 22.261 multimedia KPIs 5/5
Annex A, table A.1-1 (latency needs from example vertical use cases)
Services/ Use cases | Automotive use cases | Transport, logistics, IoT use cases | Health and wellness, smart cities use cases | Media and entertainment
Description | Expand detectable range beyond on board sensor capability by sharing views or detected objects among traffic participants, coordinate trajectories among vehicles, sharing coarse driving intention, real-time remote operation of vehicles | Real-time sensing, reporting, feedback, control, remote, asset tracking, monitoring; context-aware services, recommendations at shopping mall, airport | Live video feed (4K, 8K, 3D for remote healthcare (consultation, monitoring) and assisted surgery, real-time commands to control medical devices for treatment (e.g., medication, surgery); remote monitoring, surveillance and guidance for citizens and law enforcement officers. | Media production services based on aggregation of various media feeds at servers; real-time peer-to-peer or server-client sharing of data (object information) for collaborative gaming, live streaming at live events
Latency | For mid/long-term environment modelling (dynamic high-definition digital map update): Not critical (100 ms end-to-end) For short term environment modelling (sensor sharing): <20 ms end-to-end For cooperation (coordinated control): - <3 ms end-to-end for platooning , - <10 ms end-to-end for cooperative manoeuvres . - <100 ms end-to-end for coarse driving intention For remote vehicle operation: 10-30 ms end-to-end | For massive connectivity for time-critical sensing and feedback: <30 ms end–to-end. For remote drone operation and cooperative farm machinery: 10-30 ms end-to-end Real-time control for discrete automation: ≤1 ms end-to-end | For real-time video/ telepresence/augmented reality for remote healthcare and assisted surgery, for monitoring and guidance (smart cities): 100 ms end-to-end Real-time command and control for remote medication and surgery: 10-100 ms end-to-end For smart grid: - <5 ms end-to-end for transmission/grid backbone, - <50 ms end-to-end for distribution/grid backhaul, Time-critical sensing and feedback for smart cities: 30 ms end-to-end | For live streaming in crowded areas, services for media production, augmented reality for collaborative gaming etc.: 20 ms end–to-end

## Slide 8: Specific media bandwidth
SA 1 is looking for guidance on the bandwidth on the following media types and how they might fit into bandwidth categories such as low, medium, high, very high, ultra high:
720p video @ 30fps
1080p video @ 30fps
4k video @ 30fps
8k video @ 30fps
Basic 360 VR
HD 360 VR
Retinal VR
AR UL/DL
Narrowband voice
Wideband voice
Super-wideband voice
Normal quality audio
High quality audio
Extreme quality audio
Are there others SA 1 should consider or be aware of?
<Eddy>