## Slide 1: Questions REFEC
S1-190455
(revision of S1-19xxxx)

## Slide 2: Authorization UEs/ User permission
The 5G system shall support the relaying of traffic between remote UEs and a gNB using a chain of UEs which have the capability of doing so.
Editor’s Note: clarify ‘which have the capability of doing so’ e.g., would use of the correct term, UE-UE relay, indicate the capability?
The 5G system shall enable the MNO to authorize UEs to be relayed by a chain of UEs.
The 5G system shall enable the MNO to authorize UEs to relay traffic in a chain of UEs to / from other UEs.
Editor’s note: Clarification is needed on the above 2 requirements – does this authorization apply for relaying traffic for UEs belonging to the same MNO or different MNOs?
The 5G system shall support a mechanism to verify that the user of a UE has given permission to its being used as a relay in a relay chain.
Editor’s note: clarification is needed – is this verification expected at the time of being requested to relay? Would this be a subscribed capability?

## Slide 3: Authorization UEs/ User permission
“Gap analysis”: No reference so ever in TS 22.278 7B Indirect 3GPP Communication or TS 22.261 6.9 Connectivity models about User permission
About network authorization:
A UE shall be capable of acting as an Evolved ProSe UE-to-Network Relay between an Evolved ProSe Remote UE and E-UTRAN if it is authorised by the3GPP network to act as a relay and served by this E-UTRAN.
An authorised Evolved ProSe UE-to-Network Relay shall be capable of being enabled/disabled by the 3GPP network to act as a relay to/from E-UTRAN for other Evolved ProSe Remote UEs unable to access E-UTRAN.

## Slide 4: Answers [Authorization UEs/ User permission]
First requirement will be moved to Relay Selection. And split in two: one part capability and one part selection.
The 5G system shall support the relaying of traffic between remote UEs and a gNB using a chain of UEs.
Editor note: we need to have something on selection.
The following requirement will be rephrase to talk about ”UE consent” or similar in to include multi-hop relay, taking into account scenarios like smart factories, public safety scenarios.
The 5G system shall support a mechanism to verify that the user of a UE has given permission to its being used as a relay in a relay chain.

## Slide 5: Answers 2
Rewrite the requirements:
The 5G system shall enable the MNO to authorize UEs to be relayed by a chain of UEs belonging or not to the same MNO
The 5G system shall enable the MNO to authorize UEs to relay traffic in a chain of UEs to / from other UEs. belonging or not to the same MNO.
Authorization may take into account use cases where authorization can be done in advance.

## Slide 6: Relay Selection
Relay selection
The 5G system shall support the relaying of UE traffic through a chain of UEs which can support its intended traffic characteristics.
Editor’s note: clarification is needed – is some additional information/process needed for a UE to find a relay UE with necessary traffic support?
“Gap analysis”: TS TS 22.278 7C Relay UE Selection
The 3GPP system shall support selection of an Evolved ProSe UE-to-Network Relay based on a combination of different criteria e.g.,
  - the subcriptions of Evolved ProSe UE-to-Network Relay and Evolved ProSe Remote UE,
  - the capabilities of the Evolved ProSe UE-to-Network Relay,
  - the QoS that is achieveable by selecting the Evolved ProSe UE-to-Network Relay,
  - the power consumption required by Evolved ProSe UE-to-Network Relay UE and Evolved ProSe Remote UE,
  - the pre-paired Evolved ProSse UE-to-Network Relay,
  - the 3GPP or non-3GPP access the Evolved ProSe UE-to-Network Relay uses to connect to the network, or
  - the 3GPP PLMN the Evolved ProSe UE-to-Network Relay connects to.
  Note: Other criteria can play a role in selection of an Evolved ProSe UE-to-Network Relay.

## Slide 7: Answers
We will use the list of different criteria for relay selection and see if it needs to be extended for the multi-hop scenario.

## Slide 8: Service continuity
Service
The 5G system shall maintain service continuity when remote UE traffic is relayed through a different chain of relays than the original.
Editor’s note: clarification is needed – does this imply the entire chain of relay’s changes or 1 or more relay UEs change?
The 5G system shall maintain service continuity when remote UE traffic is relayed to a different gNB.
Editor’s Note: The last requirement refers to the handover of the last relay in a chain of UE relays to a different gNB and may require further clarification.
New proposal [Interdigital’s Contribution] - edited
The 5G system shall maintain service continuity when remote UE moves from direct network connection to indirect network connection through a chain of relays and vice-versa.
The 5G system shall maintain service continuity for a remote UE when the communication path to the network changes (e.g. change of one or more relay of UEs, change of the gNodeB).

## Slide 9: Service continuity
“Gap analysis”: TS TS 22.278 7B2 General Requirements for Indirect 3GPP Communication
The 3GPP network shall be able to ensure service continuity when the Evolved ProSe Remote UE changes from a direct 3GPP communication to an Indirect 3GPP Communication and vice-versa.
Answers Service continuity:
The Service Coninuity requirements have been rewritten in the previous slide.

## Slide 10: Exposure
The 5G system shall provide a suitable API by which an authorized 3’rd party shall be able to provide the network with permission information of UEs.
Editor’s note: clarification is needed – what permission information? Of any/all UEs? Of UEs associated to the 3rd party? Is this permission provided in real time – implying based on a request or provisioned?
The 5G system shall provide a suitable API by which an authorized 3’rd party shall be able to receive from the network information regarding the accessibility of UEs.
Editor’s note: clarification is needed – what does ‘accessibility’ pertain to? Of any/all UEs? Of UEs associated to the 3rd party?

## Slide 11: Answers
If we have a requirement for “UE consent”, the first requirement is already covered and it can be deleted.
Second requirement needs more off-line discussion. The API already exists and it is supported by 3GPP system.