## Slide 1: Motivation of new WID on 5G system with High Altitude Platform Station (HAPS)
3GPP TSG-SA1 Meeting #94e
Electronic Meeting, 10 - 20 May 2021
S1-211299
Source：China Unicom

## Slide 2: Justification
Background
  HAPS is expected to deployed in remote / wide area to provide high data rate and IOT services.

## Slide 3: Justification
Background
  China Unicom deployed a field trial in the altitude of 1km in 2020
  Configurations
    Altitude：1km （because of the limitation of aircrafts and the instability of feeder link, 3km is tried but the data are not included in statistics）
    Frequency band： 20MHz@2.1GHz， 100MHz@3.5GHz
 | 2.1GHz | 3.5GHz
Work mode | FDD | TDD DDDSU/DDSUU
GP | - | 10:2:2 /8:4:2(for long distance)
Antenna | 4T 4R | 64T64R
Output Power | 320W | 200W
Antenna gain |  | 25dBi
5GC
Network Management System

## Slide 4: Justification
Background
  Road test & fixed test
 | 3.5GHz |  | 2.1GHz | 
 | Distance | throughput | Distance | throughput
UL | 11km | 20Mbps | 11km | 50Mbps
DL | 11km | >120Mbps | 11km | 100Mbps
  There are terrestrial gNBs deployed at a distance of 8km. The city is about 11-12km far from the HAPS.
  According to the trial, the Rel-15 NR can work in HAPS scenarios but the performance is not stable and there are some issues need to be enhanced.

## Slide 5: Justification
Interference from the terrestrial network has an impact on the performance for the UEs
  Adjacent channel interference
    It is under study in the existing NTN WI in RAN.
  Co-channel interference
    Lower Frequency band, especially below 3GHz is valuable for MNOs.
    3GPP should evaluate the interference and verify the applicability of existing Rel-16 DC or HetNet interference cancelation techniques to solve this interference and develop enhancements if needed
    As shown in Figure 4, when the UE got into suburban area where terrestrial gNBs were deployed, the RSRP was relative similar but the PDCP data rate decreased quickly.

## Slide 6: Justification
  Unstable gNB antenna surface cause inaccurate beam measurement
  The HAPS gNB antenna surface is not stable in the stratosphere and may jerk up and down by 1° even the stabilizing device is already deployed at the HAPS in the trial in the altitude of 1km.
  The outer beam may depart the original direction by kms, which may cause inaccurate beam measurement and then unnecessary handover between beams in one HAPS/between HAPS/ between HAPS and TN or cause beam failure.
Vertical Azimuth Angle
Horizon Azimuth Angle
Vertical Azimuth Angle
Horizon Azimuth Angle

## Slide 7: Justification
handheld UE can access in the HAPS directly but the margin is small and it is easily influenced by clutter loss and topography
  3GPP need to define the HAPS gNB based the TN macro gNB with as few necessary enhancements as possible to access legacy UE and possible new UE.
  Necessary performance optimization for UE to support the link budget.
  The HAPS gNB will move in the stratosphere in a relative small area, which will cause new neighbor cell issues with terrestrial networks.
  Verify the applicability of existing Rel-16 ANR techniques to solve PCI confusion in order to support co-channel operation between HAPS & terrestrial networks and develop enhancements if needed [RAN2/3]. This is considered with 2nd priority in the existing NTN WI in RAN. But it is very important for HAPS.

## Slide 8: Justification
Requirements to proposed in R18
  Clear commercial demand to deploy HAPS in remote/wide area for high data rate and IoT services.
  The NTN work in Rel -17 are focus on the transparent mode and adjacent-channel scenarios, but as for the MNOs, regenerative mode and co-channel scenarios are rather important, it is not included in the Rel-17 work.
  The Rel-18 RAN work is going to start in H1 2022 and will complete in H2 2023 or H1 2024. It is time to define HAPS in Rel-18.
  China Unicom is planning to launch a trial in high altitude (target 20km) in the end 2021 or H1 2022. More scenarios to fulfil the requirements we proposed will be test in the future trial, and China Unicom will also proposed HAPS SI/WI in the RAN R18 to study and try to solve the issues found in the field trail.

## Slide 9: Objectives
Specify differentiate KPI for 5G system with HAPS in SA1
  Include the KPI requirements into the TS 22.261 as a new clause 7.X, including delay, coverage and performance requirements in different scenarios.