## Slide 1
S1-221073, 3GPP TSG SA1#98e, 9 - 19 May 2022, e-meeting
China Mobile
Motivation of Study on Service Enhancements of Energy Efficiency

## Slide 2: Motivation and typical scenarios
In 2022 MWC, It’s requested that 5G should help in building up sustainable development of green city.
There’s gap in generating systematic requirements for better service-level energy efficiency
In 3GPP, there are existing study of EE in SA, SA5 which concentrate in different domains, and the ongoing studies in RAN, SA5 could be further utilized in this study.
Motivation
Main goals
Introduce energy efficiency as a service for customers
Provide systematic energy efficient network approach
Notes: Our earth is facing a very critical time in controlling the carbon releasing. Carbon green and carbon neutral are very heat concepts which were raised these days. In the European Green Deal, it states that Europe is “Striving to be the first climate-neutral continent”, and China has also set the goal of reaching emission peak in 2030 and achieving carbon neutral in 2060. So carbon-neutral is the shared goal of global, and we also need to consider the carbon emission in communication field.

## Slide 3
Introducing energy efficiency as a service
Users can have the choice to select proper energy efficiency criteria as well as other network performance when they need.
Which may include:
  Introduce service-level energy efficiency as a SLA dimension.
  Provide information exposure on systematic energy consumption/ level of energy efficiency to vertical customers who needs E2E energy efficiency.
  Use energy consumption statue of UE/application as a initiation in network modification for less resource consumption.
5G System
EE SLA
EE exposure

## Slide 4
Use case 1: satellite and terrestrial integrated cover
  5G-Advanced network consider involve satellite. RAN, 5GC NF, Application can be deployed in ground or satellite. In critical area, network may access via satellite only. In some area, UE can access network via both RAN in ground and satellite.
    Consider service level energy efficiency as a dimension in routing selection. Especially in long distance communication, multi-hop routing will lead to energy consumption.
    GEO launch cost is high. Energy in GEO is not limited. While LEO launch has low cost, low latency, small size and energy limited.
      System level energy efficiency needs to be consider in low-orbit satellite scenario, with the limitation of total energy consumption of RAN or 5GC NF on satellite, achieve the balance of user experience and connect number.

## Slide 5
Use case 2：signal application performance adjustment in low battery situation
When UE is in low battery, and is using only one high battery consumption application which requires for high picture quality, high frequency frame rate and abundant background sounds, terminal can provides the information of low battery to 5GC. 5GC may:
Provide information to application to adjust amount of data (e.g. lower picture quality, slower frequency frame rate, reduce unnecessary background sounds). In this way, terminal is available to complete the game this time based on the current battery.
Adjust network resource to provide lower QoS level. Ensure application service for current battery and energy saving for 5G system.
DN
App

## Slide 6
Use case 3：multi-application performance adjustment in low battery situation
5G Core
DN
App
App
UE is in low battery, and is using multi applications. In this situation, UE do not need to be guaranteed to high level QoS in every application. As we can see, in the figure above, the video application is in a little window which do not need to transport high picture quality, high frequency frame rate and abundant background sounds. In such situation, terminal provides the information of low battery to 5GC. 5GC may:
Choose one or several application which requires for higher network performance guarantee based on user habit analysis which can be performed by NWDAF.
  Keep QoS for those who requires for higher network performance guarantee.
  Adjust network resource to provide lower QoS level for those who can be adjust to lower QoS.
  Provide information to lower priority QoS guarantee application to adjust amount of data (e.g. lower picture quality, slower frequency frame rate, reduce unnecessary background sounds).
  In the whole operator’s network, there will be a fixed proportion of low battery users. This leads to a fixed proportion of network resource consumption decrease.

## Slide 7: Objectives:
The objectives include:
  Support energy efficiency in 5G through new approaches to delivering services (e.g. adding energy efficiency as a selection criteria).
  Support energy consumption framework to optimally use different communication capabilities of the 5G system taking into account energy consumption along with efficiency, latency, and data rate.
  Interaction between network and application on UE/application energy consumption statues for network condition modification.
  Note: There’s no implication on 3GPP will provide energy efficiency as a trade-off to service quality.
Other aspects include security, charging and privacy.

## Slide 8
Thank you!