TSG-SA Working Group 2 (Architecture ) meeting #5	TSGS2#5(99)413

25 - 28 May1999

Sophia Antipolis

To:	TSG CN 1

Source:	TSG S2

Title:			Draft LS on  the requirements of multimedia call control

²

Document for:	Information and action

___________________________________________________________________________

TSG-SA WG2 during its #5 meeting has worked on requirements of multimedia call control. This corresponds to agreed Tdoc S2-9939. These principles are:

P1) GSM/UMTS shall enable the provisioning of multimedia services and multivendor interworking between UE and network.

P2) Basic voice and PDP-context establishment shall be based on GSM CC/SM respectively.

P3) Handover and roaming to and from GSM shall be supported provided GSM is capable of supporting the ongoing media service.

P4) Ideas, concepts and procedures developed by other fora e.g. other standards bodies such as ITU, IETF etc. shall be included or referenced in GSM/UMTS when found suitable.

P5) To ensure multi-vendor inter-working and UE roaming, a single standardised multimedia protocol for CS domain and a single standardised multimedia protocol for PS domain shall be  selected for GSM / UMTS R99. This does not preclude the selection of other protocols by UMTS in the future.

P6) For multimedia services the standardized multimedia protocol shall be run transparently via a PDP-context or a circuit-switched connection established using GSM SM/CC . This allows transparent hand-over and roaming between GSM and UMTS provided that GSM supports the QoS requirements.