## Slide 1: Discussion on the problem of UE Radio Capability information size
NTT DOCOMO
S2-133918
TSG SA WG2 #100
San Francisco, USA, 11-15 November 2013

## Slide 2: UE Radio Capability size @TS23.401
In “5.11.2 UE Radio Capability Handling” of TS23.401, the size of UE Radio Capability information that MME should support is mentioned.
this information can be sufficiently large (e.g. >50 octets) that it is undesirable to send it across the radio interface at every transition from ECM‑IDLE to ECM‑CONNECTED.
the MME shall store the UE Radio Capability Information even if it is larger than specified in TS 36.331 [37], up to a maximum size of 510 octets.
MME may seem to support the size of UE Radio Capability information from 50 to 510 octets.

## Slide 3: UE Radio Capability size @RAN2
However, there was a discussion in RAN2 that capability size of Rel-10 UE supporting Carrier Aggregation may exceed the maximum value of 510 octets. (R2-133602)
The estimated size will be over 900 octets!

## Slide 4: Current Issue
The size of UE Radio Capability will be growing more and more!
  CT4 once asked RAN2 to define the maximum size of UE Radio Capability, but RAN2 couldn’t determine. (R2-131513)
Impact on MME's capability
-> It may lead to a decrease of the number of UE connections that MME can support.
Impact on network planning and cost
-> Operator is forced to increase of the number MMEs due to the memory shortage.

## Slide 5: Proposal
SA2 should ask RAN2 to
  inform SA2 the current maximum UE Radio Capability size to define the MME memory size in TS23.401.
  discuss future enhancements to suppress the increase of UE Radio Capability size including a study of reporting mechanism where the MME storage size is smaller than the UE capability size.