## Slide 1: Discussion on Core Network Type Selection based on the Subscription Information - REPORT OF OFFLINE DISCUSSION -
NTT DOCOMO
Vodafone?
Telecom Italia?
China Mobile?
Verizon?
Deutsche Telekom?
S2-134328
TSG SA WG2 #100
San Francisco, USA, 11-15 November 2013
Cisco?
ZTE?
NSN?
Huawei?
ALU?

## Slide 2: Conclusions from the offline session
Full-set of functionality will be needed.
Multi-meeting work will be needed.
(Potentially) a new WI for Rel-13
After SA2#100, NTT DOCOMO will initiate activities to progress the work / facilitate technical discussion

## Slide 3: Open questions
Are SGW separate for overlay networks?
Can MME of one overlay select SGW/PGW of another overlay?
Is SGW/PGW selection procedure the same?
How is load balancing performed/ changes to load balancing behavior?

## Slide 4: Annex
Next pages are the discussion material used in the offline drafting session (Tue 12 Nov Lunch)
  Please pay particular attention to p.5, which added a few points for further consideration (in red text)

## Slide 5: Agenda
Solutions on the table
  #1. Redirection + Identification Req/Resp (DOCOMO/Cisco)
  #2. Redirection after AIR/AIA (DOCOMO)
  #3-1. Specific GUTI + Non-broadcast TAI (ZTE)
  #3-2. null-MMEGI (Huawei)
  #4. MME-triggered S1-HO (NSN)
Scenarios to consider for each solution
  1) IMSI Attach
  2) GUTI Attach
  3) TAU/RAU
  4) Service Request
  5) Intra-RAT Idle Mode Mobility
  6) Inter-RAT Idle Mode mobility
  7) Handover (IRAT & intra-RAT)
  8) SGW/PGW/GGSN selection
  9) Initial assignment of a UE to a CN
  10) Determination of the wanted CN
  11) Roaming
  12) Shared network
  13) Load balancing
  14) For 2G/3G also
  15) Frequency of redirection
  16) Interworking with LAPI solution we have

## Slide 6: Discussion- handling of scenarios
 | Redirection + Identification Req/Resp | Specific GUTI + Non-broadcast TAI | MME-triggered S1-HO | 
1) IMSI Attach |  |  |  | 
2) GUTI Attach |  |  |  | 
3) TAU/RAU |  |  |  | 
4) Service Request |  |  |  | 
5) Intra-RAT Idle Mode Mobility |  |  |  | 
6) Inter-RAT Idle Mode mobility |  |  |  | 
7) Handover |  |  |  | 
8) SGW/PGW/ GGSN selection |  |  |  | 
9) Initial assignment of a UE to a CN |  |  |  | 
10) Determination of the wanted CN |  |  |  | 

## Slide 7: Solutions on the table

## Slide 8: #1. Redirection + Identification Req/Resp (DOCOMO/Cisco)
IMSI Attach is converted into GUTI Attach, and eNB select the right pool and pick one of the overlay MMEs according to “Core Network Type”.
eNB
Overlay
MME
UE
HSS
MME
Overlay
S/PGW
S/PGW
0. Attach Request
1. ULR/ULA
ULA: New Parameter to indicate that UE can select “Core Network Type” in the Subscription Data.
2. Reroute Command
(NAS, Core Network Type, GUTI)
4. Identification Req/Resp
(Security Context)
3. Attach Request
(GUTI)
5. (Optional) NAS Security Mode Command between Overlay MME and UE, and continue Attach procedure.
It is possible for Overlay MME to communicate with UE by using first MME’s Security Key.
6. Bearer estb.
7. ULR/ULA

## Slide 9: #2. Redirection after AIR/AIA (DOCOMO)
Overlay MME
Reroute Command
(Attach Request Message, Core Network Type)
Attach Request
“Core Network Type” is contained
Authentication Information Request
Authentication Information Response
REVISED
Notes: Does authentication complete? No. New MME does autherntication with HSS.
The full process needs to complete before UE timer runs out ( 10-15 sec)

## Slide 10: #3-1. Specific GUTI + Non-broadcast TAI (ZTE)
eNB
Overlay
MME
UE
HSS
MME
Overlay
S/PGW
SGW
0. Attach Request
1. ULR/ULA
ULA: New Parameter to indicate that UE can select “Core Network Type” in the Subscription Data.
2. Attach Accept
MME allocates specific GUTI (including MMEGI-B) with a non-broadcast TAI if “Core Network Type” is contained in the Subscription Data.
MMEGIs are pre-configured.
MMEGI-A -> of blue MME
MMEGI-B -> of overlay MME
3. TAU Request (w/ MMEGI-B)
A non-broadcast TAI (e.g. 0000, FFFF) drives UE to perform TAU procedure.
Overlay MME trys to get context information from blue MME due to the configuration of MMEGI-B
MMEGIs are pre-configured.
MMEGI-A -> redirect to blue MME
MMEGI-B -> redirect to overlay MME
MMEGIs are pre-configured.
MMEGI-A -> of blue MME
MMEGI-B -> of blue MME
4. Identification Req/Resp
2. Bearer estb.
(PGW would be Overlay PGW)
5. Bearer estb.
6. ULR/ULA

## Slide 11: #3-2. null-MMEGI (Huawei)
eNB
Overlay
MME
UE
HSS
MME
Overlay
S/PGW
0. Attach Request
1. ULR/ULA
ULA: New Parameter or default APN indicates CN
2. Attach Accept
Blue MME allocates specific GUTI (consisting of null-MMEGI of red CN (instead of blue MMEGI) and MME code of blue MME).
MMEGIs configured:
MMEGI-A -> of blue MME for its UEs
Null-MMEGI red -> of overlay CN
3. Next TAU Request (GUMMEI)
Null-MMEGI of red CN causes eNB to select an MME from red CN.
4. Context Req/Resp
2. Bearer estb.
(normal GW selection by APN)
5. Bearer modify
5. ULR/ULA
Red null-MMEGI + MME code identifies specific blue MME for context retrieval.

## Slide 12: #4. MME-triggered S1-HO (NSN)
NEW
UE
eNB
MME
Overlay MME
Overlay S/P-GW
HSS
0. Normal Attach procedure completion
PDN connenction established to overlay GW (based on subscription)
1. Handover trigger
2.Handover Required
7.Modify Bearer Req/Resp
3.Forward Relocation Request
4.Handover Request/Acknowledge
5.Forward Relocation Response
6.Handover Command
9.Update Location Request/Response
New procedure, triggered by MME after Attach is completed
Serving cell and eNB does not change. Procedure is modified/simplified compared to normal S1HO.
Following steps can be skipped and not shown in figure : measurements, data forwarding, status transfer, SGW relocation , handover notification.
Notes: The handover procedure is new/modified.
Here the source MME selects target MME.

## Slide 13: Evaluation of Alternatives
We propose that alt.1 is the best solution.
Alternatives |  | Pros Cons
1 | Redirection + Identification Req/Resp (DOCOMO/Cisco) | - Reuse existing procedures - Faster (Bearer establishment is needed only 1 time) - Take some of the same procedures
2 | Redirection after AIR/AIA (DOCOMO) | - Fastest (ULR/ULA with 1st MME can be omitted) - Bigger HSS impact expected - Security authorization would delay than usual
3-1 | Specific GUTI + Non-broadcast TAI (ZTE) | - Reuse existing procedures - No impacts on eNB - All MMEs must store the list of GUTI for each MME in the overlay network MME pool. - All MMEs and eNBs must have complex pre-configurations about GUTIs (MMEGIs). -> This may lead to exhaustion of MMEGIs in network. - May not be simple to apply this to 2G/3G where the NNI field structure is not well defined.
3-2 | null-MMEGI (Huawei) | 
4 | MME-triggered S1-HO (NSN) | - Reuse existing procedures - There may be some difficulties about selecting overlay SGW in the normal Attach procedure (if normal and overlay pools are different).
REVISED

## Slide 14: Clarification of #1 in each scenario

## Slide 15: 1) IMSI Attach
IMSI Attach is converted into GUTI Attach, and eNB select the right pool and pick one of the overlay MMEs according to “Core Network Type”.
eNB
Overlay
MME
UE
HSS
MME
Overlay
S/PGW
S/PGW
0. Attach Request
1. ULR/ULA
ULA: New Parameter to indicate that UE can select “Core Network Type” in the Subscription Data.
2. Reroute Command
(NAS, Core Network Type, GUTI)
4. Identification Req/Resp
(Security Context)
3. Attach Request
(GUTI)
5. (Optional) NAS Security Mode Command between Overlay MME and UE, and continue Attach procedure.
It is possible for Overlay MME to communicate with UE by using first MME’s Security Key.
6. Bearer estb.
7. ULR/ULA

## Slide 16: 2) GUTI Attach
Overlay MME
“Core Network Type” is contained
Reroute Command
(Attach Request Message, Core Network Type)
Attach Request

## Slide 17: 3) TAU/RAU
No need to perform
“Core Network Type” is contained
Indicating failure due to the mismatch of “Core Network Type”
Reroute Command
(TAU Request Message, Core Network Type)
Overlay MME
TAU Request
RAU takes (almost) the same procedure
REVISED

## Slide 18: 3) TAU/RAU
Open Issue
  Some optimizations may be needed to reduce inter-RAT TAU/RAU and redirection.
NEW

## Slide 19: 4) Service Request
No impact.
  NAS messages are always sent to overlay MME from eNB.
NEW
Overlay MME

## Slide 20: 5) Intra-RAT Idle Mode Mobility
No impact.
  GUTI/P-TMSI never change??
NEW

## Slide 21: 6) Inter-RAT Idle Mode mobility
No impact.
  GUTI/P-TMSI never change??
NEW

## Slide 22: 7) Handover
NEW
Appropriate MME/SGSN selection based on “Core Network Type” in Subscription Data
Overlay MME/SGSN

## Slide 23: 8) SGW/PGW/GGSN selection ~ 1. DNS solution ~
NEW
MME
/SGSN
DNS
Server
Attach
DNS: NAPTR Query (APN-FQDN)
Return NAPTR Record
(including the type of core network as one of the “List of Available Services”)
DNS: SRV Query
Return SRV Record
(List of Available Hosts)
DNS: A/AAAA Query
Return A/AAAA Record
(IP Address of the PGW)
If MME/SGSN contains the parameter of using overlay network in the Subscriber Data,
MME/SGSN selects one of the NAPTR records of overlay network and perform the SRV procedure to this record.

## Slide 24: 8) SGW/PGW/GGSN selection ~ 2. APN solution ~
If we prepare an APN per each CN, we can select “specific” overlay PGW/GGSN.
Overlay SGW selection is achieved by appropriate pool and DNS configuration.
NEW
Alternatives |  | Pros Cons
1 | DNS solution | - No need to prepare specific APN - No impact on UE - Impact on MME/SGSN
2 | APN solution | - Reuse existing procedures - No impacts on nodes - Impacts on UEs, especially when changing subscription property (e.g. UE’s default APN changing) - Need some cost for APN preparation and maintenance

## Slide 25: 9) Initial assignment of a UE to a CN
No impact.
  No problem of the overlay MME/SGSN selection.
  Faster than other 2 cases because of the only-1-time bearer establishment.
NEW

## Slide 26: 10) Determination of the wanted CN
No impact (except the GW/GGSN selection).
NEW