## Slide 1: S2-143325 Motivation for extending DRX - Release 13
May 2014

## Slide 2: Rel-12 MTC Power consumption optimization (MTCe-UEPCOP)
What was accomplished:
  Introduction of Power Saving Mode
    UE becomes unreachable for paging during PSM, it stops access stratum activities.
    How to enter PSM:
      UE negotiates Active time with MME (and optionally periodic TAU timer)
      UE starts active timer when it enters idle mode.
      When Active time expires it enters PSM.
    How to exit PSM:
      Trigger: MO data, Periodic TAU timer expires
      Action: Service request or TAU, respectively.

## Slide 3: Limitations of Power Saving Mode
PSM has limited applicability for unscheduled Mobile Terminated data with some requirement on MT data delay tolerance
  What can be done today with PSM for MT data:
    Negotiate Periodic TAU timer equal (or slightly shorter) to maximum allowed delay tolerance for MT data.
    UE needs to perform periodic TAU procedure to become available after entering PSM.
    Store & Forward functionality is required in the network:
      E.g.: SMS, SMS based triggering
    UE needs to negotiate an Active Timer large enough to allow the network to send the MT packet once UE updates registration:
      E.g.: SMS infrastructure is notified once UE performs periodic TAU
      Therefore Active timer should be 2min+
Drawbacks:
  Increased signaling due to unnecessary periodic TAUs
    Example: Delay tolerance = 30min, but only one MT data per day, there could be 47 unnecessary periodic TAUs per day per UE (if no MO data).
  Increased Power consumption due to unnecessary periodic TAUs

## Slide 4: Proposal for Rel-13
Open a new Rel-13 WID to adopt a solution that is effective for MTC power consumption reduction in scenarios requiring mobile terminated data.
Proposed solution: Extended DRX cycle
  Already introduced in TR 23.887 in Rel-12
  Benefit for MT data:
    Does not introduce additional signaling load
    DRX cycle can be set depending on the requirements on delay tolerance for MT data
    Has better power consumption than PSM for scenarios requiring mobile terminated data (see next slides for comparison)
  Proposal is to address all open issues from core network perspective in SA2 and engage RAN2 for RAN specific aspects.
    A companion Work Item will proposed in RAN plenary in December.

## Slide 5: PSM vs Extended DRX – Battery Life Comparison
Model for MO data:
  Device warm-up from deep sleep = 40ms
  Service request delay = 220ms
  X=4 MO data communications per day
  Time in connected mode for data transmission/reception = 400ms
    After 400ms of transmission UE is moved to I-DRX
Model for MT data:
  Non-scheduled Y=1 MT data per day, variable delay tolerance=60, 30, 15, 5 min.
  MT data communication lasts 1 second
  For PSM:
    It is assumed that MT data is SMS message.
    Periodic TAU timer = MT delay tolerance
    Active timer = 1min [Example value used in TR 23.887] & 10s [optimistic value]
    MT data arrives 30 seconds & 5 seconds after periodic TAU respectively
      UE performs TAU, stays in I-DRX with 2.56s DRX cycle for active time.
      UE is paged, performs SR, stays connected with data transmission/reception for 2.56s, and goes back to I-DRX
      UE stays in I-DRX for active time before going back to PSM.
NOTE: Comparison shown only for idle mode DRX vs PSM

## Slide 6: PSM vs Extended DRX – Battery Life Comparison (2)
Power values assumed (based on values used in RAN2 discussion in Rel-12 UEPCOP, see R2-132560)
Parameter | Value | Comments
 | 1 unit/ms | Power consumed for RX.
 | 2 unit/ms | Average power consumed for TX
 | 0.01 unit/ms | Power consumed during sleep mode, including power consumed for low accuracy clock and memory maintaining, leakage current (e.g. caused by power management unit), etc.
 | 0.0001 unit/ms | Optimized sleep state

## Slide 7: PSM vs Extended DRX – Battery Life Comparison (3)
Observations against PSM with Active time of 1 minute:
  Even with 1hr delay tolerance, PSM performs worse in terms of battery life than extending idle mode DRX cycle to 5 minutes.
  The performance of PSM drastically diminishes as delay tolerance decreases.

## Slide 8: PSM vs Extended DRX – Battery Life Comparison (4)
Observations against PSM with Active time of 10 seconds:
  Even for 1hr delay tolerance, PSM has similar power performance than extended I-DRX with DRX cycle of 5 minutes.
  This is a very optimistic active time value for PSM, as it assumes that whenever the UE performs periodic TAU, the UE will be paged before 10s span (example: SMS infrastructure would be notified, then resend stored SMS message to MSC->MME, and MME page in less than 10s)

## Slide 9: Why large DRX values?
We propose to extend DRX cycle length in idle mode to values in the order of minutes.
  Exact maximum value may be studied further in RAN2 but our target is at least around 5 minutes, beyond 10.24s.
As shown in R2-132560 during RAN2 UEPCOP study phase:
  A DRX cycle of 2 min can increase battery life by around 6 times the battery life for DRX=10.24s. A DRX cycle of 5 minutes can increase it by almost 9 times.
    (Comparative performance depends on traffic characteristic)

## Slide 10: Why the need for SA2 WID ?
Some companies expressed in SA2#104 that they prefer RAN2 to do the work on extended DRX, and SA2 aligns afterwards, using RAN2 design and TR 23.887.
However, there are purely Core Network aspects for which a solution has not been properly documented in TR 23.887, or the proposed solution(s) have not been concluded to be the solution to adopt.
  See following slides for list of open issues.
Given that these issues are not dependent on RAN2 work, and that the SA2 timeline for Rel-13 is ~6 months ahead of RAN2:
  SA2 should clearly conclude on the way forward on purely CN aspects, before or in parallel with RAN2 work on extended DRX.
  SA2 can align on the aspects dependent on RAN2 design for extended DRX once RAN2 has progressed the RAN aspects.
  NOTE that waiting for RAN2 work to progress before starting the two bullets above would be too tight at the end of the release, and likely result in poor outcome due to rushed agreements or need for exceptions at the end of Rel-13.

## Slide 11: Open issues for extended DRX
Idle mode:
  How does the S-GW know that a device is in extended DRX idle mode when the a DL packet arrives?
    This issue was brought up by Cisco, the S-GW needs to know that a DL packet may need to be stored for a long time. This has not been considered in TR 23.887.
  How to handle retransmissions from the SMS infrastructure. A hint of a solution was included in the TR 23.887, but not complete. Handling may also be slightly different for the case of SMS over SGs and SMS in MME. (Should we also consider SMS over IMS?)
  Retransmissions in P-GW. This issue was not solved in TR 23.887.
Connected mode:
  NAS retransmissions. Increasing NAS retransmission timers is hinted in TR, but not clear how MME knows of extended DRX in connected mode.
  Retransmissions from SMS infrastructure not solved.
  Retransmissions in P-GW.