## Slide 1: Problems and solutions for Co-existing of “SMSoverSGs”, “SMSinSGSN”, “SMSinMME”
CATT

## Slide 2: Possible Co-existing Scenarios
 | SMS in SGSN used | SMS in SGSN Not supported, i.e. SGSN in CSFB configuration used.
SMS in MME used | Scenario 1: Whole NW support “PS only” | Scenario 2: SGSN in CSFB configuration
SMS in MME Not supported | Scenario 3: SMS over SGs used at LTE side; | Scenario 4: Current CSFB setting, without PS only features.
Scenario 1:
  Theoretically exists in Spec now, but in future, may be popular due to 1) the increase of “PS only” devices, and 2) CS domain phased out gradually;
Scenario 2:
  Almost an impossible scenario,
Scenario 3:
  May be the first scenario in real deployment; discuss this first;
Scenario 4:
  Not related to “SMS in SGSN” and “PS only”;

## Slide 3: #3: “SMS in SGSN” and “SMS over SGs” Co-existing Scenario, Showing Problem # 1.1
E-UTRAN
GERAN/
UTRAN
MME
SGSN
HSS
SMS-GMSC/
IWMSC/
SMS Router
S6a
S6a/Gr
SGs
Gd
S6c/C
S3
MSC/VLR
E
C
ISR Activated by MME ( UE firstly attach via 2G/3G and get SMS in SGSN, and the re-select to E-UTRAN, and get “SMS only” and ISR Activated during Combined TA/LA Update procedures.
MSC/VLR, and SGSN (may still) is already registered in HSS as MT-SMS routing nodes.
Problem # 1.1: Un-necessary CS paging
MT-SMS arrives at MS/VLR, S1 paging sent, and S3 paging for CS/SMS forwarded to SGSN, in this case, SGSN is required to send CS Paging via GERAN/UTRAN…..(See 8.2.5.f of TS23.272)
MS, if camped on 2G/3G, may ignore CS paging if it is registered for “PS and SMS only services”, (See 4.5.1.4 of 7S24.008) .
Notes: 8.2.5f Mobile Terminating SMS when ISR is active and SGs is active between MSC/VLR and MME
When the MME receives the SGs Paging message for SMS, and ISR is active, and the UE is in idle mode, the MME sends the S1 interface paging message to the E‑UTRAN (using the S-TMSI as temporary identity) and sends a CS paging message (SMS indicator) to the SGSN using the MSC TMSI as temporary identity (unless the MSC did not allocate a TMSI, in which case the IMSI is used for paging).
The UE is paged on E‑UTRAN and by the SGSN on GERAN and/or UTRAN. For GERAN A/Gb mode, the SGSN sends a PAGING CS message to the BSS (see TS 48.018 [30]). For UTRAN, the SGSN sends a PAGING message to the UTRAN (see TS 25.413 [29]) with the CN Domain Indicator set to 'CS domain' and the Paging Cause set to 'Terminating Low Priority Signalling'. The UE responds on the cell on which it is camped. When camped on E-UTRAN, the UE responds to the MME. When camped on GERAN or UTRAN, the UE responds to the MSC.

## Slide 4: #3: “SMS in SGSN” and “SMS over SGs” Co-existing Scenario, Showing Problem # 1.2
E-UTRAN
GERAN/
UTRAN
MME
SGSN
HSS
SMS-GMSC/
IWMSC/
SMS Router
S6a
S6a/Gr
SGs
Gd
S6c/C
S3
MSC/VLR
E
C
Problem # 1.2: Second delivery attempt Fails.
GMSC may use SGSN as second route for MT-SMS, upon receipt of MT-SMS, SGSN pages in GERAN/UTRAN, if UE camped in GERAN/UTRAN, the MT-SMS is delivered.
However, if UE re-select to E-UTRAN, the second route delivery will fail.

## Slide 5: Option #1 to Problem#1.1
E-UTRAN
GERAN/
UTRAN
MME
SGSN
HSS
SMS-GMSC/
IWMSC/
SMS Router
S6a
S6a/Gr
SGs
Gd
S6c/C
S3
MSC/VLR
E
C
Option #1 to Problem # 1.1:
  If SMS in SGSN is used for a UE, this SGSN discard S3 CS Paging message received for this UE;
  Pros: Un-necessary CS paging avoided for PS only Ues;
  Cons: MT-SMS maybe delayed, if PS only UE is implemented to answer CS-Paing;

## Slide 6: Option #2 to Problem#1.1
E-UTRAN
GERAN/
UTRAN
MME
SGSN
HSS
SMS-GMSC/
IWMSC/
SMS Router
S6a
S6a/Gr
SGs
Gd
S6c/C
S3
MSC/VLR
E
C
Option #2 to Problem # 1.1:
  MSC/VLR forward MT-SMS to MME, then MME forward MT-SMS to SGSN, SGSN and MME page with “PS domain” indicator;
  Pros: In time MT-SMS delivery .
  Cons: network entities enhancement needed.

## Slide 7: Option #3 to Problem#1.2
E-UTRAN
GERAN/
UTRAN
MME
SGSN
HSS
SMS-GMSC/
IWMSC/
SMS Router
S6a
S6a/Gr
SGs
Gd
S6c/C
S3
MSC/VLR
E
C
Option #3 to Problem # 1.2:
  If SMS in SGSN is used for UE, SGSN forward received MT-SMS to MME, then SGSN and MME page with “PS domain” indicator;
  Pros: In time MT-SMS delivery .
  Cons: network entities enhancement needed.

## Slide 8: Proposals for Scenario #3 – (1)
Normally, operator should be able to deploy/upgrade MME and SGSN from different releases. Thus we propose that:
  Adopt option #1 to problem #1.1;
  Adopt option #3 to problem #1.2;
  Not adopt Option #2, since it impacts MSC/VLR a lot;
Why can not let MME deactivate ISR in Scenario #3?
  ISR is support capability exchanged between MME and SGSN is not per UE basis, is per MME/SGSN node basis;
  In current TS23.272, “So an SGSN in a CSFB/SMS over SGs configuration never indicates ISR activated in combined RAU procedures for a UE that supports CSFB/SMS over SGs. “
    WHY ? Only deactivate ISR for CSFB enabled UE, in order to take full ISR benefits for non-CSFB enabled UE, e.g. SRVCC UE ( Introduced byS2-090804, Do Co Mo, ISR deactivation based on UE's CS Fallback capability)

## Slide 9: Proposals for Scenario #3 – (2)
  How to handle ISR in SMS in SGSN case, is not clear;
Based on above consideration, i.e. to take full ISR benefits, it is proposed that:
  If “SMS in SGSN” is used for a UE, this SGSN also Activated ISR for this UE;
  Pros:
    Full ISR benefits:
    In time MT-SMS delivery:
    No more CS-Paging for PS-Only UE;
  Cons:
    Impacts on MME, SGSN, and MSC/VLR;
    No UE impacts;

## Slide 10: Possible Co-existing Scenarios
 | SMS in SGSN used | SMS in SGSN Not supported, i.e. SGSN in CSFB configuration used.
SMS in MME used | Scenario 1: Whole NW support “PS only” | Scenario 2: SGSN in CSFB configuration
SMS in MME Not supported | Scenario 3: SMS over SGs used at LTE side; | Scenario 4: Current CSFB setting, without PS only features.
Scenario 3:
  Activate ISR for “PS only” UE, if SMS in SGSN is used for this UE;
Scenario 1 :
  Theoretically exists in Spec now, but in future, may be popular due to 1) the increase of “PS only” devices, and 2) CS domain phased out gradually;
  Thus we propose that:
    If SMS in MME is used for a UE, this MME also activated ISR for this UE

## Slide 11: #1: “SMS in SGSN” and “SMS in MME” Co-existing Scenario, with S3 enhancements ( i.e. option 2 to P1.1, option1 to P1.2 )
UE attach in GERAN/UTRAN, then combined TA/LA in E-UTRAN and get ISR activated, on network side, SMS in MME is used for this UE;
UE camped in GERAN/UTRAN, and the SMS-GMSC use MME as first route to delivery MT-SMS(Step (1) ); MME also forward received MT-SMS to SGSN Step (3) ; both MME and SGSN page UE at E-UTRAN and GERAN/UTRAN(step (2) and (4) ); UE response to SGSN(Step(5)) to get MT-SMS, then SGSN report back to MME that forwarded SMS has been delivered successfully(Step (6)).
If SMS-GMSC first delivery MT-SMS to SGSN, in such case, SGSN will also forward MT-SMS to MME;
E-UTRAN
GERAN/
UTRAN
MME .
SGSN .
HSS
SMS-GMSC/
IWMSC/
SMS Router
S6a
S6a/Gr
SGd
Gd
S6c/C
S3
(1)
(2)
(3)
(4)
(5)
(6)

## Slide 12: #2: “SGSN in CSFB configuration” and “SMS in MME” Co-existing , with S3 enhancements ( i.e. option 2 to P1.1, option1 to P1.2 )
E-UTRAN
GERAN/
UTRAN
MME
SGSN
HSS
SMS-GMSC/
IWMSC/
SMS Router
S6a
S6a/Gr
Gs
S6c/C
S3
UE first combine attach via GERAN/UTRAN, the combine TA/LA, and network choose SMS in MME, ISR Activated by MME, UE current camped RAT is not known.
In this case, HSS will send cancel location to MSC/VLR; and use MME as MT-SMS delivery.
With enhancement, the MME page on E-UTRAN, and MME forward SGd received MT-SMS to SGSN via S3, SGSN will page on UTRAN, for MT-SMS delivery.
Once UE perform Combine RAU/LAU, ISR will be deactivated by SGSN in CSFB configuration according to current Spec, Gs will be re-established, and HSS will cancel previously registered MME “i.e. MME registerd as MSC/VLR for MT-SMS”;
MSC/VLR
C
E
SGd

## Slide 13: Summary of Proposals
If the “SMS in SGSN” is used, then
  SGSN activated ISR in combined RAU/LAU procedure.
    Use existing ISR activation signaling;
    No need to check “EMM combined procedure capability”;
If the “SMS in MME” is used, then:
  MME activated ISR in combined TA/LA procedure.
    Use existing ISR activation signaling;
Enhancement to SGSN
  If CS paging received from S3 paging, and SMS in SGSN is used for this UE, then discard this CS-paging;
Enhancement to MSC/VLR:
  Forward MT-SMS to MME;
  Not adopted. Due to un-willing/difficult to change the MSC/VLR.
Enhancements to S3 interfaces:
  MME/SGSN forward MT-SMS received on SGd/Gd to SGSN/MME via S3 interface;
  If forwarded MT-SMS has been delivered to UE, SGSN/MME report back to MME/SGSN;
  Pros:
    Full ISR benefits: In time MT-SMS delivery:
    No more CS-Paging for PS-Only UE;