## Slide 1: eCSFB evaluation
S2-144098

## Slide 2: Evaluation Part
 | Sol 1 Huawei et al SRVCC based eCSFB Solution | Sol 2 Intel SRVCC based eCSFB Solution w. proper CS resource allocation | Sol 3 Ericsson Enabling target cell(s) system information provision | Sol 4 Ericsson UE radio capabilities consideration during PLMN and RAT selection | Sol 5 Ericsson Optimized CSFB Procedure | Sol 6 Samsung eCSFB with IMS#1 | Sol 7 Ericsson, Intel CS security key derivation for eCSFB
Performance improvement | See later slide | Same as Sol 1 | See later slide | TBD | See later slide | TBD Additional time needed for IMS call setup | See later slide
UE impact | SRVCC required + UE handling of CC is unspecified | SRVCC required + new functionality | No | No | No | Rel12 functionality (pre-alerting SRVCC) | Yes (SW only) no SRVCC required
Network impacts | eNB, MME, MSC | eNB, MME, MSC | eNB | eNB | MSC | eNB, MME, MSC, P-CSCF | MME, MSC
Other | Potentially additional UE impacts (HO failure handling, MO calls) |  | RIM or Sol 3 combined with Sol 5 or Sol 7 ~ same performance as Sol 1 and Sol 2 |  |  |  | UE impact is SW only

## Slide 3: Performance Considerations
Many parts of the different solutions are the same, hence can be ignored when comparing the performance
Note: focus on solutions 1,2, and 3 + (5 or 7)
  Sol 4 is a solution to avoid CSFB failures in certain networks
  Sol 6 is worse than the other solutions discussed
Possible differences of Sol 1, 2, and 3 + (5 or 7) are
  T1: Time spent prior moving to 2G/3G, and after Extended Service Request
  T2: Time to move the terminal to 2G/3G
  T3: Time for Bearer setup in 2G/3G
  T4: Start of Ciphering/Integrity protection
Note: in all these solutions there is no need to authenticate the UE, otherwise there would be also
  Tx: Time to authenticate the UE in CS (only needed in solution 7 if not falling back to the same MSC, but even that could be fixed for both mobile terminal (extending MTRF) and originated calls by forwarding in both cases the CS security keys to the new MSC

## Slide 4: Sol 1 revisit MO

## Slide 5: Sol 1 revisited MT

## Slide 6: Sol 3+ 7 or 5 MO
Note: Very Early Assignment is assumed in this example
Notes: Early assignment (at CM service request) would add some 200 ms extra delay

## Slide 7: Sol 3+ 7 or 5 MT
Note: Very Early Assignment is assumed in this example
Notes: Early assignment (at CM service request) would add some 200 ms extra delay

## Slide 8: Performance Comparison Spotlight on T1 - T4
 | Solution 1 | Solution 2 | Solution 3 + (5 or7)
T1 (Time spent prior moving to 2G/3G, and after Extended Service Request) | IRAT measurement: ~400-2400 ms Handover preparation time: ~400-600ms | Same as solution 1 | Not applicable
T2 (Time to move the terminal to 2G/3G) | ~110-200ms |  | ~300-700ms
T3 (Time for Bearer setup in 2G/3G) | Not applicable |  | ~400 ms
T4 (Time to start Ciphering/integrity protection) | Not applicable |  | ~200 ms
Summary | ~900-3200 ms |  | ~900-1300 ms
The above is the additional time compared to normal CS setup if there is no need to authenticate the UE and only sum of the times that differ between the different solution (i.e., it is not the total additional call setup time in case of CSFB). No need to authenticate the UE in CS in any of these solutions.
Note: T2+T3 in case of CSFB without enhancements is ~2.7 sec to 2G and ~1.5 sec to 3G.

## Slide 9: Performance Comparison Spotlight on T1 - T4
 | Solution 1 | Solution 2 | Solution 3 + (5 or7)
T1 (Time spent prior moving to 2G/3G, and after Extended Service Request) | IRAT measurement: ~400-2400 ms Handover preparation time: ~400-600ms | Same as solution 1 | Not applicable
T2 (Time to move the terminal to 2G/3G) | ~110-200ms |  | ~300-700ms
T3 (Time for Bearer setup in 2G/3G) | Not applicable |  | ~400 ms
T4 (Time to start Ciphering/integrity protection) | Not applicable |  | ~200 ms
Summary | ~900-3200 ms |  | ~900-1300 ms
The above is the additional time compared to normal CS setup if there is no need to authenticate the UE and only sum of the times that differ between the different solution (i.e., it is not the total additional call setup time in case of CSFB). No need to authenticate the UE in CS in any of these solutions.
Notes: T2+T3 and CSFB without enhancements can take is 2.7 sec to 2G and 1.5 sec to 3G.
Unlike SRVCC, CSFB can happen anywhere in the cell and It is hence likely that the measurement procedures has to start from scratch i.e. the typical numbers would tend to be in the top half.

## Slide 10: GERAN Capacity Considerations
The GERAN specification offer a set of different options on when to assign a full TCH during the call establishment.
  Very early assignment
  Early assignment
  Assignment
These assignment options allow for a operator to tune the balance between call setup time and resource usage
Solution 3, 5 and 7 allows to operator to keep the flexibility and select any of the assignment options.
Solution 1 and 2 does not maintain this flexibility since the SRVCC HO always use FACCH (a full TCH) when moving to GERAN.

## Slide 11: Conclusion
The combination of:
  RIM or Solution 3 (Provides 2G/3G Target System Information to E-UTRAN)
  Solution 5 or 7 (decreases or avoids authentication on the target side)
Brings the most significant call setup time improvements
RIM, Solution 3, 5 and 7 are all independent
  i.e. an operator can pick and choose what to deploy
RIM, Solution 3 and 5 have no UE impact
  These improvements work for the existing UE’s in the field
Solution 7 does not require SRVCC and existing UE’s can be SW updated. The solution for key derivation can be reused from SRVCC.

## Slide 12: Conclusion
The combination of:
  RIM or Solution 3 (Provides 2G/3G Target System Information to E-UTRAN)
  Solution 5 or 7 (decreases or avoids authentication on the target side)
Brings the most significant call setup time improvements
RIM, Solution 3, 5 and 7 are all independent
  i.e. an operator can pick and choose what to deploy
RIM, Solution 3 and 5 have no UE impact
  These improvements work for the existing UE’s in the field
Solution 7 does not require SRVCC and existing UE’s can be SW updated. Solution for key derivation can be reused from SRVCC.
Specification of solution 3, 5 and 7 gives most “bang for the buck”
Solution 1 may be outperformed by the combination of RIM or Sol 3 with Solution 5 or 7.