## Slide 1: Discussion on intra-DÉCOR offloading
NTT DOCOMO
S2-150929
TSG SA WG2 #108
13 - 17 April 2015,San Jose Del Cabo, Mexico

## Slide 2: What is intra-DÉCOR offloading?
TAU might access common pool if legacy load balancing TAU is used.
  Strongly recommended to steer TAU to MMEs within Décor pool for avoiding signaling impact on common pool.
  This procedures should be used for O+M related work, not for congestion control. See TS 23.401 clause 4.3.7.3.
Common Pool
MME
MME
MME
eNB
UE
1. S1 release (cause: load balancing TAU required) + RRC conn. release
2. TAU w/ RRC conn. estb
3. MME selection from all MMEs
Normal load balancing TAU
Common Pool
MME
MME
MME
eNB
UE
1. S1 release (cause: load balancing TAU required) + RRC conn. release
2. TAU w/ RRC conn. estb
3. MME selection from all MMEs which have S1 connection w/ eNB
Load balancing TAU w/ Decor
Décor Pool
D-MME
D-MME
Take out of service
4. TAU would be transferred to Décor pool by rerouting.
Take out of service
Access to common pool might happen (at 60 % in above case).

## Slide 3: Alt 3: Two MMEGIs per Décor Pool; normal MMEGI + null-MMEGI
Common Pool
MME
MME
MME
eNB
UE
2. TAU
Décor Pool
D-MME-A
D-MME-D
D-MME-B
D-MME-C
1. GUTI reallocation + non-broadcast TAI allocation + S1 release
For inducing immediate TAU from UE
(but it depends on UE’s implementation)
3. Steer TAU to D-MMEs if null-MMEGI is included in new GUTI
Take out of Service
4. Get the UE context from old MME
by referring MMEC in new GUTI (existing procedure)
Configuration of association between Décor MME pools and null-MMEGIs needed
normal MMEGI + null-MMEGI
Null-MMEGI (+MMEC) included if load balancing performed
All Décor pools need extra MMEGis, i.e. null-MMEGIs.
-> The number of MMEGIs for normal usage would be reduced according to the number of Décor pools.

## Slide 4: Alt.4: GUTI/P-TMSI reallocation + non-broadcast TAI/RAI
Common Pool
MME
MME
MME
eNB
UE
2. TAU
Décor Pool
D-MME-A
D-MME-D
D-MME-B
D-MME-C
1. GUTI reallocation + non-broadcast TAI allocation + S1 release
For inducing immediate TAU from UE
(but it depends on UE’s implementation)
3. Send TAU to D-MME-D (existing procedure)
Take out of Service
5. Get the UE context from old MME
by referring MMEC in GUTI (existing procedure)
Configuration of association between Décor MME pools and their normal MMEGIs needed
normal MMEGI only
D-MME-D’s GUTI included if load balancing performed
4. Do redirection to other dedicated MME.

## Slide 5: Common function for all alternatives < Intra-Common pool load balancing - Existing Procedure >
Common Pool
MME-A
MME-B
MME-C
eNB
UE
1. S1 release (“Load balancing TAU”)
2. TAU
(no S-TMSI or MMEID in RRC Connection Setup)
3. Steer TAU to common MME
Décor Pool
D-MME-A
D-MME-D
D-MME-B
D-MME-C
If eNB gets no S-TMSI or MMEID in RRC Connection Setup, eNB load-balances from common MME pool only.
[modification from existing function, i.e. eNB does not select Décor MMEs]
Take out of service
4. DNS based on GUTI. (existing function)

## Slide 6: Evaluation & Proposed Conclusion
Alt 4 is our preference.
Alternatives | Pros | Cons
Alt 3. Alt 3: Two MMEGIs per Décor Pool; normal MMEGI + null-MMEGI | Use legacy procedures only | Need additional MMEGI for dedicated CN
Alt 4. GUTI/P-TMSI reallocation + non-broadcast TAI/RAI | Use legacy procedures + redirection No additional MMEGI | Need additional signaling by redirection