## Slide 1: Discussion on S8HR VoLTE Roaming
NTT DOCOMO
TSG SA WG2 #108
San Jose Del Cabo, Mexico
13-17 April 2015
S2-150985

## Slide 2: [Pre-read] LS-in’s related to this paper
S2-150710: LS from CT3 (SA3)
S2-150704: LS from GSMA PSMC
S2-151015: LS from GSMA Networks Group

## Slide 3: VoLTE Roaming: Latest Status in GSMA
Ongoing discussion on VoLTE roaming architecture in GSMA
  LBO (RAVEL) vs S8HR (new)
GSMA endorsed S8HR as a candidate, subject to technical issues resolved in 3GPP
  Issues are described in LS from GSMA Networks Group
O-HPMN
T-HPMN
T-VPMN
O-VPMN
SCSCF
PCSCF
SCSCF
PCSCF
HSS
O-HPMN
T-HPMN
T-VPMN
O-VPMN
SCSCF
PCSCF
SCSCF
PCSCF
S-GW
P-GW
S-GW
P-GW
P/S-GW
P/S-GW
TRF
LBO (RAVEL)
S8HR (new)

## Slide 4: S8HR Overview
All IMS entities are in HPLMN
S8 interface is used as inter-PLMN interface for VoLTE
Assumed that UE is based on GSMA PRD IR.92 (same UE can be used for LBO and S8HR)

## Slide 5: Issues Identified in GSMA (so far)
Unauthenticated Emergency Call
Non UE Detectable Emergency Call
Lawful Intercept in VPLMN
SRVCC for S8HR
Co-existence of LBO and S8HR
Netloc for S8HR (upon IMS registration)
Geo-local number translation

## Slide 6: Issue 1: Unauthenticated Emergency
Question: How exactly should UE behave when emergency IMS registration fails, taking into account all the different regulatory requirements?
Same issue as previously discussed in SA2
  S2-150156, 0157, 0158, 0159
NTT DOCOMO and Co. submitted a discussion paper + CRs again to 3GPP maintenance session, hoping to continue the debate there.

## Slide 7: Issue 2: Non UE Detected Emergency
With S8HR, Non UE Detected Emergency calls are routed to P-CSCF in HPLMN.
P-CSCF in HPLMN needs to identify whether the dialed digits are local emergency number in VPLMN, and then proceed or return SIP 380..
  Current 3GPP specs need update to ensure P-CSCF in HPLMN can take MCC into account
VPLMN
PCSCF
Non UE Detected
Emergency Call
380
Or proceed…
HPLMN
VPLMN
PCSCF
Non UE Detected
Emergency Call
380
Or proceed…
LBO (RAVEL)
S8HR (new)
P-CSCF in the HPLMN, based on the roaming agreement and the configured local emergency numbers for that VPLMN, analyses the dialled digits, and if an emergency call is detected, rejects that call with SIP response code "380".
This requires “per MCC” configuration in P-CSCF

## Slide 8: Issue 3: Lawful Interception
LI for IMS is currently done at IMS entities in both HPLMN and VPLMN
With S8HR, LI for IMS in VPLMN requires LI at SGW / MME.
Lawful Interception in VPLMN must be defined for S8HR.
GSMA assume that operators do not use IPSec confidentiality protection on SIP / RTP
For SA3/SA3-LI
GSMA asks 3GPP to study / define IMS LI in VPLMN where IMS (SIP/RTP) traffic is routed directly back to HPLMN using S8 interface.

## Slide 9: Issue 4: SRVCC
SRVCC (a/b/e/midcall/r) uses ATCF/ATGW, but ATCF/ATGW are defined as entities in VPLMN
With S8HR, ATCF/ATGW must be in HPLMN
GSMA thinks that roaming SRVCC, with ATCF/ATGW in HPLMN, technically works (putting aside potential interruption time issues), but requires 3GPP feedback on the feasibility
  GSMA is aware IMS NNI is needed for some SRVCC scenarios e.g. a/b/midcall

## Slide 10: Issue 5: Co-Existence of LBO + S8HR
It is assumed “IMS well-known APN” is used for both LBO and S8HR options (as per GSMA IR.92)
Usage of “VPLMN Address Allowed” in conjunction with IMS Roaming Agreement needs clarification in 3GPP
HPLMN
VPLMN
HPLMN
VPLMN
S-GW
P-GW
MME
HSS
LBO (RAVEL)
S8HR (new)
Acc. GSMA IR.88, HSS sets “VAA” for IMS APN, when there is IMS roaming agreement – in order to enable LBO
With S8HR, “VAA” shall NOT be set for IMS APN, as the bearer for IMS must be home routed.
MME
HSS
Although undefined, “VAA” may carry a meaning that the UE has IMS Roaming Agreement
S-GW
P-GW
“VAA” must not imply anything about IMS roaming agreement
Discussion is requested to sort out the usage of “VAA”, also taking into account also the signalling / resource usage impacts in VPLMN. (as per previous SA2 – GSMA LS exchange a couple years ago)

## Slide 11: Issue 6: Netloc for IMS Registration
Netloc does not support location retrieval during IMS registration (for both LBO + S8HR)
For S8HR, VPLMN ID needs to be obtained at the time of IMS registration to enable charging / communication barring / data retention.
(Discussion required whether this also applies to LBO/RAVEL scenarios)
LBO (RAVEL)
S8HR (new)
O-HPMN
O-VPMN
SCSCF
PCSCF
O-HPMN
O-VPMN
SCSCF
PCSCF
S-GW
P-GW
PCRF
PCRF
FFS if similar function is needed
P-CSCF needs to obtain (at the time of IMS reg) VPLMN ID..

## Slide 12: Issue 7: Geo-local number handling
UE / NW have option to support geo-local number (23.228)
Clarification required in TS23.228 whether HPLMN has the decision to enable / disable the support of geo-local numbers.
If VPLMN local numbers (geo-local) numbers must be supported, then HPLMN must be able to translate the number based on configuration, taking into user location information into account.
  E.g. Local short-code service, calling local number without country code, calling local number without country + area code, etc
GSMA LS requests 3GPP to look into this issue and reply whether solution is available
LBO (RAVEL)
S8HR (new)
O-HPMN
VPLMN
SCSCF
PCSCF
O-HPMN
VPLMN
SCSCF
PCSCF
S-GW
P-GW
PCRF
TRF
Entities (CSCF/AS) in HPLMN must be able to identify the location of the UE, modify the geo-local number to number in international format, and route the call to the destination
LBO with Home-Routing (no loopback) same problem may exist.
With LBO with loopback, S-CSCF can route the INVITE to TRF in VPLMN and ask the TRF to modify the number; TBC if location information can be made available at TRF
General discussion expected on:
who’s deciding whether to provide numbers in non-int’l format and to what extent(=HPLMN?)
How to minimise the operational complexity (e.g. HPLMN keeping the huge translation table)

## Slide 13: Proposal: Work Plan for SA2#108 + #109
LS back to GSMA by July (= deadline is SA2#109, May 2015)
  Alt 1) Work directly on LS Back
    Draft LS available in this meeting
  Alt 2) Report to TSG SA, let TSG SA consolidate input from various SA WGs, and let TSG SA reply to GSMA
In SA2#108, progress the discussion on issues identified
  On each topic:
    Open discussion paper / CRs (where applicable)
    Work directly on LS back (for items where relevant tdocs are not available)
    Although GSMA still undecided on official S8HR endorsement, it is ultimately up to SA2 to decide whether or not to approve these CRs
In May 2015 (SA2#109), discuss:
  Continue discussion on tdocs raised in SA2#108
  Discuss issues that are not captured in GSMA LS but are newly found
    Company contribution expected (i.e. don’t expect further LS from GSMA)
  Discuss how/when to handle issues that cannot be completed
  Approve the LS (or report to TSG SA)

## Slide 14: List of relevant SA2 tdocs (to be updated after tdoc deadline)
Issue # | Tdoc # | Source company | agenda
Draft LS back to GSMA | S2-150986 | NTT DOCOMO | 4.2 (GSMA LS)
Issue 1: Unauthenticated IMS emergency | S2-150989 S2-150992 | NTT DOCOMO | 5.4 (IMS maint)
Issue 2: Non UE Detected IMS Emergency | S2-150993 | NTT DOCOMO | 5.4 (IMS maint)
Issue 3: Lawful Intercept | n/a (SA3 / SA3-LI) | n/a | n/a
Issue 4: SRVCC | S2-150997 | NTT DOCOMO | 5.4 (IMS maint)
Issue 5: Co-existence of LBO + S8HR | S2-150998 | NTT DOCOMO | 5.1 (3GPP maint)
Issue 6: Netloc for IMS registration | S2-151000 | NTT DOCOMO | 5.4 (IMS maint)
Issue 7: Geo-local number handling | S2-150884 | CMCC, NTT DOCOMO | 5.4 (IMS maint)