## Slide 1: Discussion on Unauthenticated IMS Emergency Call
NTT DOCOMO
TSG SA WG2 #108
San Jose Del Cabo, Mexico
13-17 April 2015
S2-150989

## Slide 2: INTRODUCTON Recap of SA2 discussion in SA2#107
TS23.167 Subclause 4
  If a UE has sufficient credentials, it shall initiate an emergency registration with the network (requiring the involvement of the home network). […] If the registration fails, the UE may attempt an anonymous emergency call.
This behaviour is not fully captured in Annex H / Subclause 6
IMS registration can fail for whatever reasons (thus not only relevant to roaming and S8HR without IMS NNI, but also to non-roaming scenarios and roaming with LBO/RAVEL)
The discussion at SA2#107 revealed that there are different requirement as to allow/disallow anonymous emergency call
This paper tries to sort out the (combination of) different requirements
and proposes the way forward…

## Slide 3: We all live in a complex world…
Assuming UE / VPLMN support IMS Emergency Call, we need to take into the following parameters, in order to make sure 3GPP specifications are compliant with whatever regulatory requirements that exist around the world:
UE
UE has UICC / has no UICC
Local VPLMN Policy:
Types of IMS Emergency Bearer Support in VPLMN (as in TS23.401, Subclause 4.3.12.1)
  a. Valid UEs only. No limited service state UEs are supported in the network. Only UEs that have a valid subscription, are authenticated and authorized for PS service in the attached location are allowed. UEs should be attached to the network and then perform a PDN Connection Request when an IMS emergency session is detected by the UE.
  b. Only UEs that are authenticated are allowed. These UEs must have a valid IMSI. These UEs are authenticated and may be in limited service state due to being in a location that they are restricted from service. A UE that can not be authenticated will be rejected.
  c. IMSI required, authentication optional. These UEs must have an IMSI. If authentication fails, the UE is granted access and the unauthenticated IMSI retained in the network for recording purposes. The IMEI is used in the network as the UE identifier. IMEI only UEs will be rejected (e.g., UICCless UEs).
  d. All UEs are allowed. Along with authenticated UEs, this includes UEs with an IMSI that can not be authenticated and UEs with only an IMEI. If an unauthenticated IMSI is provided by the UE, the unauthenticated IMSI is retained in the network for recording purposes. The IMEI is used in the network to identify the UE.
VPLMN Policy: IMS emergency registration (i.e. IMS level authentication) required / not required
VPLMN Policy: Callback support required / not required
Context:
Availability of CS domain in VPLMN
LTE Roaming agreement:
  data-only (=no IMS voice but CSFB works)
    PS attached, either CS attached or not attached, VoIMS not indicated, EMC indicated
  Data+IMS voice / IMS voice-only (no data)
    PS attached, either CS attached / not attached, VoIMS indicated, EMC indicated
  No agreement
    PS Not attached, either CS attached / not attached, VoIMS not indicated, EMC indicated

## Slide 4: Issue #1
PLMN operates in “a) All UEs are allowed”, and supports EMS and VoIMS
UE is not attached to CS domain
  some error in CS domain and UE not attached; or
  LTE-only PLMN i.e. no CS domain;
    Maybe the future world where PLMN turns off CS
Table H.1 Case A
  assume PS domain is used
If IMS emergency registration fails (for whatever reason);
  If UE implements the anonymous option;
    IMS emergency call can be made
  If UE does not implement the anonymous option;
    Emergency call fails
Proposal: UE shall retry with the anonymous emergency
(for success rate of emergency call is considered legally sensitive… )

## Slide 5: Issue #2
When PLMN uses TS23.401 Operator Behaviour C)
    c. IMSI required, authentication optional. These UEs must have an IMSI. If authentication fails, the UE is granted access and the unauthenticated IMSI retained in the network for recording purposes. The IMEI is used in the network as the UE identifier. IMEI only UEs will be rejected (e.g., UICCless UEs).
3GPP specs do not define whether same policy applies to IMS
Do we assume the same principle also in IMS layer?
If yes (UE with IMSI accepted / UICC-less UE rejected),
    In case of UE not IMS emergency registered, anonymous INVITE does not carry IMSI
      According to TS24.229 Subclause 5.1.6.8.2 “Emergency session set-up in case of no registration”
        From Header = “anonymous”
        P-Preferred-Identity = Equipment identifier
    So how can the IMS entities handling emergency call recognise whether UE has UICC?
    Callback not possible even with UE with UICC…
Proposal: UE with IMSI shall include IMSI + MSISDN when attempting anonymous emergency call