## Slide 1: Way forward on CIoT architecture design

## Slide 2: Contents
Agreements for the NB-IOT architecture
Agreed working assumption on NB-IOT architecture

## Slide 3: Agreements for NB-IOT(1)
R13 should support a non-IP bearer/transport service
SMS needs to be supported in battery efficient manner on NB-IoT - avoid establishment of DRBs when sending/receiving SMS - e.g. move to 2 radio interface messages (rather than 4) per SMS.
The specifications shall support that the NB-IoT control plane node CAN be physically separate from the legacy MME. - this does NOT preclude implementations where they are co-located or in the same node.

## Slide 4: Agreement on NB-IOT(2)
4. Attach without activating a Bearer Service is permitted - e.g. EMM only attach without any ESM signalling (as possible in 2G and 3G). - i.e. Attach without allocating any PDN/Serving GW - i.e. different to Rel 8 LTE (where PDN/bearer activation is mandatory)
- a Bearer Service may be activated any time after Attach

## Slide 5: Agreed working assumption on NB-IOT architecture
Solution 2 from TR 23.720 is a mandatory feature for UE and Network and a solution from 5/6/13 is an optional feature.