## Slide 1: Getting UE Usage type from HSS C4-151802 (S2-153746)
Discussion based on incoming LS C4-151802
NTT DOCOMO
S2-154098
TSG SA WG2 #112
16-20 November 2015, Anaheim, California, USA

## Slide 2: Background
For Decor MME needs to know the UE Usage Type (subscription parameter) from HSS BEFORE attempting to authenticate the UE.
SA2 had proposed to re-use “Update Location Request” with a new flag to get this info from HSS, without having the MME registered at the HSS.
CT4 created a new solution to re-use the “Authentication Request” with a new flag instead. (See C4-151802).
The decision on use of Auth Req/Response if not final in CT-4, based on meeting report (Draft CT4-70-meeting Report-000):
  If SA2 disputes CT4 AIR/AIA solution, CT4 will complete specification with ULR/ULA solution as specified in current TS 23.401 in Rel13 time frame.

## Slide 3: CT4 Concerns with ULR/ULA approach and Docomo Responses
Reasons given for not using ULA/ULA (see C4-151802)
  perverts the meaning and purpose of the current Update Location procedure
    ULR/ULA has two purposes: (i) register the new CN node in HSS, and (ii) respond with subscription information in ULA to the CN node. The Decor use is to enable (ii) and hence is no “perversion” of ULR/ULA procedure. There is no separate procedure for CN node to obtain only subscription information from the HSS.
  inefficient, that could be saved using other approaches in scenarios where the (first) new MME/SGSN needs to retrieve authentication vectors and the UE Usage Type;
    The reason that CN node requests UE Usage type from HSS is that it is not sure if the MME/SGSN should serve the UE. So there is a high probability that the MME/SGSN will not serve the UE based on receiving the UE Usage type. Hence, in large number of cases the authentication vectors will be wasted. This is much more inefficient, since this leads to additional processing on HSS (as the second new MME will again need to authenticated the UE) and also wastage of authentication vectors. If the MME/SGSN needs to get the UE Usage Type from HSS, it will typically not get authentication vectors along with the UE usage type, but after UE usage type has been received and the MME/SGSN has determined that it should serve the UE. There is no efficiency gain.
  risk of unwanted side-effects, for those cases where a serving node supporting DÉCOR, interacts with an HSS not supporting DÉCOR; in those cases, the HSS will ignore the “No registration” flag, and proceed with a normal Update Location.
    This is correct and must be avoided.

## Slide 4: DOCOMO/SA3 Concerns with Authentication Request/Response approach
Docomo has submitted a contribution to SA3 (S3-152448) for Nov 9-13 meeting to discuss these concerns:
  Wastage of security vectors and processing in HSS
    When security vectors are requested along with UE Usage Type and not used for authentication of the UE (eg. HSS does not support the new procedure, (first) new MME decides to redirect UE to Dedicated MME), then these security vectors are wasted and cannot be used. These vectors have to be deleted in the (first) new MME. Also, this increases processing load in HSS which created new vectors that are un-used.
  Violates separation of AuC from subscription info in HSS
    UE Usage type is a subscription parameter. In several cases the AuC is a separate secure component of HSS and this piggy-backing is requesting the AuC to go fetch data from the non-so-secure subscription portion of the HSS.
  Not any more efficient than ULR/ULA
    CT4 claimed that could be saved using other approaches in scenarios where the (first) new MME/SGSN needs to retrieve authentication vectors and the UE Usage Type.
    See previous slide
  perverts the meaning and authentication procedures.
    UE Usage type is a subscription parameter. In some cases only UE usage type and not authentication vectors are returned, which is not the purpose of authentication request/response.

## Slide 5: Unused Authentication vectors
UE
eNB
Old MME/SGSN
new MME
Dedicated MME
HSS
TAU Request
TAU Request
Context Request
Context Response (no UE Usage Type)
Reroute NAS Message Request (original TAU message, MMEGI for Dedicated CN)
Initial UE message (original TAU message, MMEGI for Dedicated CN)
Authentication Request(vectors, UE Usage Type Request)
Authentication Reply(vectors, UE Usage Type)
Context Request
Context Response
Context Acknowledge (NACK)
Update Location Request
Cancel Location Request
Cancel Location Acknowledge
Update Location Answer
bearer estb.
TAU Accept
Authentication / Security
Context Acknowledge
bearer deletion
Authentication Request(vectors)
Authentication Reply(vectors)
MME decides to re-route. Does not complete authentication procedure with UE.
Unused authentication vectors at new MME MUST be deleted.
Dedicated MME decides to authenticate UE. Gap in authentication vectors sequence number
Wasted Processing in HSS

## Slide 6: Solution Options (1of2)
Option-1: ULR/ULA with roaming configuration for Decor
  The main issue with the ULR/ULA approach is risk of unwanted side-effects, for those cases where a serving node supporting DÉCOR, interacts with an HSS not supporting DÉCOR; in those cases, the HSS will ignore the “No registration” flag, and proceed with a normal Update Location.
  This case is only present for roaming scenario. In non-roaming scenario this is not an issue, since both the HSS and MME/SGSNs need to be updated to support DECOR.
  To solve the solution, for roaming-scenarios, the MME/SGSN uses ULR/ULA only if it is configured to know that the the HPLMN also supports Decor.

## Slide 7: Solution Options (2of2)
Option-2: Create a new procedure
  We are impacting the HSS anyway and there is no existing procedure for MME/SGSN to request subscription parameters from the HSS.
  Decor is a key feature also for 5G.
  Create a new procedure (eg. “UE Usage Type Request/Response) to obtain this information from HSS and not impact existing procedure. If HSS supports this new procedure it will respond with the UE Usage Type, otherwise it will not.
  No side-effects, no perversions, new and clean.

## Slide 8: Way forward
SA2 agrees which option to use.
  Docomo has provided CR with both options. So select one.
Send LS to CT4 with the selected option and let CT4 update their specifications.