## Slide 1: Report of NextGen work status in SA2 on xRAN yCN Combinations
China Mobile, Nokia
(Rapporteurs)

## Slide 2: 1. Architecture Assumptions
The goal of NextGen Arch. SI is to study the system architecture and design a common NextGen Core
  Support the new RAT(s), the evolved LTE, and non-3GPP access types. GERAN and UTRAN is not supported.
  Allow independent evolutions of core network and RAN, and minimize access dependencies.
  A NextGen Core-NextGen RAN interface supporting new RAT(s) and the evolved LTE shall be specified.
    Editors note: interface support non-3GPP access if FFS.

## Slide 3: 2 Initial High Level Architecture and Reference points
SA2 agreed to the high level architecture used as a reference model for NextGen study.
The Initial High level architecture shows the NextGen UE, NextGen RAN, NextGen Core and their reference points.
NG1-C: Reference point for the control plane between NextGen RAN and NextGen Core.
NG1-U: Reference point for the user plane between NextGen RAN and NextGen Core.
NOTE1: The above reference point name follows TR 23.799 v0.4.0. They are subject to be updated in SA2#115 (NG1-C->NG2; NG1-U->NG3)
NOTE2: NextGen RAN connected to EPC is not in the scope of NextGen TR (not explicitly mentioned in the TR)

## Slide 4: 3 Related Definitions
Evolved LTE: it is E-UTRAN upgraded to interface with the Next Generation Core.
NextGen RAN (NG RAN): it refers to a radio access network that supports Evolved LTE and/or New RAT and interfaces with the Next Generation Core.
NextGen System (NG System): It refers to NextGen System including NG RAN and NextGen Core.
NextGen UE (NG UE): It refers to an UE connecting to the NG System.
Q1: SA2 would like to check the views of RAN on the definition on Evolved LTE and NextGen RAN (NG RAN). It is recommended to have a consistent understanding and terminology use across WGs.
Term be updated per S2-162955

## Slide 5: 4 Interworking and Migration
The interworking and migration of the NextGen system with EPC has been created as one key issue and will be studied by SA2.
SA2 observes that the RAN study will include deployment scenarios with both the New RAT and Evolved LTE (RAT) and stand alone deployments scenarios. Is this the correct understanding?

## Slide 6: 5. Time Plan of NextGen in SA2
SA2 targets to complete a baseline NextGen architecture study in Release 14 and normative work completed in Release 15.
  Its features can further be enhanced in Release 16.
Work is planned in SA2 for
  An early availability of basic system for trials and deployments that fulfils the goals and expectations set about for Next Generation of System including the Core Network.
  Building of a complete and feature rich system using the basic system defined in step 1 as a foundation thereby ensuring backwards compatibility within Next Gen Ecosystem.
  (from Annex C in NextGen TR 23.799)

## Slide 7: 6. Proposed Way Forward
Proposed Way Forward
  Achieve the common understanding on the terms - “Evolved LTE” , “NextGen RAN”.
  Kindly take SA2’s status and timeline for NextGen as a reference