## Slide 1: UE provided information for serving node selection in eDECOR
CATT
S2-164562

## Slide 2: Problem
UE
3GPP RAN
DCN1
DCN2
DCN3
……
HSS
(DCN1-ID, GUTI_1)
UE is currently associated with DCN1, DCN1-ID and GUTI_1 is stored in UE.
HSS changes the DCN type from DCN 1 to DCN 2.
DCN2-ID is changed and sent to the UE.
(DCN2-ID, GUTI_1)

## Slide 3: Problem
UE
3GPP RAN
DCN1
DCN2
DCN3
……
HSS
(DCN2-ID, GUTI_1)
UE sends TAU/RAU message, DCN2-ID and GUMMEI_1 which is obtained from GUTI_1 are included in RRC message for network selection.
RAN selects MME, GUMMEI_1 is take precedence over than DCN2-ID. Old MME in DCN 1 is selected for the UE.
Old MME in DCN1 triggers redirecting procedure, redirecting UE to DCN2.
MME in DCN2 send NAS response message to UE.
(1)
(2)
(3)
(4)
NAS redirect procedure cause more signaling and need to be avoid for MME/SGSN selection.

## Slide 4: Solution for E-UTRAN
UE
3GPP RAN
DCN1
DCN2
DCN3
……
HSS
(DCN2-ID)
UE sends TAU message only with DCN2-ID, no GUMMEI_1.
RAN selects MME based to DCN2-ID information
DCN2 is selected by RAN directly, no need to perform NAS redirect procedure.
(1)
(2)
(3)

## Slide 5: Difference between E-UTRAN and UTRAN
UE can obtain GUMMEI from GUTI, but UE can not obtain NRI from P-TMSI.
How to solve the problem in UTRAN/GERAN?
  Initial UE identity is mandatory in RRC CONNECTION SETUP message in TS 25.331
Information Element/Group name | Need | Multi | Type and reference | Semantics description | Version
Message Type | MP |  | Message Type |  | 
UE Information Elements |  |  |  |  | 
Initial UE identity | MP |  | Initial UE identity 10.3.3.15 |  | 
Initial UE identity could be
  TMSI
  P-TMSI
  IMSI
  IMEI

## Slide 6: Solution for UTRAN/GERAN
NNSF for SGSN in TS 23.236:
  If the NAS Node Selection Function has a CN node address configured for the NRI derived from the initial NAS signalling message or from the LLC frame then this message or frame is routed to this address. If no CN node address is configured for the derived NRI or if no NRI can be derived (e.g. the MS indicated an identity which contains no NRI) then the NAS Node Selection Function selects an available CN node (e.g. according to load balancing) and routes the message or LLC frame to the selected CN node.
If UE provide a UE identity that contains no NRI, e.g. IMSI to the RAN, RAN can derive a SGSN which is configured for the NRI and the DCN ID will be used for SGSN selection.

## Slide 7: Proposal
For E-UTRAN, if the DCN-ID is updated in the UE and a TAU is initiated, UE provides the new DCN-ID to the RAN and do not provide the old GUMMEI to the RAN. RAN will use the DCN-ID for MME selection.
For UTRAN/GERAN, if the DCN-ID is updated in the UE and a RAU is initiated, UE provides the new DCN-ID along with the UE identity that contains no NRI to the RAN. RAN will use the DCN-ID for SGSN selection.
Related proposal is captured in CR#3090.