## Slide 1: Proposal on NextGen Architecture Top-Down Approach
Deutsche Telekom AG
S2-163708

## Slide 2: Background
Current TR focuses on bottom up approach
  provides solutions to key issues with narrow scope to specific functional areas of the network
  not yet put into context of an overall architecture
  limited focus on the “common core” requirement
  aspects that span multiple KIs still need to be looked at
We believe a top down approach is also needed on architecture principles and solution approaches that
  create a common core network architecture capable of integrating multiple 3GPP and non-3GPP access technologies
  span over multiple KIs and/or don’t fit or are not already considered under existing KIs
  focus on minimizing access dependencies and creating a common core with a single AN – CN Interface
2

## Slide 3: NGMN 5G White Paper design goals and principles
    A converged access-agnostic core where identity, mobility, security, etc. are decoupled from the access technology
    Common AN – CN interface which integrates fixed and mobile accesses on an all-IP basis
    Minimize Legacy interworking, for example towards circuit switched domain in the 2G and 3G networks
    A rethink of models such as bearers, APNs, extensive tunnel aggregation and gateways is needed
    State information should be split from functions and nodes, so that contexts can be easily relocated and restored even in failure events
    The UE state machine and entities which store UE context should be revisited and redesigned
    Control and user plane functional split
    Minimize the Total Cost of Ownership (TCO)
    Options and possibilities for ultra-low cost deployments tailored for very low ARPU use cases

## Slide 4: Overall architecture and AN–CN interfacing
      NGMN preferred 5G architecture option
      “4G Evolution” (eNB supporting both EPC and 5G NW) provides coverage for both legacy UEs (using EPC) and 5G UEs (using 5G NW)
      Today’s existing 2G/3G/4G EPC-based system as well as fixed/WiFi systems may continue to exist with no impact from 5G
      RAN-level integration between LTE and/or NR and/or non-3GPP radio accesses to be addressed by RAN WGs

## Slide 5: Minimal High Level Architecture
UE
Minimal NextGen Core Network
Ctrl Plane
External Data Network
Application Functions (AF)
UE
Subscriber Repository
Authentication Function
User Plane
Access Network (AN)
UP GW / Forwarder
UE – AN User Plane
UE – AN Signaling (AS)
UE – CN Control Plane (NAS)
Network Signaling
Network User Plane
Controller

## Slide 6: High Level Architecture Principles
TCO-optimized system blueprint
communication (CP and UP) between UE and AN as well as AN internal communication is access specific
all other CP/UP communication and functions are access independent:
  User Plane GW / Forwarder routes service data flows between AN and external Data Network (e.g. Internet)
  CP controller programs flows into UP Forwarder based on subscriber profile
  Access independent subscriber repository and authentication function
  additional CN functions (QoS, charging, …) beyond this blueprint are needed in more demanding usage scenarios

## Slide 7: Example Optional Architectural Elements
functions
Application Functions (AF)
Forwarder
Subscriber Repository
QoS control
Policy / Charging
Mobility / Session Manager
Policy / Charging enforcement
QoS Assurance
Mobility / Session Anchor
Authentication Function
Controller
Minimal NextGen Core Network
User Plane
Control Plane

## Slide 8: Optional Architectural Elements Principles
Optional CN control plane functions are enabled on demand, as required by the specific customer use case, e.g. configuring the following functions per UE / flow:
  Quality of Service
  Charging
  Policy Control
  Mobility Management
  Session/Service Continuity
    with or without intra-AN mobility
    with or without AN change
CN user plane functions associated with the active CP functions can be chained into the user plane path
AF may be shared with external network, or exist exclusively within or outside of the operator domain

## Slide 9: Proposal
    Focus on re-design of items needed in order to achieve the common access-agnostic core and the single AN-CN I/F:
  QoS, bearers
  Mobility management
  Common security framework
  Non-AS signaling of the UE
  Common data layer for subscriber, context and state information