## Slide 1: Position of Network Slice Selection Function (NSSF) in overall architecture
NTT DOCOMO, Ericsson, LG Electronics
SA WG2 Meeting #119
13 - 17 February 2017, Dubrovnik, Croatia

## Slide 2: NSSF definition
We have proper definition for the Network Slice Selection Function (NSSF)?
  No.
    Before defining the NSSF definition, first we should understand the network slicing definition
Definition from TR 23.799:
At present, we have inter-linked definitions between NS NSI  NST.
In the end, network slice is nothing but a set of network functions formed as a slice (group) and which provides specific business/telecom services
  By this, selecting a slice is nothing but a selecting set of network functions
NSSF selects the set of network functions of a slice based on NSSAI, which is provided by UE or network.
Network Slice (NS): is a concept describing a system behaviour which is implemented via Network Slice Instance(s). Network Slice Instance (NSI): is an instance created from a Network Slice Template (NST). Network Slice Template (NST): is a logical representation of the Network Function(s) and corresponding resource requirements necessary to provide the required telecommunication services and network capabilities.

## Slide 3: Slice selection by NSSF
If a UE provides no NSSAI in RRC and NAS, and the RAN sends NAS signaling to a default CCNF (TR conclusion)
Default CCNF selects the dedicated/slice specific CCNF#1 and re-route* the request to CCNF#1
  NSSF in default CCNF selects the CCNF#1
After, NSSF in CCNF#1 selects the slice specific SMF based on S-NSSAI
NSSF selects the both CCNF (AMF) and SMF functions as a set of network functions
CCNF#1
(AMF, NSSF)
SMF1
SMF2
UPF1
UPF2
Default CCNF
(AMF, NSSF)
Group B architecture
RAN
*Note: Re-route can be via RAN or direct communication between CCNFs. In above figure, we showed via RAN option.
2
1

## Slide 4: Position of NSSF in overall architecture
TR 23.799 conclusion on network slicing
In overall architecture, we not concluded the position of Network Slice Selection Function (NSSF)
Possible NSSF position options:
    NSSF as a separate and independent function
      NSSF placed as independent function and other network functions are communicated via standardized interface
    Co-located with AMF
      NSSF is co-located with AMF
      AMF selects the slice in addition to the SMF selection
    Co-located with NRF
      In addition to the network function discovery, NRF will also selects the network slice
4. A UE may access multiple slices simultaneously via a single RAN. In such case, those slices share some control plane functions, e.g. AMF and Network Slice Instance Selection Function. These common functions are collectively identified as CCNF (Common Control Network functions). 5. The CN part of network slice instance(s) serving a UE is selected by CN not RAN. 5a. The NSSF is one function of CCNF, which is a set of NFs including the AMF and the NSSF, and is used to select the NSI for the UE.

## Slide 5: Opt#1. NSSF as a separate and independent function
Pros
  Centralizing the NSSF, the slice selection management will be easier, any changes in the slice configuration, need to update only one NSSF
Cons
  Scalability issues: NSSF may encounter with bottlenecks and single point of failure
  High latency: distributed AMFs need to communicate with centralized NSSF for slice selection, which increases the latency to perform slice selection. Latency is crucial for mission-critical application
  Signaling overhead: back and forth extra signaling from AMF and NSSF, which generate more signaling overheads in the network especially in the control plane
  New Interfaces
    With AMF: SA2 need to standardized a new interface between AMF and NSSF, which leads to overall architecture impact
    With UDM: NSSF need an interface with UDM in order to extract the UE subscription data and select based on the subscription
    With NRF: NSSF may also required an interface with NRF in order to discovery the NFs (i.e. AMF, SMF, etc.,)
NSSF
AMF1
AMF2
AMF3
AMF4
Centralized location
Distributed location
UDM

## Slide 6: Opt#2. NSSF is Co-located with AMF
TS 23.501 conclusion on SMF Selection
Pros
  AMF already incorporated NSSF functions e.g. AMF selects the SMF function based on S-NSSAI (Clause 6.3.2 in TS 23.501).
  SA2 doesn’t required to standardize new interfaces and doesn’t have overall architecture impact
  Doesn’t required extra signaling for selection of a slice and their functions
  Slice selection is much faster, since it doesn’t required to communicate with external entity like Opt#1 i.e. communicated latency reduced
Cons
  Management complexity increases, since any changes in the slice configuration, operator need to update respective effected AMFs
Clause 6.3.2 SMF selection function The SMF selection function is supported by the AMF and is used to allocate an SMF that shall manage the PDU Session. The SMF selection function in AMF is applicable to both 3GPP access and non-3GPP access. The following factors may be considered during the SMF selection: Selected Data Network Name (DNN). S-NSSAI. EN: It is FFS what other information may be considered for SMF selection. It is also FFS what parts of S-NSSAI is considered, e.g. whether both SST and ST is used or only SST.

## Slide 7
Clause 6.2.6
  NRF is a service discovery function. Receive NF Discovery Request from NF instance, and provides the information of the discovered NF instances (be discovered) to the NF instance.
Pros
  Doesn’t required new interface and overall architecture will not be impacted.
  AMF utilizes the NRF to discover the SMF instance (clause 6.3.2), existing discovery mechanism required to enhance in order to select the network slice in addition to function discovery
Cons
  NRF is design to discovery the network function, for slice selection significate impact to the existing NRF terminology and also may required to new selection features
  If NRF already does selection of slice and their functions, it has significate impact to AMF (AMF already support the selection of SMF, which doesn’t required any more)
Opt#3. NSSF is co-located with NRF

## Slide 8
After evaluation of these possible options, Opt#2 (i.e. NSSF is part of AMF) as a way forward for NSSF position, since
  AMF shall select the SMF based on parameter defined in clause 6.3.2
  AMF already support of slice selection mechanism based on S-NSSAI
  Doesn’t have overall architecture impact
  SA2 doesn’t required to standardize a new NSSF, selection function in AMF can be enhanced if there are any missing function/procedure required
Conclusion