## Slide 1: Background information on Architectures 3/3a/3x and Dual Connectivity
Source: Vodafone
SA WG2 Meeting #120 March 27 – 31, 2017, Busan, Korea
Agenda item: 6.14
Tdoc S2-172281

## Slide 2: Terminology
Xx
  “The interface allowing to interconnect EPC connected gNB and LTE eNB, is referred to as the Xx interface”
  RAN 3 TR 38.801, v2.0.0, clause 10.1.2.1
Xn
  “The interface allowing to interconnect two gNBs or one gNB and one eLTE eNB with each other is referred to as the Xn interface. The interface Xn is also applicable for the connection between two eLTE eNBs”
  RAN 3 TR 38.801, v 2.0.0, clause7.4.1.1
Definitions in TR 38.801 v2.0.0
  eLTE eNB: The eLTE eNB is the evolution of eNB that supports connectivity to EPC and NGC.
  gNB: A node which supports the NR as well as connectivity to NGC. NOTE : The definitions of gNB and eLTE eNB may require revision in the normative phase.

## Slide 3: Option 3: - E-UTRAN splits EPS bearer between eNB master cell and «new radio» secondary cell - c.f. Release 12 Dual Connectivity Alternative 3C (section 8.1.1.8, TR 36.842)
eNB
Master Cell Group
RLC-LTE
MAC-LTE
PHY-LTE
PDCP-LTE
S1-MME
S1-U for EPS bearer “j”
gNB
Secondary Cell Group
RLC-NR
MAC-NR
PHY-NR
PDCP-NR
Xx user plane
Xx control plane
UE uses PDCP-LTE for EPS bearer “j”

## Slide 4: Option 3a: - E-UTRAN instructs MME to route EPS bearer to «new radio» secondary cell. - Only secondary cell radio resources used for that EPS bearer - c.f. Release 12 Dual Connectivity Alternative 1A (section 8.1.1.1, TR 36.842)
eNB
Master Cell Group
RLC-LTE
MAC-LTE
PHY-LTE
PDCP-LTE
S1-MME
S1-U for EPS bearer “k”
gNB
Secondary Cell Group
RLC-NR
MAC-NR
PHY-NR
PDCP-NR
Xx control plane
UE uses PDCP-NR for EPS bearer “k”
As Rel 8 S1-AP allows independent eNB IP addresses for S1-MME and S1-U, the MME is unaware whether the EPS bearer terminates on eNB or gNB

## Slide 5: Option 3x: - E-UTRAN instructs MME to route EPS bearer to «new radio» secondary cell. - gNB splits EPS bearer between eNB master cell and «new radio» secondary cell - no direct Rel 12 DC equivalent. From MME side, looks like DC-1A
eNB
Master Cell Group
RLC-LTE
MAC-LTE
PHY-LTE
PDCP-LTE
S1-MME
gNB
Secondary Cell Group
RLC-NR
MAC-NR
PHY-NR
PDCP-NR
Xx user plane
Xx control plane
UE uses PDCP-NR for EPS bearer “m”
As with 3a, MME is unaware whether S1-U terminates on eNB or gNB
S1-U for EPS bearer “m”

## Slide 6: TS 23.401 changes for Release 12 Dual Connectivity
Clause 4.3.2a Support for Dual Connectivity
  general description
  some impacts on CSG, LIPA, SIPTO, relaying
  eNB seems able to respond to MME’s S1-AP Initial Context Setup request with S1-U termination point of a Secondary Cell
5.4.7 E-UTRAN initiated E-RAB modification procedure
  Used by the master eNB to move the RAN termination point of an EPS bearer without moving the S1-U termination point
5.4.8 E-UTRAN initiated UE Context Modification procedure
  Currently only used by master eNB to verify CSG membership

## Slide 7: Other points to consider
(per UE and) Per EPS bearer choice of 3 / 3a / 3x ?
  It seems to be allowed that the master eNB can select on a per EPS bearer basis
  At least with 3a, it should be expected that
    RRC signalling between master eNB and UE uses PDCP-LTE, while
    User plane between gNB and UE uses PDCP-NR
  Implying that UE can simultaneously use more than of choice of PDCP
  Example use case for this: - IMS signalling (QCI=5) and IMS voice (QCI=1) bearers could be “locked” (by eNB configuration files) to use E-UTRAN (which sort of looks like option 3 to the MME), while - the eMBB bearer on QCI 8 could be connected to the 5G secondary cell group (looking like option 3a or 3x to the MME)
RAN 3 Centralised Unit / Distributed Unit functional split
  With a Centralised Unit (potentially shared between E-UTRAN and NR) it becomes a bit less clear whether that CU is an eNB or a gNB
  but this does seem to matter from an SA2 point of view

## Slide 8: End