## Slide 1: Cellular IoT evolution towards 5G requirements
SA WG2 Meeting #120 S2-171815 23 - 27 March 2017, Busan, South Korea

## Slide 2: Background
Substantial recent E-UTRAN/EPC evolution for IOT (particularly Rel-13/Rel-14):
  RAN: eMTC and NB-IoT.
  SA: Cellular IOT (Rel-13) and CIOT_ext (Rel-14):
    E.g. CP optimizations, UP optimizations, non-IP data, SCEF, reliable communication via SCEF, etc…
    EPC CIoT features apply (with little differences) to NB-IoT and WB-E-UTRAN (eMTC).
RAN agreement for 5G:
  Use NB-IoT and eMTC as baseline for 5G submission to ITU.
On one hand:
  There needs to be a natural evolution of C-IOT in EPC.
    At least to support the evolution of NB-IoT and eMTC.
  Also, some operators have shown interest in leveraging the newly standardized technology (e.g. NB-IoT + EPC/CIOT)
    Interest to evolve NB-IoT/EPC to cover the “5G IOT” requirements (confirmed in RAN).
    It would be useful to study which (and how) 5G service requirements can be supported by EPC.
On the other hand:
  The 5G CN should also support IOT:
    Enable the possibility to connect WB-E-UTRAN/eMTC and NB-IoT to 5G CN.
    Meet the 5G requirements for IOT as defined by SA1, and support in the CN of the RAN requirements.
    Also, a new CN that provides less features than the existing one is less attractive.

## Slide 3: Qualcomm proposal
As a standards body, 3GPP should provide full flexibility to operators to evolve their network deployments while providing valuable IoT services.
Ultimate goal:
  Reach Feature Parity between EPC and 5C CN for IOT.
  Best of both worlds
    Operators choosing to deploy NB-IoT/eMTC with EPC/CIOT can leverage their deployment for IOT through natural evolution of EPC, and meet the 5G requirements.
    Operators that want to migrate to 5G CN to have standardized solutions to provide IoT service via their 5G CN deployment.
Timeline:
  Both EPC enhancements for IOT and 5G CN Cellular IOT can be studied in Rel-15.
  Normative work for 5G CN to be completed by Rel-16.
  EPC enhancements for IOT to be completed by Rel-16.

## Slide 4: Two approaches to meet the Feature Parity Goal
Approach 1: Fully parallel approach:
  SID on EPC further enhancements for IoT
    Based on IOT requirements for 5G (no new SA1 study/work needed)
    Study gaps of current C-IoT solution with IoT requirements for 5G.
    Study solutions for that gap.
  SID on IOT support in 5G CN
    Transport (with relevant modification) CIoT features.
      Leveraging the CIOT design for EPC when possible. Study gaps of current C-IoT design with IoT requirements for 5G.
    Additional feature addition/ optimizations for IoT based on identified gaps.
    NOTE: This should not be an open ended study on IoT:
      Very valuable recent progress and conclusions done during C-IOT work should not go to waste.
      Open ended studies have proved inefficient.
Approach 2: Only one SID: Transport C-IoT to 5CN + study further enhancements for EPC/5G CN together
  Main Objective 1: Transporting C-IoT features to 5G CN.
    Quick study on transporting all C-IoT features to 5G CN to achieve “Rel-14 parity”
  Main Objective 2: Core Network enhancements to meet 5G requirements on top of C-IoT.
    Study gaps of current C-IoT solution with respect IoT requirements for 5G.
    Study enhancements for 5G CN and EPC.

## Slide 5: Other approaches that do not meet the Feature Parity goal
Approach 3:
  Evolve only EPC, and support IoT service requirements only for EPC.
  This prevents Operators that want to migrate to 5G CN to have standardized solutions to provide IoT service via their 5G CN deployment connecting to NB-IoT/eMTC RAN.
    This lack of feature support could even be a deterrent for operators to deploy 5G CN.
  Not acceptable approach to Qualcomm.
Approach 4:
  Leave EPC as it is now.
  Have only one SID for IOT in 5G CN.
  This prevents operators that will deploy NB-IoT/eMTC with EPC Cellular IoT solution to leverage their deployment and evolve to new service requirements.
  Not acceptable approach to Qualcomm.

## Slide 6: Qualcomm preference: Approach 2
Benefits of Approach 2:
  Leverages recent knowledge/discussions/conclusions accumulated through multiple releases in the field of IoT.
    5G CN feature parity with Rel-14 C-IoT/EPC can be achieved with relatively minor effort, compared to an open ended discussion which could make 5G CN not get fully up to speed with EPC for IOT, even in Rel-16 timeframe.
  Study on gaps of C-IoT with respect to 5G IoT requirements is not repeated:
    No duplicated effort on an already tight schedule.
    No risk of having incompatible conclusions in separate studies (and therefore no risk of not reaching feature parity for IoT between EPC and 5G CN).
Qualcomm can also accept Approach 1:
  Although potentially there could be repetition of work from two separate SIDs, it could still (with enough coordination between SIDs) achieve feature parity.
Qualcomm cannot accept Approach 3 nor Approach 4.

## Slide 7: Example on “C-IoT Transporting to 5G CN” effort: SCEF
Goal:
  Maintain service parity when possible.
  Adapt architecture/procedures to 5G CN.
Achieved by:
  Same SCEF northbound interface (S8) for EPC and 5G CN.
  Adapt southbound interface:
    To MME:
      Option1: Split to AMF and SMF
      Option 2: Only to AMF
    To HSS -> To UDM
    To PCRF -> To PCF

## Slide 8: Further considerations for Main Objective 2: Core Network enhancements to meet 5G requirements on top of C-IoT
There are two sources of requirements on top of Cellular IOT:
  Source 1: RAN evolution of NB-IoT and eMTC
    System Architecture requirements caused by RAN evolution are common for EPC and NB-IoT.
  Source 2: Service requirements for 5G IoT (SA1 SMARTER).
    These clearly apply to 5G CN.
    It should be evaluated also for each of these service requirements whether and how it could adopted via EPC.