## Slide 1: N2TP and AMF selection Issues and solutions for N2 persistence control
Deutsche Telekom

## Slide 2: N2 Persistence Control (Option 1 of S2-172812)
N2 Termination Point (N2TP) is representative for the communication between AMF and (R)AN
Assignment of Resources is done inside the AMF in a vendor specific manner
Issues:
  “big” single-vendor AMF
  Same mechanics of AMF (re)selection as in 4G
AMF
(Vendor specific)
N2TP
AMF Resource
#1
AMF Resource
#2
AMF Resource
#n
…
N2

## Slide 3: N2 Persistence Control (Option 2) N2AP UE-TNLA-binding
“An AMF shall be able to change the N2AP UE-TNLA-binding, i.e. change the TNL association for the UE in CM-Connected mode at any time.“
This solution externalises the behaviour of Option 1 towards the (R)AN, causing additional signalling
Triangular or Re-Route via (R)AN result in signalling between UE, (R)AN and the respective AMF instances
Triangular redirection
Re-route via RAN

## Slide 4: N2 Persistence Control (new Option 3)
Option 3 is similar to Option 1
N2TP is extracted from (v)AMF
Interaction between N2TP and AMF Resources needs to be standardised for multi-vendor deployments of AMF Resources
UE and associated (R)AN only know the N2TP, whereas different AMF Resources may exist “behind” that N2TP
N2TP
AMF Resource
#1
AMF Resource
#2
AMF Resource
#n
…
N2
I/f N2TP – AMF Resource

## Slide 5: Conclusion
Option 1 of S2-172812 may be acceptable in a single-vendor deployment if the vendor assures in the implementation that any change of AMF Resource is done without interruptions or additional signalling towards (R)AN or UE
Option 2 of S2-172812 introduces more signalling without any obvious advantage over option 1 and should be avoided
Option 3 keeps changes of AMF Resources completely transparent to the UE and the (R)AN while allowing multi-vendor deployments and avoiding any associated signalling
N2TP – AMF Interface needs to be standardised to support option 3