## Slide 1: S2-176927
OI#19 – EPC-5GC interworking for N3GPP access
Discussion paper
Nokia, Nokia Shanghai Bell, Samsung
<Change information classification in footer>

## Slide 2: EPC IWK for N3GPP
An UE is attached to 5GC and moves between patchy 5G, patchy WLAN and almost ubiquitous 4G coverage. Assumptions are: a) when the 5G-UE is attached to 5GC via WLAN, it should select an N3IWF (rather than an ePDG). b) it is assumed that selecting an N3IWF is independent from whether the UE is attached to 5GC, EPC or no 3GPP coverage
  This is obvious when there is no 3GPP coverage
  The 5G-UE user expects to get SMS service even if under WLAN coverage only
  c) Operators that have deployed ePDGs with location based selection may update their ePDG into N3IWF/ePDG step by step (see slide 7).
Use case description
WLAN (via N3IWF)
5GS
4GS
5GS
5GS
5G UE
WLAN
4GS
To be specified
To be specified
To be specified

## Slide 3: EPC IWK for N3GPP
When 5G-UE moves between NR and WLAN in the same PLMN, the same AMF can be used. -> This minimizes the accesses to AUSF and UDM as full authentication is not required (If the UE would have selected an ePDG, authentication would be required for both 5G to/from WLAN and EPS to WLAN mobility)
Services such as SMS over NAS are still supported when accessing Core Network via N3IWF even if no access via 3GPP radio. This is not possible via ePDG, which requires SMS over IMS
Unlike ePDGs, there is no need for 3GPP AAA servers since N3IWF is connected to AMF that handles authentication towards AUSF
N3IWF-EPS mobility can be supported with existing procedures: -> For N3IWF to EPS: regular EPC procedures for WLAN handover -> For EPS to N3IWF: regular 5G N3GPP registration + PDU establishment procedure
Advantages for accessing Core via N3IWF rather than via ePDG

## Slide 4: EPC IWK for N3GPP
Reference architecture
Same reference architecture as for NR

## Slide 5: EPC IWK for N3GPP
Handover from "5GC-WLAN" (i.e. connected to 5GC via N3IWF) towards EPS
* only once since MME UE context will not be deleted when the UE goes to the other RAT
N3IWF
RAN
HSS/UDM
2c- Location Update (retrieve of SMF ID) (*)
3- Create Session Rq
4- Create Session Resp
5- Namf-com-N1N2-Msg-Transfer [N2 SM Release Rq]
6- N2 SM Release Rq
7- N2 SM Release Ack
8- Nsmf-PDUsession-UpdSMC-Context Rq [N2 SM Release Ack]
9- Nsmf-PDUsession-UpdSMC-Context Resp
2b- Authentication & Authorization (*)
2a- Authentication & Authorization
5- Initial Context Setup Rq [NAS Attach Accept]
6- Initial Context Setup Resp
6- RRC [NAS Attach Accept]
EPS procedure for WLAN to EPS mobility
Regular 5GC release procedure
UE
MME
SGW
SMF/ UPF
AMF
1- NAS Attach (handover flag)

## Slide 6: EPC IWK for N3GPP
Handover from EPS to 5G-WLAN" (i.e. WLAN connected to 5GC via N3IWF)
UE
AMF
SGW
SMF/ UPF
MME
.
1- IKE_AUTH [NAS Registration Rq]
RAN
N3IWF
HSS/UDM
6- Regist/Subscript Retrieval (SMF-ID) (*)
2- N2-msg [NAS Registration Rq]
11- Delete Bearer Request
12- UE Context Release Command
13- UE Context Release Complete
7- Nsmf-PDUsession-Create SMContext Req
2b- Authentication & Authorization (*)
2a- Authentication & Authorization
3- IPSec establishment
4- IPsec [NAS Registration Accept/Complete]
5- IPsec [NAS PDU Session Establishment Req]
9- Child SA setup for UP
10- IPsec [NAS PDU Session Establishment Accept]
8- Nsmf-PDUsession-Create SMContext Resp
14- Delete Bearer Response
Regular 5G N3GPP registration + PDU establishment procedure
Regular EPS release procedure
* only once since AMF UE context will not be deleted when the UE goes to the other RAT

## Slide 7: N3IWF selection
If the UE is 5G capable, it should try to select an N3IWF (because of the advantages described in slide 3). If the UE is 4G capable, it shall try to select an ePDG per TS 23.402.
For operators having deployed ePDGs and using TA-location discovery: it is assumed that the operator will upgrade their ePDG into (N3IWF+ePDG) step by step. Several migration schemes can be foreseen:
  The operator prefers that the UE selects an N3IWF: In this case, the 5G capable UE uses TA-location discovery to find the closest N3IWF. If there is no N3IWF in the PLMN, the UE selects the closest ePDG.
  The operator prefers that the UE selects the closest node (N3IWF or ePDG). In this case, the 5G capable UE uses TA-location discovery to find the closest node. If there is a N3IWF in the closest TA, the UE selects the N3IWF.
Selection of the "Core Network Access Node via non-3GPP access" can be done the following way:
  The UE constructs a Tracking/Location Area Identifier FQDN for N3IWF selection and queries the DNS server;
  If no N3IWF were found, the UE constructs a Tracking/Location Area Identifier FQDN for ePDG selection as described in TS 23.402;
  If the UE has been configured by its home operator for the AN selection with "N3IWF preferred", the UE selects the closest N3IWF from the PLMN it is located in. If no N3IWF were found in the PLMN the UE is located in, the UE selects the closest ePDG;
  If the UE has been configured by its home operator for the AN selection with "closest node preferred", the UE selects the closest N3IWF or ePDG node. The UE shall prefer an N3IWF node.
  Note that the N3IWF selection information has precedence over the ePDG selection information.

## Slide 8: N3IWF selection
In the case the UE has selected an ePDG, the UE will have seamless mobility with EPS, but not seamless mobility with 5G.
As the Tracking Area Identity based ePDG FQDN is constructed as: "tac-lb<TAC-low-byte>.tac-hb<TAC-high-byte>.tac.epdg.epc.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org"
  , the TAI based N3IWF FQDN can be constructed as e.g. : "tac-lb<TAC-low-byte>.tac-hb<TAC-high-byte>.tac.n3iwf.5gc.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org"

## Slide 9: N3IWF selection
If an ePDG has been enhanced to support both N3IWF and ePDG functions, then it should know whether it has to operate as an N3IWF or as an ePDG. This could be done via several ways (to be defined):
  The different (public) IP addresses (there are separate FQDNs, so it is possible)
  After the IKE SA_INIT exchange, the combined ePDG/N3IWF can detect that the UE is 5G by looking in the IKE-AUTH Request message, at:
    Either a specific "Registration Parameter" (there is already the SUPI/GUTI and NSSAI) that is conveyed together with the NAS Registration Request message
    Or to the NAI (another possibility would be to append <5G> to the NAI, used for the ID. But it is not nice to have a NAI that would depend on the access technology.
   Specific registration parameter is proposed