## Slide 1: Proposal of an Rel-16 SID on the Enhancement to 5GC LoCation Services
CATT
S2-178369
3GPP TSG SA2 WG Meeting #124
Reno, USA, Nov. 27th –Dec. 1st , 2017

## Slide 2: Current Status for LCS Architecture Discussion
Option A: by Nokia during the CC#1
  PtP based, E-SMLC is extended to support location services for 5G-AN; (S2-178505 in SA2#124)
Option B: by Ericsson, etc. (S2-177590 in SA2#123) (S2-178340/41 in SA2#124)
  SBI based, but still uses SLh between UDM and GMLC. Now, Full SBI based!
  Location related function is majorly located in AMF.
  LMF is similar to E-SMLC
Option C: by Qualcomm, etc (S2-177591)
  Full SBI based,
  Location related function is majorly located in LMF.

## Slide 3: Observations on LCS in Rel-15 and Possible Way forward (1)
Observation 1: What is agreed:
  In Rel-15, LCS support requirements of regulatory is a must have;
    This is in line with NR WD (RP-172115).
  Keep existing protocols developed outside of 3GPP, i.e. Le and Lr reference point unchanged.
  LCS for commercial support deferred to Rel-16.
Observation 2: What is not concluded:
  Select which option (a or b or c) for Rle-15 LCS architecture?
    Majority company in favor of SBA for LCS
  How to do function split if option b or c is select as way forward?
  How to precede the stage 2 work once SBA-LCS was select?
    Outsource to stage 3 WGs, or
  Still under SA2, but maybe one month Exception?
Observation 3: Possible Way forward in Rel-15:
  An SBA based LCS architecture, corresponding SBI definition, will be specified in Rel-15, for regulatory services.

## Slide 4: Observations on LCS in Rel-15 and Possible Way forward (2)
Observation 4: Non-3GPP Access and IMS Emergency:
  Un-trusted Non-3GPP access and IMS services (including support for emergency calls) are within REL-15 5GS-Ph1 WID scope;
    Nokia already prepared P-CRs, on Emergency IMS support over un-trusted WLAN, and How NFs provide Locations Information;
    LCS support for EMC IMS over un-trusted NON 3GPP will be specified in Rel-15;
  Trusted Non-3GPP access are deferred to Rel-16;
    The Trusted Non-3GPP access Architecture design work contained in SID 5WWC(SP-170380);
    The SID ATSSS (SP-170411) also rely on the output of 5WWC when considering steering, switch, splitting traffic between trusted non-3GPP access;
    Location Services support for Trusted Non-3GPP access should be studied and fulfilled in Rel-16;

## Slide 5: An SID Proposal for enhancement to 5GC-LCS in Rel-16
Justification:
  Enable full support of LCS requirement defined in TS22.261 and TS22.071;
Some Thoughts:
  In general, enhancement to Service based Architecture for LCS specified in Rel-15 is preferred;
Objectives:
  Fulfill requirements defined in SA1 TS22.261 and TS22.071 but not achieved in Rel-15, e.g. commercial LCS, etc.
    Via enhancing existing architecture;
    Minimize the impacts to existing NF;
    Compatible with Rel-15 UE;
    No impacts on reference point which is NOT defined by 3GPP;
    Both 3GPP access and Non-3GPP access are considered:
  Phased work suggested:
    From UE access perspective, Firstly, study will focus on both 3GPP access and Un-trusted Non-3GPP access connect to 5GC;
    Secondly, begin consider how to support LCS for trusted non 3GPP access once its architecture has been defined;

## Slide 6: Tentative Work plan and TU allocation
Meetings | Major tasks | TU requirement
Jan/Feb | Skeleton, scope of TR. Gap analyses, Propose key issues, possible some solutions, | 1 for Jan 2 for Feb
April/May | Propose solutions, initial evaluation of each solutions; Key issue will not be accepted in May meeting. | 2 each
July/Aug | Finish evolution of solutions, and Conclude on which solution could be go to normative phase. Propose an WID. | 2 each

## Slide 8: Objective of Positioning in RP-172215 (NR WID)
Support of positioning to comply with regulatory requirements:
  via RAT independent and E-UTRA RAT dependent positioning schemes, including:
    - Transport of LPP messages between 5G-CN and UE through gNB [RAN2];
    - Transport of LPPa type messages between 5G-CN and NG-RAN hosting E-UTRA (eNB) [RAN2, RAN3];
NOTE: This objective is intended for the architecture options 4 and 7, and can be reused for option 5.
    - Support of measurement gaps and idle periods for location related inter-RAT measurements [RAN4, RAN2].
NOTE: This objective strives for common design of NR parts of inter-RAT measurement between NR and E-UTRA
  via network based NR CID and cell portion positioning, including:
    - Definition of messages and transport between 5G-CN and NG-RAN hosting NR (gNB) [RAN3, RAN2].