## Slide 1: Discussion on Handover between 3GPP and N3GPP via different PLMN
3GPP SA WG 2 Meeting#124
27 November – 1 December, Reno, USA
Source: LG Electronics
Title: Discussion on Handover between 3GPP and N3GPP via different PLMN
Document for: Discussion
Agenda Item: 6.5.10 Non-3GPP access specific functionality and flows
Work Item / Release: 5GS_Ph1 / Rel-15
S2-178614
LG Electronics

## Slide 2: Non-roaming case
Figure 4.2.8.2.1-1: Non-roaming architecture for 5G Core Network with non-3GPP access

## Slide 3: Non-roaming case
PDU Session Establishment over 3GPP access
UE
AMF
UDM
H-SMF
N3GPP
access
N3IWF
① PDU Session Establishment Request (Initial request)
(New PDU Session ID, DNN)
② Select new SMF
⑤ SMF Identity/Address
PDU Session ID
DNN
(Nudm_UEContextManagement_Registraion)
3GPP
access
④ PDU Session Establishment Request
H-UPF
③ The AMF stores an association of the PDU Session ID and the SMF ID.

## Slide 4: Non-roaming case
PDU Session Handover from 3GPP access to N3GPP access
UE
AMF
UDM
H-SMF
3GPP
access
N3GPP
access
N3IWF
① PDU Session Establishment Request
(Existing PDU Session)
(Existing PDU Session ID, DNN)
③ PDU Session Establishment Request
H-UPF
② Select the serving SMF associated with the PDU Session ID

## Slide 5: Home-routed Roaming via different PLMN case
Figure 4.2.8.2.5-1: Home-routed Roaming architecture for 5G Core Network with non-3GPP access - N3IWF in the different VPLMN from the 3GPP access

## Slide 6: Home-routed Roaming via different PLMN case
PDU Session Establishment over 3GPP access
UE
AMF1
UDM
H-SMF
VPLMN1
HPLMN
V-SMF1
N3GPP
access
AMF2
N3IWF
V-UPF1
H-UPF
② Select new SMF
3GPP
access
④ PDU Session Establishment Request
① PDU Session Establishment Request (Initial request)
(New PDU Session ID, DNN)
③ The AMF stores an association of the PDU Session ID and the SMF ID (H-SMF)
⑤ SMF Identity/Address
PDU Session ID
DNN
(Nudm_UEContextManagement_Registraion)

## Slide 7: Home-routed Roaming via different PLMN case
PDU Session Handover from 3GPP access to N3GPP access
UE
AMF1
UDM
H-SMF
VPLMN1
HPLMN
V-SMF1
N3GPP
access
AMF2
N3IWF
V-UPF1
H-UPF
3GPP
access
① PDU Session Establishment Request (Existing PDU Session)
(Existing PDU Session ID, DNN)
② SMF Identity/Address
PDU Session ID
DNN
(Nudm_???)
1. Which service operation is used to get SM context of the UE?
2. Does AMF get all PDU information or only a specific (HO requested) PDU information?
④ PDU Session Establishment Request
③ Select the serving SMF associated with the PDU Session ID (i.e. H-SMF)

## Slide 8: Possible solutions
1. Which service operation is used to get SM context of the UE?
  When storing session information, Nudm_UEContextManagement_Registraion is used.
  We propose to use Nudm_UEContextManagement_Get
    Need to update the service operation
NF service | Service Operations | Operation Semantics | Example Consumer(s)
Subscriber Data Management (SDM) | Get | Request/Response | AMF, SMF, SMSF
 | Subscribe | Subscribe/Notify | AMF, SMF, SMSF
 | Unsubscribe | Subscribe/Notify | AMF, SMF, SMSF
 | Notification | Subscribe/Notify | AMF, SMF, SMSF
UE Context Management (UECM) | Registration | Request/Response | AMF, SMF, SMSF
 | DeregistrationNotification | Subscribe/Notify | AMF
 | Deregistration | Request/Response | AMF, SMF, SMSF
 | Get | Request/Response | NEF
 | Update | Request/Response | AMF, SMF
UE Authentication | Request | Request/Response | AUSF
EventExposure | Subscribe | Subscribe/Notify | NEF
 | Unsubscribe |  | NEF
 | Notify |  | NEF
Table 5.2.3-1: NF Services provided by UDM
5.2.3.2.4 Nudm_UE ContextManagement_Get
Service operation name: Nudm_UEContextManagement_Get
Description: The NF consumer requests the UDM to get the NF ID of the NF serving the UE or SM UE Context.
Example NF Consumers: NEF, AMF.
Inputs, Required: UE ID, NF Type, Access type
Inputs, Optional: None.PDU Session ID
Outputs, Required: SUPI, NF ID of the NF corresponding to the NF type requested by NF consumer.
Outputs, Optional: None.NF ID of the NF corresponding to the NF type requested by NF consumer, SM UE Context (e.g. SMF identity / address)

## Slide 9: Possible solutions
2. Does AMF get all PDU information or only a specific (HO requested) PDU information?
  The AMF need to retrieve PDU Session information whenever the UE requests handover of a PDU Session because
    the AMF serving one access is not notified when the other access' PDU Session information stored in the UDM is changed for the case which 3GPP access and N3GPP access are in different PLMNs.
      For example, SMF address/identity might be changed due to the SSC mode procedure.
    Retrieving all PDU Session information is not efficient because UE may not request handover of all PDU Sessions
  We propose the AMF get a specific PDU Session information by indicating PDU Session ID requested by the UE.

## Slide 10: Home-routed Roaming via different PLMN case
PDU Session Establishment over 3GPP access
  Established as a LBO
UE
AMF1
UDM
H-SMF
VPLMN1
HPLMN
V-SMF1
N3GPP
access
AMF2
N3IWF
V-UPF1
H-UPF
3GPP
access
① PDU Session Establishment Request (Initial request)
(New PDU Session ID, DNN)
② The AMF stores an association of the PDU Session ID and the SMF ID (V-SMF1)
④ SMF Identity/Address
PDU Session ID
DNN
(Nudm_UEContextManagement_Registraion)
③ PDU Session Establishment Request

## Slide 11: Home-routed Roaming via different PLMN case
PDU Session Handover from 3GPP access to N3GPP access
  Handover request of LBO session shall be rejected
UE
AMF1
UDM
H-SMF
VPLMN1
HPLMN
V-SMF1
N3GPP
access
AMF2
N3IWF
V-UPF1
H-UPF
3GPP
access
① PDU Session Establishment Request (Initial request)
(New PDU Session ID, DNN)
② The AMF stores an association of the PDU Session ID and the SMF ID (V-SMF1)
④ SMF Identity/Address
PDU Session ID
DNN
(Nudm_UEContextManagement_Registraion)
③ PDU Session Establishment Request
① PDU Session Establishment Request (Existing PDU Session)
(Existing PDU Session ID, DNN)
② SMF Identity/Address
PDU Session ID
DNN
(Nudm_???)
③ Need to select the serving SMF associated with the PDU Session ID (i.e. V-SMF1). BUT…
1. How to handle this PDU Session Establishment message if the SMF is not located in the HPLMN?

## Slide 12: Possible solutions
1. How to handle this PDU Session Establishment message if the SMF is not located in the HPLMN?
  Both UE based and Network based Solution are necessary
    How a UE and Network know whether handover is possible or not?
    Which entity in the network rejects handover request?
UE based Solution | Network based Solution
UE requests only for handover possible PDU Sessions | Network rejects if handover is not possible
UE needs to know whether a PDU Session can be handed over | Network needs to know whether a PDU Session can be handed over
Even though UE based Solution is used, network needs to validate UE request | Even though Network based Solution is used, need a mechanism to prevent repeated request by a UE

## Slide 13: Possible solutions – Network based solution
1. Which entity reject the message based on which information?
  Reject in the AMF v.s. SMF
  How to know whether handover is possible or not?
    AMF can decide based on
      Whether the AMF serves both accesses
      Roaming Mode (Home Routed or LBO)
Reject in the AMF | Reject in the SMF
Not aligned with MM-SM separation | Aligned with MM-SM separation
No need to select SMF | AMF need to select SMF for error handling Pre-configuration Random selection Existing SMF selection (S-NSSAI / DNN)
No additional signaling between AMF and SMF | AMF need to indicate failure reason to the SMF
Explicit method | Implicit method
Roaming Mode is stored in the UDM during the PDU Session Establishment procedure | AMF decides Roaming Mode of PDU Session based on PLMN ID of SMF identity and HPLMN of a UE
- SMF stores additional information in the UDM | - No additional information is stored in the UDM - SMF identity needs to include PLMN ID (MNC+MCC = 3byte) which potentially increases data size between VPLMN and HPLMN - Need to be confirmed by CT4

## Slide 14: Possible solutions – UE based solution
2. How a UE knows whether handover is possible or not?
  The cause implicitly indicates whether the PDU Session is allowed to handover or not
  If the UE has multiple PDU Sessions which are cannot be handed over,
    Each of PDU Session needs to be rejected
    Each time the AMF needs to contact UDM in HPLMN and retrieves PDU Session information
    This increases unnecessary signaling between HPLMN and VPLMN
  Providing a Roaming Mode is more efficient because the UE will not request handover of a PDU Session that cannot be handed over
Cause Value | Roaming Mode
Stored when handover request is rejected | Stored during the PDU Session Establishment
Network provides proper cause value so that a UE does not try handover request again | UE decides whether PDU Session can be handed over to the other access based on Roaming Mode Connected PLMN of each access

## Slide 15: Summery of proposals
Use Nudm_UEContextManagement_Get to retrieve PDU Session information in the AMF
AMF get a specific PDU Session information by indicating PDU Session ID requested by the UE when it retrieves PDU Session information
SMF stores Roaming Mode in the UDM during the PDU Session Establishment
AMF may reject handover request based on the information (Roaming Mode)
UE requests handover only for a handover possible PDU Session