## Slide 1: Discussion on optimizations for PCF services
Oracle/ZTE/Ericsson?/Sandvine
3GPP SA WG 2 Meeting#125
Gothenburg, Sweden, 22 – 26 January 2018
S2-180166

## Slide 2: Introduction
This discussion paper evaluates the basic operation of the PCF services in conjunction with the SMF event exposure related services (similarly will be concluded for the AMF notification related services, ie. SMF will be discussed for simplicity’s sake, however the conclusions of this paper apply to AMF as well).
The paper identifies a few deficiencies and race-condition issues with the current design.
Some optimizations to the PCF services are suggested, in order to resolve the identified issues.
This paper is a stage-2 level reflection of a corresponding CT3 discussion paper brought up during the CT3 December 19th conference call.

## Slide 3: Outstanding issues with PCF, SMF services
Efficiency
Handling PDU session updates requires at least 2 separate interactions (Event notification, then
policy decision updates via UpdateNotify). This results in:
At least doubling processing/network load
Increased latency to get policy decisions’ updates
Tight coupling
Handling PDU session updates results in tight coupling between the event notification and UpdateNotify as the SMF has to understand that it needs to wait for the UpdateNotify before it can respond back to the triggering
procedure (e.g. N11 session update)
Race conditions
When a PDU session is created, subscriptions to event happens separately from policy decision provisioning.
This create a window of time where events may occur before the PCF can subscribe to them, e.g. if a RAT
change occurs in between PDU session establishment and the subscription to events.
Similarly during a PDU session time may elapse between the event notification provided by the SMF, and the
consequent/corresponding policy rules provided by the PCF. During that time the system is not in stable state.
For example a user may breech the quota or otherwise may use an authorized service without the NW being
able to properly address the situation.

## Slide 4: Outstanding issues with PCF, SMF services
Tight coupling – additional aspects
Some events may be relate to PCC rules and their exposure might be problematic as the policy decision and
event notification are done via unrelated services.
For example, in some cases SMF event exposure service would need to use PCC rule names that a dynamically
allocated by the PCF and are unique for a single PDU session. If these are received by the PCF as part of
unrelated Event notifications, correlation to/identification of the proper PDU session might be problematic.
An example from 23.503 Table 6.1.3.5-1: Access independent event triggers
Next slides will illustrate the Efficiency, Tight coupling and Race conditions issues by using example procedures
from 23.502.
Enforced PCC rule request | SMF is performing a PCC rules request as instructed by the PCF. | None | PCF
Event trigger | Description | Difference compared with table 6.2 in TS 23.203 [4] | Conditions for reporting | Motivation

## Slide 5: Illustration of the Efficiency issue - taken from 23.502 as is
23.502 4.16.4 - Session Management Policy Establishment
Efficiency – 4 messages instead of 2

## Slide 6: Illustration of the Race conditions issue - taken from 23.502
23.502 4.16.4 - Session Management Policy Establishment
Race conditions – an event may occur (eg RAT change) before the PCF got a chance to subscribe to it (the event will not get reported, and so the consequent policy action will not take place)

## Slide 7: Illustration of the Tight coupling issue - taken from 23.502 as is
23.502 4.16.5 - Session Management Policy Modification
Tight coupling – SMF sends the PCF an event notification. Then it needs to sit and wait for a resulting policy update, which comes on a different service in an asynchronous way.
This makes it hard for the SMF to correlate an event with a respective action.
Also this may cause *gaps* in the system, for example: quota breech, which does not get an immediate policy action.
Also the policy rules sent in step 5 and the event subscription performed in step 7 are not provided at the same time, thus introducing gaps/latency.
3X Inefficiency – 6 messages instead of 2!
Also additional latency to get policy updates

## Slide 8: Proposed solution
Add an event subscription(PCF->SMF) and notification(SMF->PCF) functionality respectively to the Npcf_SMPolicyControl_Get service operation and to the Npcf_SMPolicyControl_UpdateNotify service operation.
Next pages will illustrate the change of the PCF related basic procedures as a result of the above optimization.
NOTE: This does NOT impact the Nsmf_EventExposure Service! AMF, AF/NEF and/or any other consumer can still use this service as is, as long as the SMF simply notifies subscribers of events in a “fire and forget” fashion.
Editor’s note: It is FFS whether a new service operation (e.g. Npcf_SMPolicyControl_Update) should be added for SMF initiated session modifications as opposed to re-using the Npcf_SMPolicyControl_Get service operation or whether the Get operation name should be changed (e.g. GetOrUpdate).

## Slide 9: Illustration of the solution - taken from 23.502 w/ a change
23.502 4.16.4 - Session Management Policy Establishment (optimized)
Event subscription included in the Npcf_SMPolicyControl_Get service response (step 5).
Original steps 6 and 7 are gone. SMF knows right away what the events it needs to report.

## Slide 10: Illustration of the solution - taken from 23.502 w/ a change
23.502 4.16.5 - Session Management Policy Modification (optimized)
In case the session update is initiated by the SMF, steps 1a and 2a use the Npcf_SMPolicyControl service, and so no additional steps are needed.
Else In case the session update is initiated by the H-PCF (eg triggered by step 1b o1c or 4 (eg time based policy)) then
Event subscription included in the Npcf_SMPolicyControl_UpdateNotify service request (step 5).
Original steps 7 and 8 are gone. SMF receives from the PCF the policy rules and event subscription in an atomic way.
Editor’s note: Might want to change the name of the Get operation to GetOrUpdate or introduce a new service operation.

## Slide 11: Post mortem
The way services are defined in stage 2 currently results in tight coupling between the event exposure and policy control services, somewhat defeating the basic principles of SB design.
This paper supports the generic 5G principle of having an independent event exposure service, but it has to be defined in such a way (e.g. fire and forget type of events).
The issues identified in this paper and the proposed solution may not be specific to PCC.
It is suggested that this should be handled on a case by case basis as optimization, ie consider PCC services in this paper, and if need, investigate other services in an end to end fashion, and possibly extended the solution proposed in this paper to other services.
The topic/issues presented by this paper were discussed in CT3. It was agreed that the best way forward is to go ahead with the proposed stage 2 changes first to avoid any further delays given the short amount of time CT3/CT4 have for completing 5G phase 1, and the fact that stage 3 cannot progress on this issue(s) until stage 2 changes are agreed.