## Slide 1: Discussion on PCF
3GPP SA WG 2 Meeting#125
22 - 26 January, 2018, Gothenburg, Sweden
Source: LG Electronics
Title: Discussion on PCF
Document for: Discussion & Decision
Agenda Item: 6.5.6
Work Item / Release: 5GS_Ph1 / Rel-15
S2-180302
LG Electronics

## Slide 2: Question – PCF selection
PCF selection in TS 23.501
  Q1: which node selects the V-PCF and the H-PCF for a UE in roaming case?
    Proposal: The AMF may select both PCFs. Based on operator policies, the AMF may send the H-PCF address to the V-PCF, and V-PCF uses it unless locally configured on V-PCF. (TS 23.501 draft CR – S2-180303, TS 23.502 draft CR – S2-180304)
  Q2: which procedure is used to send the PCF selected by the AMF to the SMF?
    Proposal: The SMF sends the PCF selected by the AMF to the SMF during the PDU session establishment procedure. (TS 23.501 draft CR – S2-180303)
6.3.7.1 PCF selection for a UE or a PDU Session
The AMF selects the PCF for a UE, the SMF selects the PCF for a PDU Session. The selected PCF may be the same or may be a different one, following one of the alternatives below:
  - The AMF utilizes the NRF to discover the PCF instance(s) for a UE unless PCF information is available by other means, e.g. locally configured on AMF based on operator policies.
  - The SMF utilizes the NRF to discover the PCF instance(s) for a PDU Session unless PCF information is available by other means, e.g. locally configured on SMF or received from the AMF. The following factors may be considered during the PCF selection by the SMF:
  a) Local operator policies.
  b) Selected Data Network Name (DNN).
  c) PCF selected by the AMF. This is to select the same PCF for the AMF and the SMF.

## Slide 3: Question – PCF ID
The procedures in TS 23.502
  Issue1: more clarification to align with the above agreements.
    Proposal:
      removing some sentences to avoid the misunderstanding (TS 23.502 draft CR – S2-180304, TS 23.503 draft CR – S2-180305)
        e.g. ‘The AMF decides to terminate the Policy Association during Deregistration procedure or due to mobility with change of AMF in the registration procedure, then if a Policy Association was established with the (V-)PCF steps 2 to 3 are performed.” [TS 23.502]
        e.g. Upon change of AMF, the source AMF informs the PCF that the UE context was removed in the AMF. [TS 23.503]
      adding the PCF ID into the table of “UE Context in AMF” in TS 23.502 (TS 23.502 draft CR – S2-180304)
  Issue2: in the roaming case, the V-PCF follows the same principle to the H-PCF?
    Proposal:
      Adapt to the same principle because of using the same service operation - between AMF and V-PCF vs. between V-PCF and H-PCF
      i.e. to separate the initial association and the case having the existing policy context, use PCF ID in Npcf_AMPolicyControl_Get service operation
        In the initial policy association establishment with H-PCF (i.e. initial registration or V-PCF re-allocation), V-PCF does not include PCF ID in the service operation towards the H-PCF.
        With the existing policy association, if the V-PCF received the PCF ID from the AMF during inter-AMF mobility, the V-PCF includes the H-PCF ID in the service operation towards the H-PCF. (TS 23.502 draft CR – S2-180304)
4.2.2.2.2 General Registration
…………………
[Optional] new AMF performs a Policy Association Establishment during Registration procedure as defined in clause 4.16.1.2. For an Emergency Registration, this step is skipped.
  If the new AMF contacts the PCF identified by the (V-)PCF ID received during inter-AMF mobility in step 5, the new AMF shall include the PCF-ID in the Npcf_AMPolicyControl Get operation. This indication is not included by the AMF during initial registration procedure.

## Slide 4: Question – Service operations between V-PCF and H-PCF
The procedures in TS 23.502
  Issue: In the current specification, the service operations between V-PCF and H-PCF are missing.
    Proposal: The corresponding descriptions are needed. (In this meeting, we do not provide any CR)
    Also at least, the following table should be updated (TS 23.502 draft CR – S2-180304)
4.16.1.2 Policy Association Establishment during Registration
This procedure concerns both roaming and non-roaming scenarios.
In the non-roaming case the V-PCF is not involved and the role of the H-PCF is performed by the PCF. For the roaming scenarios, the V-PCF interacts with the AMF:
…………………
  In roaming scenario, the V-PCF contacts the H-PCF.

## Slide 5: Question – Interaction between V-PCF and H-PCF
Interactions between V-PCF and H-PCF in TS 23.503
  Issue: HR or LBO should be referring to a particular PDU session instead of per UE.
    Proposal: (TS 23.503 draft CR – S2-180305)
      For per UE policy,
        In roaming, the H-PCF that provides access and mobility related policy rules, ANDSP rules and URSP rules subscribes to AMF related events via the V-PCF.
      For per PDU session policy, the following two alternatives
        (option 1)
          In HR roaming, the H-PCF that provides session management related policies subscribes to session related events to SMF in HPLMN.
          In LBO roaming, the V-PCF that provides session management related policies subscribes to session related events to SMF in VPLMN.
        (option 2)
          The PCF that provides session management related policies (i.e. H-PCF in HR roaming, V-PCF in LBO roaming) subscribes to session related events to the SMF in the same PLMN.
5.3.4 Interactions between V-PCF and H-PCF
………
In LBO roaming, the H-PCF that provides mobility policy rules and URSP rules subscribes to AMF related events via the V-PCF. The V-PCF provides access mobility management policies, UE policies and session management policies in the VPLMN. The V-PCF subscribes AMF related events in the AMF and session related events in the SMF as in the non-roaming case.
In HR roaming, the H-PCF providing URSP policies to the V-PLMN subscribes to AMF related events via the V-PCF. The H-PCF that handles the session related policies subscribes all the events via the H-SMF.