## Slide 1: Configured NSSAI discussion
SA2#127-bis May 28 – June 1 Newport Beach, USA Tdoc S2-185836

## Slide 2: Changes of Configured NSSAIs following changes to Subscribed NSSAIs
If the set of subscribed S-NSSAIs or their values changes:
  If UE not reachable: set a flag in UDR to make sure the UE config is updated when the UE is reachable next (the UDM sends indication to AMF). Unset the flag in UDR when the UE is reachable and successfully updated.
    To be decided if the UE needs to reregister with indication of successful update (the UE may get a new URSP also if slice set changes and the HPLMN must provide it before clearing the configuration change flag in UDR)
    Note the HPLMN indicates Subscription change to any PLMN the UE registers with when it is reachable again, regardless of whether this PLMN configuration is affected, as long as at least one roaming partner configuration is affected by the subscription change.
  UE reachable:
    push the updated config to VPLMN (or simply indication of subscription change that may affect a roaming configuration in any PLMN) and update the URSP if necessary
    VPLMN updates the UE with new configured NSSAI if applicable and its mapping to HPLMN S-NSSAIs
    The UE has to also make sure the Configured NSSAIs for to other PLMNs are not assumed to be valid and that the other PLMNs will also update the UE configuration ->
S2-184880 | DISCUSSION | Approval | Configured NSSAI updates triggered by changes in Subscribed S-NSSAIs | Ericsson
S2-184881 | CR | Approval | 23.501 CR0360: Configured NSSAI updates triggered by changes in Suscribed NSSAI | Ericsson
S2-185396 | CR | Approval | 23.501 CR0442: Update of UE Configured NSSAI | Huawei, Hisilicon
S2-185399 | DISCUSSION | Discussion | Updating Configured NSSAI when HPLMN subscription to S-NSSAIs changes | Nokia, Nokia Shanghai Bell
S2-185412 | CR | Approval | 23.501 CR0444: Network slicing subsription change and update of UE configuration | Nokia, Nokia Shanghai Bell
S2-185417 | CR | Approval | 23.502 CR0497: Network slicing subsription change and update of UE configuration | Nokia, Nokia Shanghai Bell

## Slide 3: Changes of Configured NSSAIs following changes to Subscribed NSSAIs
How to provide the new up to date configuration:
  5supporters Proposal A: remove the Slicing configuration for all other PLMNs so the UE gets fresh config. The current PLMN configuration is changed if one is provided to the UE.
  1 supporter Proposal B: mark the UE information (e.g. configured NSSAI and Allowed NSSAI) as possibly outdated and send such indication that it is possibly outdated to network in first registration in PLMNs While still use the information when deriving Requested NSSAI.
  1supporter Proposal C: upon all first registrations to a PLMN AMF, the AMF provides the UE with the latest configured NSSAI for PLMN
  (no support in this form, an hashing vairant was discussed with no conclusion)Proposal D: when the UE performs initial registration, or mobility registration from another PLMN it provides to the AMF also the Configured NSSAI. If the configured NSSAI is out of date the AMF can provide an Allowed NSSAI based on the subscribed default S-NSSAIs (as if the Requested NSSAI is empty) and at the same time provides an updated Configured NSSAI; after that it would be up to the UE decide if it is fine with the received Allowed NSSAI or if it prefers to re-register building the Requested NSSAI starting from the updated Configured NSSAI.
  Proposal C needs no flags in UDR but may lead to a re-registration and some frequent inefficiency for rare events handling (same for proposal D). Proposal D may have some issue if the UE is not reachable and does not change PLMN (flag in UDR still needed)
  Proposed conclusion from drafting : move forward with A

## Slide 4: Changes of Configured NSSAIs following changes to Subscribed NSSAIs
Ericsson proposes the concept of configured NSSAI for HPLMN is implicit in the URSP/NSSP info.
  Way forward: treat the Configured NSSAI for HPLMN the same way as any Configured NSSAI for any serving PLMN in the procedures. Clarfy this in the text of specs.
Define that a change of subscription triggers URSP update
  Current path of information exchange is using UDM->AMF->PCF i.e. CR re-used that path, but path to be decided.
  agreement: the URSP needs update when the S-NSSAI subscription changes and there is more than one S-NSSAI. How this is done needs to be discussed with the PCC people.
S2-184875 | DISCUSSION | Approval | Handling of Configured NSSAIs in Roaming Scenarios - DP | Ericsson
S2-184876 | CR | Approval | 23.501 CR0359: Handling of Configured NSSAIs in Roaming Scenarios - 23.501 | Ericsson
S2-184877 | CR | Approval | 23.502 CR0410: Handling of Configured NSSAIs in Roaming Scenarios - 23.502 | Ericsson
S2-185088 | CR | Approval | 23.503 CR0081: Handling of Configured NSSAIs in Roaming Scenarios - 23.503 | Ericsson

## Slide 5: Changes of Configured NSSAI in serving PLMN
If the Configured NSSAI and/or its mapping to HPLMN S-NSSAIs for serving PLMN (different from HPLMN) changes based on local decision:
  The AMF updates the UE without indication this is caused by HPLMN subscription change. All other PLMNs configuration remains not affected.
  This is already well defined in the TS as is, except that:
    if the local PLMN adds support to some slices that were previously rejected in the VPLMN for lack of support of a corresponding slice in VPLMN, we need to add text to TS clarifying that this needs to be addressed by the roaming partners to define a time when this is signaled to the VPLMN as a HPLMN subscription update for the UE and then the same provisions apply as for the case of Subscription update (this causes the UE obtains new configuration in VPLMN including the new supported slice).
    If the mapping information to HPLMN Subscribed S-NSSAI changes, and the UE uses out of date Mapping is detected in AMF, the AMF shall update the local UE configuration. Text to this effect needs to be added to the TS.
If the UE serving PLMN is the HPLMN:
  The selected behavior among A, B,C, D applies as this is also a subscription change (configure NSSAI for HPLMN is = to subscribed S-NSSAIs)

## Slide 6: Configured NSSAI valid for all PLMNS
The TS allows the existence of a configured NSSAI valid for all PLMNs
This is standardized S-NSSAIs (so no need of global agreement on values) or result of global agreement with all PLMNs (then de fact it is a collection of PLMN Specific NSSAIs all set to same value)
In all cases the HPLMN cannot assume the VPLMN supports these without roaming agreement
It also implies the HPLMN takes interest on what value the VPLMN uses in identification of a slice – note it is not mandatory that a standard NSSAI in HPLMN subscription needs to be supported by same value in V-PLMN – V-PLMN may adds an SD field e.g. for inbound roamer).
It is proposed to continue with the concept that the default S-NSSAI set is the basis for interoperability and the configuration triggered by not sending a requested NSSAI provides the right tool for the VPLMN to configure the Configured NSSAI for the VPLMN and its mapping to HPLMN S-NSSAI values, based on the roaming agreement that is actually S-NSSAI agnostic, rather based on a agreement on slice attributes e.g. defined by a GSMA GST (global slice template).
  There is no clear benefit for the HPLMN taking care of VPLMN values configuration and it creates the premise for more need of information exchange and even global synchronization of configuration updates among operators.
  It is proposed to abandon the concept of configured NSSAI for all PLMNs as it implies the HPLMN taking unnecessary interest in the value used in serving PLMNs
S2-184944 | DISCUSSION | Decision | Discussion on use and update of the Configured NSSAI | Qualcomm Finland RFFE Oy
S2-184945 | CR | Approval | 23.501 CR0373: Use and update of the Configured NSSAI | Qualcomm Incorporated, Mediatek, AT&T
S2-184946 | CR | Approval | 23.503 CR0074: Use and update of the Configured NSSAI | Qualcomm Incorporated, Mediatek, AT&T
NOT DISCUSSED YET

## Slide 7: AMF cannot determine new Allowed NSSAI
When there is the need to update the Allowed NSSAI, the AMF shall provide the UE with the new Allowed NSSAI and the associated mapping with Configured NSSAI for the HPLMN, unless the AMF cannot determine the new Allowed NSSAI (e.g. all S-NSSAIs in the old Allowed NSSAI have been removed from the Subscribed S-NSSAIs), in which case the AMF shall not send any Allowed NSSAI to the UE but indicate to the UE to perform a Registration procedure.
S2-184867 | CR | Approval | 23.501 CR0207R3: Slice configuration change | Ericsson, Telecom Italia, Intel
S2-185015 | CR | Approval | 23.502 CR0251R2: Clarification on UE configuration update procedure | Telecom Italia, OPPO, ZTE, Ericsson
NOT DISCUSSED YET